==============================================================================
DVIDRV 1.6h                                                        09-Jul-1998
==============================================================================


Table of Contents
=================

1        Introduction
2        Running the drivers
2.1        Using the batch files
2.2        Using dvidrv.exe (DOS only)
2.3        Getting help for the calling sequence
2.4        Printing or viewing a DVI file
3        Using options
3.1        Options for message output
3.1.1        Getting a list of the options
3.1.2        Setting the verbosity level
3.2        Options for page selection
3.2.1        Selecting sides by page number
3.2.2        Double-sided printing
3.2.3        Selecting sides by side index
3.2.4        Selecting the order of the sheets
3.2.5        Printing multiple copies
3.3        Managing fonts and graphics files
3.3.1        Handling missing fonts and graphics files
3.3.2        Scaling fonts
3.3.3        Font size tolerance
3.3.4        Initial loading of fonts
3.3.5        Rounding character positions
3.3.6        Generating fonts automatically
3.4        Side layout options
3.4.1        Specifying the paper size
3.4.2        Transformation (orientation)
3.4.3        Moving the output on the sheet
3.5        Producing booklets and books, n-up printing
3.5.1        Defining the locations of the pages on a sheet
3.5.2        Arranging the pages
3.5.3        Special effects
3.5.4        Examples
3.6        Magnification and resolution
3.6.1        Setting the resolution
3.6.2        Setting the magnification
3.7        Directory and file name options
3.7.1        Search paths
3.7.2        Input files
3.7.3        Output files
3.8        Miscellaneous options
3.8.1        Meta options
3.8.2        Memory management
3.9        Additional options for dviscr and dvivik
3.9.1        Configuration
3.10       Additional options for dvipm
3.10.1       Configuration
3.11       Additional options for dvidot when printing on a dot matrix printer
3.11.1       Options for all parameter files
3.11.2       Options for all parameter files but itoh.dot and aiw.dot
3.11.3       Options for the parameter files itoh.dot and aiw.dot
3.12       Additional options for dvidot when generating graphics files
3.12.1       Controlling the bitmap file
3.13       Additional options for dvihplj
3.13.1       General options
3.13.2       Selecting the printer model
3.13.3       Using additional features of a printer
3.13.4       Solving compatibility problems
3.14       An introduction to templates
3.14.1       The simplest example of a template -- a constant template
3.14.2       A simple example of a template
3.14.3       Template parameters
3.14.4       Forming multiple expansions with a list
3.14.5       Forming multiple expansions with alternatives
3.14.6       Multiple sets of alternatives
3.14.7       Environment variables
3.14.8       The emTeX directory ($EMTEX:)
3.14.9       Template parameter modifiers
3.14.10      Default extension
3.14.11      Summary
3.14.12      Further examples
4        Managing fonts
4.1        Specifying font size (resolution)
4.2        Font substitution file format
4.2.1        Substitution with and without batch mode
4.2.2        Rule lines
4.2.3        Options in font substitution rules
4.2.4        Matching font names
4.2.5        Using built-in printer fonts
4.2.6        Example
4.3        Font search rules
4.4        Generating missing fonts automatically with MFjob and METAFONT
4.5        Using built-in printer fonts
5        Using dviscr and dvivik
5.1        Keyboard functions for dviscr and dvivik
5.2        Entering numbers
5.3        Understanding the status line
6        \special
7        Miscellaneous topics
7.1        General notes
7.2        Output with the +verbosity:4 option
7.2.1        dvihplj
7.2.2        All drivers
7.3        Return codes (ERRORLEVEL)
7.4        Known bugs
8        Installation of the printer drivers and the screen previewers
9        Explanation of warning and error messages
9.1        Warning messages
9.2        Fatal errors (2xxx)
9.3        Internal errors (3xxx)
10       History


1 Introduction
==============

The dvidrv drivers output DVI files to a printer or to the screen.
DVI files are created by TeX, for instance.

The drivers run under OS/2 1.x, OS/2 2.x, MS-DOS and PC-DOS (2.1 or
later) on IBM PC compatible computers.  At least 512 KB of memory is
required under DOS.

You'll find installation instructions in section 8.

The dvidrv family includes the following drivers:

dviscr  Screen previewer for CGA, EGA, VGA, HGC, 8514/A, and other
        adapters.  There are three versions of dviscr: dviscr.exe
        (16-bit version which does not use the math coprocessor),
        dviscr7.exe (16-bit version which uses the math coprocessor),
        and dviscrs.exe (16-bit version which does not use the math
        coprocessor; saves memory at cost of speed).

dvivik  Screen previewer for Viking I, cannot be used under OS/2

dvipm   Screen previewer for the Presentation Manager (OS/2 1.2 or
        later).  There are three versions of dvipm: dvipm.exe (32-bit
        version for OS/2 2.0 or later), dvipm16.exe (16-bit version
        which does not use the math coprocessor), and dvipm167.exe
        (16-bit version which uses the math coprocessor).

dvihplj
        Printer driver for PCL printers such as HP LaserJet+, HP
        DeskJet, HP PaintJet, HP QuietJet, HP ThinkJet, and Kyocera
        F-1010.  The HP LaserJet classic is not supported.  There are
        three versions of dvihplj: dvihplj.exe (16-bit version which
        does not use the math coprocessor), dvihplj7.exe (16-bit
        version which uses the math coprocessor), and dvihplj3.exe
        (32-bit version which uses the math coprocessor).

dvidot  Printer driver for dot matrix printers and for creating
        graphics files.  This driver can be configured for many
        dot matrix printers (including dot impact printers, laser
        printers and ink jet printers).  Moreover, it can create
        graphics files in various formats.  There are two versions
        of dvidot: dvidot.exe (16-bit version which does not use the
        math coprocessor) and dvidot7.exe (16-bit version which uses
        the math coprocessor).

The following dvidot parameter files for printing on dot matrix
printers are supplied:

    Parameter ³ Printers                   ³Resolution ³ Environ. ³+font-files
    file      ³ (incomplete list)          ³ h x v DPI ³ variable ³default (*)
    ÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄ
    fx80      ³ EPSON FX and RX series     ³ 240x216   ³ DVIFX    ³ fx
    fx80l     ³ EPSON FX and RX series     ³ 120x72    ³ DVIFX    ³ fx
    fx100     ³ EPSON FX and RX series     ³ 240x216   ³ DVIFX    ³ fx
    fx100l    ³ EPSON FX and RX series     ³ 120x72    ³ DVIFX    ³ fx
    mx80      ³ EPSON MX series            ³ 120x216   ³ DVIMX    ³ mx
    lql       ³ EPSON LQ series            ³ 180x180   ³ DVILQL   ³ p6l
    lqm       ³ EPSON LQ series            ³ 360x180   ³ DVILQM   ³ p6m
    lqh       ³ EPSON LQ series            ³ 360x360   ³ DVILQH   ³ p6h
    lqwl      ³ EPSON LQ series (wide)     ³ 180x180   ³ DVILQL   ³ p6l
    lqwm      ³ EPSON LQ series (wide)     ³ 360x180   ³ DVILQM   ³ p6m
    lqwh      ³ EPSON LQ series (wide)     ³ 360x360   ³ DVILQH   ³ p6h
    sty800    ³ EPSON Stylus 800           ³ 360x360   ³ DVISTY   ³ sty
    styc800   ³ EPSON Stylus Color 800     ³ 360x360   ³ DVISTY   ³ sty
    p6l       ³ NEC P6, Panasonic KX-P1124 ³ 180x180   ³ DVIP6L   ³ p6l
    p6m       ³ NEC P6, Panasonic KX-P1124 ³ 360x180   ³ DVIP6M   ³ p6m
    p6h       ³ NEC P6, Panasonic KX-P1124 ³ 360x360   ³ DVIP6H   ³ p6h
    p7l       ³ NEC P7                     ³ 180x180   ³ DVIP6L   ³ p6l
    p7m       ³ NEC P7                     ³ 360x180   ³ DVIP6M   ³ p6m
    p7h       ³ NEC P7                     ³ 360x360   ³ DVIP6H   ³ p6h
    itoh      ³ C.ITOH 8510A               ³ 160x144   ³ DVIITOH  ³ ito
    aiw       ³ Apple Imagewriter          ³ 160x144   ³ DVIAIW   ³ aiw
    dmp130    ³ Tandy DMP-130              ³ 240x216   ³ DVIDMP   ³ fx
    ibm4201   ³ IBM Proprinter 4201        ³ 240x216   ³ DVI4201  ³ fx
    ibm4202   ³ IBM Proprinter 4202        ³ 240x216   ³ DVI4202  ³ fx
    ibm4207l  ³ IBM Proprinter 4207        ³ 180x180   ³ DVI4207L ³ p6l
    ibm4207m  ³ IBM Proprinter 4207        ³ 360x180   ³ DVI4207M ³ p6m
    ibm4208l  ³ IBM Proprinter 4208        ³ 180x180   ³ DVI4208L ³ p6l
    ibm4208m  ³ IBM Proprinter 4208        ³ 360x180   ³ DVI4208M ³ p6m
    bj10eh    ³ Canon Bubble Jet BJ-10e    ³ 360x360   ³ DVIBJH   ³ bj
    bj300h    ³ Canon Bubble Jet BJ300     ³ 360x360   ³ DVIBJH   ³ bj
    faxworks  ³ FaxWorks for OS/2          ³ 204x196   ³ DVIFAXWK ³ fax

(*)     Due to space restrictions, this column shows only
        part of the +font-files default setting.  If this
        column contains *, the complete default setting is
        \texfonts\pixel.*\@Rrdpi\@f{.pk,.pxl}.

The IBM Proprinter type 4207 and 4208 must be set to AGM (see the
printer user's manual).

Not all printers of the EPSON LQ series support 360x360 DPI (lqh.dot
and lqwh.dot).  For instance, there are two variants of the LQ-850,
only one of which supports 360x360 DPI.

The following dvidot parameter files for creating graphics files are
supplied:

    Parameter ³                                                    ³ Default
    file      ³ Graphics file format                               ³ extension
    ÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄ
    msp1      ³ Old MSP format (Microsoft Paint of Windows 1.x)    ³ msp
    msp2      ³ Newer MSP format (Microsoft Paint of Windows 2.x)  ³ msp
    pcx       ³ PCX format (Paintbrush)                            ³ pcx
    bmpos2    ³ BMP format (OS/2 1.1)                              ³ bmp
    bmpwin    ³ BMP format (Windows 3.x)                           ³ bmp

The default resolution is 300x300 DPI, the default name of the envi-
ronment variable is DVIBMP, the default value for the +font-files
option is \texfonts\pixel.lj\@Rrdpi\@f{.pk,.pxl}.  The default exten-
sion given in the table applies to the output file.

Additional parameter files can be easily constructed -- see
makedot.doc.

If memory in real mode (DOS) is short, dviscrs.exe should be used
instead of dviscr.exe -- you can rename dviscrs.exe only if it is run
under DOS 3.0 or later.  This version runs in real mode only, needs
less memory and is somewhat slower.  Otherwise it behaves exactly
like dviscr -- for instance, @d in templates will be replaced with
`dviscr'.

When using OS/2 1.x, you must run dvipm16.exe (or dvipm167.exe to
take advantage of the math coprocessor if you have one) instead of
dvipm.exe.


2 Running the drivers
=====================

Usually, you run a DVI driver by invoking one of the batch files
supplied with the drivers.


2.1 Using the batch files
-------------------------

The following batch files for used for running the screen previewers:

    v   vs   vp

The following batch files for used for running the printer drivers:

    prtlql   prtp6l   prthpdj    prthpljh   prtmx      prtsty
    prtlqm   prtp6m   prthpdjh   prtfx      prtbj10e   prtitoh
    prtlqh   prtp6h   prthplj    prtfxl     prtbj300   prtfaxwk

The following batch files are used for creating bitmap files:

    pcxp6l   pcxdj    pcxfx
    pcxp6m   pcxlj    pcxito
    pcxp6h   pcxljh   pcxfax

Below, the commands used by those batch files are explained.  The
batch files v, vs and vp are called with one argument: the name of
the DVI file.  The other batch files are called with two arguments:
the name of the DVI file and the name of the output file.  The name
of the output file can be omitted, the drivers will then use the de-
fault output file name set with the +default-output-file option, for
instance the printer port LPT1.  Additionally, you can enter command
line options as arguments.

The batch files use the following environment variables:

DVIDRVINPUT
        Search path for DVI files.

DVIDRVFONTS
        Search path for FLI files.

DVIDRVGRAPH
        Search path for graphics files.

For instance, you can set the environment variables like this:

    set dvidrvinput=c:\mytex;c:\emtex\doc;c:\emtex\doc\english
    set dvidrvfonts=c:\texfonts
    set dvidrvgraph=c:\mytex;c:\emtex\doc

In this example, DVI files and graphics files will be sought in
\mytex in addition to the emTeX directories.  Font files and font
library files will be sought in c:\texfonts.

Note that the environment variables should not contain whitespace.
When using `Cut & Paste' blanks may sneak in at the end of the lines.

If you don't want to set these environment variables, you should in-
sert the path names into the configuration files (or preferably into
copies of the configuration files).

The batch files use configuration files for setting the options.
You can also use those configuration files on the command line of a
driver to use different fonts.  The following configuration files are
available for selecting fonts:

    File name    ³ Resolution ³ Fonts ³ Font resolution
    ÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
    bj.cnf       ³   360      ³  BJ   ³      360
    fax.cnf      ³ 204x196    ³  FAX  ³    204x196
    faxl.cnf    *³ 204x98     ³  FAX  ³    204x196
    fx.cnf       ³ 240x216    ³  FX   ³    240x216
    ito.cnf      ³ 160x144    ³  ITO  ³    160x144
    lj.cnf       ³   300      ³  LJ   ³      300
    ljh.cnf      ³   600      ³  LJH  ³      600
    mx.cnf       ³ 120x216    ³  MX   ³    120x216
    mx_fx.cnf   *³ 120x216    ³  FX   ³    240x216
    mxl_fx.cnf  *³ 120x72     ³  FX   ³    240x216
    sty.cnf      ³   360      ³  STY  ³      360
    p6h.cnf      ³   360      ³  P6H  ³      360
    p6l.cnf      ³   180      ³  P6L  ³      180
    p6l_p6h.cnf *³   180      ³  P6H  ³      360
    p6l_p6m.cnf *³   180      ³  P6M  ³    360x180
    p6m.cnf      ³ 360x180    ³  P6M  ³    360x180
    p6m_p6h.cnf *³ 360x180    ³  P6H  ³      360
    qj.cnf       ³   192      ³  QJ   ³      192
    tj.cnf       ³ 192x96     ³  TJ   ³    192x96
    tj_qj.cnf   *³ 192x96     ³  QJ   ³      192

The configuration files marked with * use scaled fonts, see
+font-scaling.

To call dviscr with P6L fonts, type

    v @p6l <filename>

or replace @lj with @p6l in v.bat (OS/2: v.cmd).


2.2 Using dvidrv.exe (DOS only)
-------------------------------

The dvidrv program calls the driver program and -- if required --
MFjob to generate missing fonts:

    dvidrv <driver> <driver-arguments>

The dvidrv program creates a temporary file for the MFjob commands
and runs the driver program given on the command line.  If missing
fonts are to be generated, MFjob will be called, then again the
driver.  Finally, the temporary file will be deleted.  The dvidrv
program is required under DOS only.  Under OS/2, the drivers directly
call MFjob (unless +call-mfjob:off is set).

See +metafont-mode and +mfjob-file and section 4.4, `Generating
missing fonts automatically with MFjob and METAFONT' for details.


2.3 Getting help for the calling sequence
-----------------------------------------

To get a list of the more common options, type ? on the command line,
for example:

    dvihplj ?

To get a list of all the options, type ??  instead of ?.


2.4 Printing or viewing a DVI file
----------------------------------

On the command line, you can enter the input file name, options and
-- for the printer drivers -- the output file name:

    dviscr  [options] input-file [options]
    dvivik  [options] input-file [options]
    dvipm   [options] input-file [options]
    dvihplj [options] input-file [options] output-file [options]
    dvidot  parameter-file [options] input-file [options] output-file [options]

If arguments are omitted the program will prompt for them (cf. the
+options option.) except that dvidot must always have the parameter
file name on the command line.  More than one argument may be entered
at each prompt, these arguments will be interpreted as if they had
been entered on the command line.

When using dvipm, you can enter the name of the input file and the
options in dialog boxes if you don't give a file name on the command
line.  In this case, you can change the options.  After changing the
options, you can open the DVI file.  After opening the DVI file,
you can't change the options until you choose File->New.  Moreover,
you can use drag & drop under OS/2 1.3 and later to open a DVI
file.  You'll find further information about dvipm in the on-line
help (select the Help menu or press F1).  The language used for the
on-line help can be changed with the Language selection of the Help
menu.  You can choose English or German help.

dvidot expects to find the dvidot parameter files (the default exten-
sion is DOT) in the `data' subdirectory of the emTeX directory, which
defined is by the EMTEXDIR environment variable.  If EMTEXDIR is not
set, dvidot will use `\emtex\data' for the parameter file.  The name
of the parameter file MUST be given on the command line and must be
the first argument.

For dvidot with a parameter file for creating graphics files, the
default extension for output files is MSP, PCX or BMP, depending on
the parameter file.  dvidot with a parameter file for a dot matrix
printer and all the other drivers have no default.  The output
filename can be a DOS device name like PRN, LPT2, COM2 if required --
though not when creating a graphics file, of course.  See also the
+xon-xoff option.

If the output is sent to a file then the file can be printed with

    COPY /B file PRN

The `/b' option is important as otherwise the copy will terminate at
the first Control-Z byte encountered.

Under OS/2 a hyphen can be used as the output file name, output will
be sent to stdout and can be piped into another program.  Output to
stdout does not work when creating a graphics file with dvidot.

Usually, dvidot with a parameter file for creating graphics files
creates only one graphics file, containing the first selected side.
Multiple graphics files (one for each side) can be created with one
dvidot run by using one or more (consecutive) `?' in the output file
name.  The question marks will be replaced by a number (with leading
zeros): 1 for the first side, 2 for the second, and so on.  If
there's one `?', up to 9 graphics files will be created, if there are
two `?', up to 99 graphics files will be created, and so on.  Example:

    dvidrv dvidot pcx @lj mytext page??

creates the graphics files page01.pcx to (at most) page99.pcx.

When entering the options in response to a driver prompt the `-' or
`/', which is required on the command line, need not be entered; `+',
however, must be entered.

An input filename, output filename or option can be replaced by
@response-file.  This will cause the lines in the response file to be
read and interpreted at this point after which interpretation of the
command line will continue.  The response file line length may not
exceed 127 characters.  An example:

    dvidrv dvidot fx80 @fx test prn

The arguments in fx will be processed first and then the file
test.dvi will be printed with the output going to the device PRN.

@response-file can be entered at a program prompt as well as on the
command line.

The default extension for response files is CNF.  The directories to
be searched for response files can be set with the +response-files op-
tion; the normal searching sequence starts with the current directory
and finally searches the `data' subdirectory of the emTeX directory.

Arguments can also be passed to the program through environment vari-
ables which are processed before arguments on the command line or
entered at a prompt.  It is recommended, however, that only options,
or response files containing only options, are put into environment
variables; if a file name is entered then only this file can be
processed.

The first environment variable looked for is DVIDRV and the next is
one with the same name as the driver.  dvidot uses a further environ-
ment variable with a name set in the parameter file.  For example,
to set +dvi-file:{,c:\mydvi\}@i as a default option for dviscr, the
operating system command:

    set dviscr=+dvi-file:{,c:\mydvi\}@i

can be given.  Note: Environment variables cannot contain `='.

Options which are common to all the drivers should appear in the
DVIDRV environment variable.  If, for instance, units should all be
in mm then the system command

    set dvidrv=+unit:mm

can be entered.  This will affect all the drivers.

In a response file a single `%' starts a comment: all characters to
the end of the line will be ignored.  The `%' can be placed at the
beginning of a line or after an option, but in the latter case it
must be preceded by at least one space.

A `@' at the beginning of a line (column 1) causes the rest of the
file to be ignored -- this allows a driver log file to be used as a
response file.


3 Using options
===============

Most options have two forms: A long form and a short form (more or
less compatible with earlier releases of the drivers).  The long form
consists of a `+' character followed by the long name of the option,
possibly abbreviated.  The short form consists of a `/' or `-' charac-
ter followed by one, two or three cryptic letters.  There are options
for which only the long form is available and there are options for
which only the short form is available (long forms for the options of
the latter variety will be added in a later version of the drivers).

Options may be separated by spaces or another option may follow
immediately: in this case the following option must start with `/'
(and thus must be given in the short form).  If your operating system
is set up to use `-' for options instead of `/', you must precede
the short form of options by `-' and you must separate options by
spaces.  In this case, you can use `/' in path names, for example

    dviscr @lj /mytex/mytext -o:3 -pt:/mylog/mytext.ddl

With a standard setup (using `/' for options), you should enter

    dviscr @lj \mytex\mytext /o:3/pt:\mylog\mytext.ddl

instead.  The examples in this manual use `/'.

The operating system switch character can be overridden by setting
the EMTEXSWCHAR environment variable to a non-empty value.  If
EMTEXSWCHAR is set to `-', this character will be used for options.
For all other settings of EMTEXSWCHAR, the drivers use `/' for op-
tions.

The long names of the options can be abbreviated as follows, as long
as the abbreviation is unambiguous (otherwise a warning message will
be displayed, along with all matching options):

- If you enter a period, the characters in the name of an option are
  skipped until a `-' or the end of the name is reached.  This way,
  you can abbreviate words contained in the name of an option.

- You can omit characters at the end of the name.

The following list shows some valid (unambiguous) abbreviations for
+font-size-tolerance:

    +font-size-tol
    +font-size-tol.
    +f.s.t.
    +fo.size-t.
    +font..tol
    +..tol

Note that you can append `-x' or `-y' to some of the options.  Only
if the input ends with `x' or `y', the driver appends `-x' or `-y',
respectively, to the internal names of the options when looking for
a match.  This is to allow for abbreviating the name of the option
without making ambiguous the name without `-x' or `-y'.  (For in-
stance, if `-x' and `-y' were appended unconditionally to all names
in the list of known options, `+resolution' would match the three
options `+resolution', `+resolution-x' and `+resolution-y'.)

Letter case is not significant in the names of the options.  However,
letter case is significant in the arguments of some options.

Options may take arguments.  For the long form of an option, there
must be `:', `=' or `:=' between an option and its argument, for exam-
ple

    +width:210mm
    +width=210mm
    +width:=210mm

are all acceptable forms.  For the short form, there may be `:', `='
or `:=' between an option and its argument, for example

    /w210mm
    /w:210mm
    /w=210mm
    /w:=210mm

are all acceptable forms.

Note: `=' may not appear in an environment variable and cannot be
given in an argument to a batch file.  Semicolon and comma can also
not appear in an argument to a batch file (dangerous in connection
with templates).

If an option may take an argument, both forms of the option can take
an argument.  Note that for some options, the syntax for arguments is
different for the long and short forms.  The type of the argument is
shown below only for the short form.  Possible types are:

#       stands for a number which will sometimes be followed by a
        dimension (the dimension must be in lowercase).  Some options
        can be used to specify a value referring to the X coordi-
        nate or a value referring to the Y coordinate, for instance
        /r#.  With /r:300 both values are set.  To set only one of
        the two values, append `x' or `y' to the short name of the
        option: /rx:240 and /ry:216.  When using the long form,
        append `-x' or `-y' when setting the X or Y coordinate.
        Example (+resolution): Use +reso:300 to set both values, use
        +res.x:240 and +res.y:216 to set the values independently.

+       stands for `+' or `-' for the short form.  + turns the option
        on, - turns it off.  When using the long form, `on' and `y'
        turn the option on, `off' and `n' turn the option off.  If no
        argument is given, the option is turned on.

*       stands for any other type of argument.

The long form is always listed without an indication of the type of
the argument.


3.1 Options for message output
------------------------------

These options are used for listing the available options and for
controlling the amount of messages shown on the screen.


3.1.1 Getting a list of the options
-----------------------------------

These options list some or all options, including the current
settings.

+short-help  /?

    List the most frequently used options with their current settings.

+help  /??

    List all the options with their current settings.  Included are
    options which are usually set only once: in the configuration
    file.


3.1.2 Setting the verbosity level
---------------------------------

The verbosity level controls what messages are displayed on the
screen.  Independent of the verbosity level, all messages are written
to the log file.

+verbosity  /v#

    Set the verbosity level:

    0       display only fatal error messages

    1       display all messages of level 0, plus page numbers and
            font substitutions in batch mode

    2       display all messages of level 1, plus serious warnings,
            `Loading ...' and the DVI file comment

    3       display all messages of level 2, plus all warnings and
            \special's

    4       display all messages of level 3, plus statistics and the
            names of font files

    5       display all messages of level 4, plus comments in the
            font files

    The default setting is +verbosity:2.

    Note that +font-load-limit:-1 suppresses font comments and
    warnings of font problems.


3.2 Options for page selection
------------------------------

These options select the pages to be printed.  In the following the
difference between `pages', `sides' and `sheets' should be noted:
A page is a page from TeX's point of view, i.e., the DVI file
contains multiple pages with a TeX page number assigned to each of
them.  There may be multiple pages on one side (n-up printing, see
below), the sides are numbered sequentially, the pages are numbered
according to the TeX page number assigned to them.  A sheet contains
either one side (if printing single sided or if using two passes for
printing double sided) or two sides (if using +double-sided:long or
+double-sided:short).

The terms `side' and `sheet' are equivalent unless +double-sided:long
or +double-sided:short is used.

The terms `page' and `side' are equivalent if +rows:1 +columns:1 is
used.

The options are applied in the order they are shown below: Initially,
all sides are to be printed.  The first option removes certain sides
from consideration, the second then restricts the remaining sides and
so on.


3.2.1 Selecting sides by page number
------------------------------------

You can select a range of sides by giving the TeX page number of the
first page and/or the TeX page number of the last page.

+first-page  /b*

    Select the first side to be printed.  The DVI file will then be
    read from the beginning until a matching page is encountered.
    Further page selection will now begin, starting at the side
    containing this page.  An asterisk stands for any page number: at
    most 10 numbers can be given which will be compared with \count0
    to \count9 -- omitted numbers will be replaced with *.  The de-
    fault is * which means begin at the first page in the file.

    In the following example, selection begins with the page having
    \count0=-3 and \count2=4:

        +fi.p:-3.*.4

+last-page  /e*

    Select the last side.  After finding a suitable first side, the
    DVI file search will continue until a page matching this option's
    specification is encountered.  The side containing this page
    will be the last one.  The sides encompassing the range of pages
    selected by +first-page and +last-page will remain selected.  The
    default is *: this is an exception, it means that no matching for
    the last page will take place.

    In the following example, the last side is the one containing the
    page with the page number 10.5:

        +la.p:10.5


3.2.2 Double-sided printing
---------------------------

There are two ways of producing double-sided output: Use a printer
which automatically prints on both sides of the paper (duplex print-
ing) or print in two passes.

+double-sided  /d:e /d:o /d:-

    Double-sided printing: every other side is selected.
    +double-sided:odd selects sides 1., 3., ..., +double-sided:even
    selects the sides 2., 4., ...  The default is +double-sided:off,
    all sides are selected.  Additionally, you can use
    +double-sided:long and +double-sided:short with dvihplj (and
    dvidot for some parameter files) to automatically print
    double-sided on a suitable printer.  See the lists of dvihplj's
    and dvidot's options for details.  Use +backside-offset-x and
    +backside-offset-y to align frontside and backside.

    The arguments `e', `o' and `-' can be used instead of `even',
    `odd' and `off'.  When using the short form of this option, you
    have to use `e', `o' or `-'.

    The following example prints the first part of a double-sided
    document:

        +doub:odd

    The following example prints the second part of a double-sided
    document:

        +doub:even

    You might have to toggle the +backward option on the second pass.


3.2.3 Selecting sides by side index
-----------------------------------

The sides selected by the options above will be numbered
sequentially.  Use the following options to select sides by side
index.

+skip-sides  /k#

    The number of sides to skip: the first # of the sides in the
    chosen range will be skipped.  The default is 0.

    The following example will skip one side, the selection will
    begin with the second side:

        +skip:1

+number-of-sides  /n#

    The number of sides to print: at most # sides will be printed.
    Default: 65535, the maximum value.

    The following example will print at most 10 sides:

        +num:10


3.2.4 Selecting the order of the sheets
---------------------------------------

Some printers stack the output sheets face-up.  On those printers,
the last sheet should be printed first.

+backward  /z+

    Print the sheets in reverse order, starting with the last sheet
    selected.  The default is +backward:off, print the first sheet
    first.


3.2.5 Printing multiple copies
------------------------------

There are two methods for printing multiple copies of a document.

+copy-sheets  /ns#

    Print # copies of each sheet (uncollated copies): each sheet
    will be printed # times before going on to the next sheet.  The
    default setting is +copy-sheets:1 -- print each sheet only once.
    This option is not supported by dviscr, dvivik and dvipm (and
    dvidot when creating graphics files).

+copy-file  /nf#

    Print the whole file # times (collated copies).  The default
    setting is +copy-file:1 -- print the file only once.  For
    example, if four sides are to be printed, +copy-file:2 will
    cause them to be printed in the order 1 2 3 4 1 2 3 4.  When
    +copy-sheets and +copy-file are combined, +copy-sheets will
    be applied first, then +copy-file.  For example, printing two
    sides with the option setting +copy-sheets:2 +copy-file:3
    will result in the following order: 1 1 2 2 1 1 2 2 1 1 2 2.
    This option is not supported by dviscr, dvivik and dvipm (and
    dvidot when creating graphics files).  If +double-sided:long
    or +double-sided:short is used, empty sides are inserted as
    necessary to avoid printing the first side of the next copy on
    the backside of the last sheet of the previous copy.


3.3 Managing fonts and graphics files
-------------------------------------

Most of these options are set only once, during installation (in a
response file).  Some of these options are set in the configuration
files that come with the drivers.


3.3.1 Handling missing fonts and graphics files
-----------------------------------------------

There are three modes of handling missing font and graphics files.
Note that you can change the mode interactively when the driver
asks for a replacement for a missing font.  The default setting is
+batch-mode.

+batch-mode  /fb

    Automatic replacement of missing fonts.  If a font is not found
    a TFM file will be sought (characters will be replaced by
    rectangles if a TFM file is found).  If no TFM file can be found,
    characters from this font will be omitted, resulting in wrong
    positions of rules, characters from other fonts, etc.  This font
    search method can be altered with a font substitution file.  If
    a graphics file is not found and +batch-mode has been selected
    then the picture will be omitted.  +batch-mode is switched off
    by either +change-mode or +interactive-mode.  If MFjob and
    METAFONT shall be called for generating missing fonts, usage of
    +batch-mode is recommended unless you want to select which of
    the missing fonts should be generated.  The default setting is
    +batch-mode.

+change-mode  /fc

    Before a font or graphics file is loaded, the name of the file
    can be changed if +change-mode is active.  +change-mode is
    switched off by either +batch-mode or +interactive-mode.  The
    default setting is +batch-mode.

+interactive-mode  /fi

    If a font or graphics file cannot be found, you can change the
    magnification or the name if +interactive-mode is active.
    +interactive-mode is switched off by either +batch-mode or
    +change-mode.  The default setting is +batch-mode.

+omit-graphics  /fo+

    All \special{em:graph} commands will be ignored (without issuing
    warnings) if +omit-graphics:on is used.  That is, no graphics
    files will be inserted.


3.3.2 Scaling fonts
-------------------

+font-scaling  /fs#

    Font scaling.  These options are used to reduce the size of the
    font allowing a font generated for a higher resolution device to
    be used at a lower resolution (disk space!).  The reduction is
    accomplished by replacing the points in the rectangle of width
    +font-scaling-x and height +font-scaling-y by a single point.  If
    the rectangle is a square, +font-scaling:# can be used to set the
    width and height to the same value.  The values may lie in the
    range 1 to 8.  Printing with fonts reduced by this method gives
    results which are of noticeably poorer quality than fonts gener-
    ated by METAFONT directly.  The desired resolution must be set
    with the +font-resolution option.  The configuration files that
    come with the drivers set +font-scaling appropriately.

    The following example replaces the P6L fonts with scaled P6M
    fonts:

        +resolution:180 +font-scaling-x:2 +font-resolution-x:360


3.3.3 Font size tolerance
-------------------------

+font-size-tolerance  /ft#

    Allow for size tolerance when searching for fonts.  Before
    seeking a font, its size will be replaced by the closest size
    available, unless the relative deviation is greater than 0.2%.
    Then, the driver tries to find the font by trying the available
    sizes starting with the closest size and proceeding with less
    close sizes until the relative deviation from the size exceeds
    the value set by +font-size-tolerance.  Sizes with a greater
    deviation are not tried.  If a font is found and the deviation
    exceeds 0.2%, warning message 1208 will be displayed.  The
    tolerance is entered as percentage, the valid range is 0 to 20,
    that is, 0 to 20% of deviation.  Default value: 0.2 (that is,
    0.2%).  Values less than 0.2 are not recommended.  The available
    sizes of fonts are set with the +font-sizes option, additionally
    the sizes found in the font library files will be used.

+font-sizes  /fz*

    Available font sizes.  To be able to find fonts close (with
    respect to size) to the fonts requested, the drivers must be
    informed with +font-sizes about the available font sizes.  The
    sizes are given in DPI, you can use magnifications by typing :0
    to :9 (see below).  To enter more than one value, separate the
    values by commas (note: commas cannot be passed to batch files).
    You can either replace the previous set of sizes or -- by
    preceding the first value by `+' -- add sizes to the previous set
    of sizes.  The default value is :0,:h,:1,:2,:3,:4,:5,:6,:7,:8,:9,
    that is, the resolution set with +font-resolution, multiplied by
    1, sqrt(1.2), 1.2, 1.44, and so on, up to 1.2^9.  If the list
    starts with a colon (`:1', for instance), you must use `:', `='
    or `:=' to separate the value from `/fz', otherwise the colon
    would be read as delimiter (and ignored).

    The following example adds sizes 200 and 240:

        +font-sizes:+200,200:1

    In the following example only magstep1 is available:

        /fz::1


3.3.4 Initial loading of fonts
------------------------------

+font-load-limit  /fl#

    Font load limit.  When the driver first loads the font
    parameters from a font file (`Loading font ...') all those
    characters are loaded that need no more than # bytes of memory.
    +font-load-limit:-1 is a special case: the font parameters are
    loaded only when needed; initially, only the existence of the
    font file is checked.  +font-load-limit:-1, however, also stops
    warnings about problems with the font files and should only be
    used when you are sure that the fonts are alright.  The default
    is 300, that is, all characters which need 300 or fewer bytes of
    memory are immediately loaded.  If later a (larger) character is
    required which has not yet been loaded, the font file will have
    to be opened again.  If dviscr, dvivik or dvipm is used with
    fonts on a fixed disk, it is better to use +font-load-limit:0 or
    +font-load-limit:-1 as the first side appears on the screen more
    quickly (initial font load takes a little time.)  If the driver
    complains about lack of memory, it may help (but not necessarily)
    to use +font-load-limit:0 or +font-load-limit:-1; this doesn't
    reduce the memory required by the driver but may improve the way
    the available memory is used.

    The following example disables initial loading of characters:

        +f.l.l:0

    The following example causes characters to be loaded on demand:

        +f.l.l:-1

    In the following example, all characters smaller than 1000 bytes
    are initially loaded:

        +f.l.l:1000


3.3.5 Rounding character positions
----------------------------------

+max-drift  /fd#

    This sets the internal variable max_drift.  If the character
    or line spacing is uneven, a different value can be tried: the
    usual values range from 0 to 2, the default value is 1 if no
    configuration file is used.  You can set the horizontal and
    vertical values separately with +max-drift-x and +max-drift-y,
    respectively.  The DVI drivers standard recommends the following
    values:

        Resolution r (DPI) ³ max_drift
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄ
                 r < 100   ³    0
          100 <= r < 200   ³    1
          200 <= r         ³    2

    The values from this table are set by the configuration files
    that come with the drivers.

+use-tfm-files  /fu+

    This option is used for telling the driver whether TFM files
    shall be used for all fonts.  The pixel rounding algorithm
    requires the word space (and other parameters) defined for a
    font for rounding the positions of characters from that font.
    The word space parameter will be taken from TFM files if
    +use-tfm-files:on has been set.  If a TFM file is not found,
    warning message 1212 will be displayed and the font is treated as
    if +use-tfm-files:off were set.  If +use-tfm-files:off is set,
    the word space will be estimated by the driver.  The default
    setting is +use-tfm-files:off because in most cases there is no a
    visible difference.


3.3.6 Generating fonts automatically
------------------------------------

+ask-mfjob  /fa+

    If the default value +ask-mfjob:on is active, the drivers will
    ask for confirmation before running MFjob.  With +ask-mfjob:off,
    MFjob will be run automatically, without asking questions.

+call-mfjob  /fr+

    If the default value +call-mfjob:on is active, the drivers
    directly call MFjob under OS/2, without terminating the
    driver.  If you want to get the same behaviour as under DOS,
    use +call-mfjob:off.  In this case, the driver is terminated
    with return code 8 to indicate that MFjob should be invoked.
    +call-mfjob is ignored under DOS.

+metafont-mode  /fm*

    This option -- together with +mfjob-file -- is required for gener-
    ating missing fonts automatically by calling MFjob.  The METAFONT
    mode used for generating missing fonts is set by this option.
    The default value is empty, if no configuration files are used:
    MFjob will not be called automatically.  The configuration files
    that come with the drivers set +metafont-mode appropriately.

    The following example uses mode hplaser for the HP LaserJet
    family at 300 DPI:

        +m.m:hplaser


3.4 Side layout options
-----------------------

The options described here are used for specifying the paper size,
the offsets for achieving correct margins and the transformation
(printing orientation).


3.4.1 Specifying the paper size
-------------------------------

See also the +paper and +set-paper options of dvihplj.

+height  /h#

    Set the paper height.  This value is used by dviscr and dvivik to
    display the sheet edges as a border.  dvipm uses this value for
    the size of the sheet.  dvidot with parameter file for creating
    graphics files uses this value to set the size of the graphics
    files unless +minimize:on is selected.  dvidot with parameter
    file for printing on a dot matrix printer uses this value to
    decide how much of the side can be printed; however, as a form
    feed is used to eject a page the physical page length must be set
    on the printer.  `dvidot itoh' and `dvidot aiw' are an exception,
    they use the value set by +form-length for page ejects.  You
    should set +height to the height of the paper you are printing on.

    The following example sets the paper format to A4:

        +height:297mm +width:210mm

+width  /w#

    Set the paper width.  dviscr and dvivik use this value for
    displaying the edges of the sheet.  dvipm uses this value for
    the size of the sheet.  dvidot with parameter file for creating
    graphics files uses this value to determine the size of the
    graphics files unless +minimize:on is given.  The dvidot driver
    with parameter file for dot matrix printers reduces this value
    by 1px if the value given is exactly the maximum paper width.
    `dvidot fx80', for example, reduces this width by 1px if, when
    converted, it is exactly 1920px.  You should set +width to the
    width of the paper you are printing on.


3.4.2 Transformation (orientation)
----------------------------------

+transformation  +portrait-mode  +landscape-mode  /tr#

    Output transformation.  The following values are available:

    0       normal output (portrait mode)

    1       rotate 90 degrees anticlockwise (landscape mode)

    2       rotate 180 degrees

    3       rotate 270 degrees anticlockwise

    4       reflect about the \ diagonal

    5       reflect vertically

    6       reflect about the / diagonal

    7       reflect horizontally

    In practice +transformation:0 (+portrait-mode) and
    +transformation:1 (+landscape-mode) are most often used.

    The transformations when applied to the pattern

        A B
        C D
        E F

    are

         0  ³   1   ³  2  ³   3   ³   4   ³  5  ³   6   ³  7
        ÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄ
        A B ³ B D F ³ F E ³ E C A ³ A C E ³ E F ³ F D B ³ B A
        C D ³ A C E ³ D C ³ F D B ³ B D F ³ C D ³ E C A ³ D C
        E F ³       ³ B A ³       ³       ³ A B ³       ³ F E

    It is important to set the paper height and width correctly with
    +height and +width (for coordinate transformations).

    The same paper dimensions and offsets can be used for all
    transformations, that is, +height, +width, +top-margin and
    +left-margin need not be changed.  The margins set with
    +page-top-margin and +page-left-margin are `above' or `left' of
    the text and will be transformed.

    If +resolution-x and +resolution-y differ then different fonts
    will be needed when rotating by 90 or 270 degrees or reflecting
    about a diagonal -- this applies to the EPSON FX-80/100, NEC
    P6/P7 (360x180DPI) C.Itoh 8510A and Apple Imagewriter printers.

    For key assignments for dviscr and dvivik, see <K> and <T>.

    When using transformations 1 through 7, some restrictions apply:

    - \special{em:graph} doesn't work and will be ignored

    - dvihplj cannot use built-in fonts (see the description of font
      substitution files for details) unless using an HP LaserJet III
      or later.

    When using transformations 4 through 7, dvihplj cannot use
    built-in fonts (see the description of font substitution files
    for details).


3.4.3 Moving the output on the sheet
------------------------------------

+left-margin  /l#

    Left margin: The output will be moved # to the right.  The
    default value is 0in.  This option is intended to be set in a
    configuration file or environment variable to adjust the margins
    for your particular printer.  To find the correct value of this
    option for your printer, print \emtex\doc\adjust.dvi with the
    option +left-margin:0 and measure the distance from the left
    margin to the printed square.  Take an inch (25.4 mm) off this,
    change the sign, and set +left-margin to the resulting value.
    The offset specified by +left-margin is always measured from the
    left of the sheet and is not affected by +transformation.  See
    also +page-left-margin.

    The following example moves output right by 1 cm:

        +left:1cm

+top-margin  /t#

    Top margin.  The output will be moved down the sheet by #.  The
    default value is 0in.  This option is intended to be set in a
    configuration file or environment variable to adjust the margins
    for your particular printer.  To find the correct value of this
    option for your printer, print \emtex\doc\adjust.dvi with the
    option +top-margin:0 and measure the distance from the top edge
    of the paper to the square.  Take 1 inch (25.4mm) from this,
    change the sign, and set +top-margin to the resulting value.  The
    offset specified by +top-margin is always measured from the top
    of the sheet and is not affected by +transformation.  See also
    +page-top-margin.

+page-left-margin  /al#

    This option specifies the (logical) left margin of a page.
    This left margin is always to the left of the page, subject to
    +transformation.  The default value is 1in, as assumed by most
    TeX formats.

+page-top-margin  /at#

    This option specifies the (logical) top margin of a page.  This
    top margin is always above the page, subject to +transformation.
    The default value is 1in, as assumed by most TeX formats.

+backside-offset-x  +backside-offset-y  /ax#  /ay#

    Shift backsides to make them align with the frontsides.
    The output on backsides is moved to the right by the value
    of +backside-offset-x and is moved down by the value of
    +backside-offset-y.  On frontsides, these options are ignored.

    With +double-sided:off and +double-sided:odd, the values
    of +backside-offset-x and +backside-offset-y are ignored.
    With +double-sided:even, the values of +backside-offset-x
    and +backside-offset-y are applied to all sides.  With
    +double-sided:long and +double-sided:short, the side first
    printed is considered a frontside.

    Both values may be negative to move in the opposite direction.
    The default value of both options is 0in.


3.5 Producing booklets and books, n-up printing
-----------------------------------------------

The options described here are used for printing multiple pages on
a side, optionally suitable for folding and saddle-stitching in the
middle.  Basically, there are two applications of printing multiple
pages on a side:

1.  Making a booklet or book.  See +section-count and +section-size
    for details.

2.  Printing multiple pages on a sheet to save paper.  In this case,
    the pages are arranged on the sheets in the order they are
    read from the DVI file, left to right, top to bottom.  See the
    description of +page-list-file for figures.

Additionally, you can assign each page to one of the locations
defined by +rows, +columns, +page-width and +page-height by supplying
a file containing a list of pages.  See +page-list-file for details.


3.5.1 Defining the locations of the pages on a sheet
----------------------------------------------------

+columns  +rows  /ac#  /ar#

    Use these options to specify the number of columns and rows
    of pages on a side.  The default value is 1 for both options,
    telling the driver to put one page on each side.  The number of
    pages to be printed side by side is set by +columns.  The number
    of pages to be printed above one another is set by +rows.

    The meaning of `side by side' depends on the +transformation and
    +fold-other options.  For +portrait-mode and +fold-other:off
    (the default values), the meaning is the usual one.  Choosing
    +fold-other:on reverses the meaning of `rows' and `columns'.
    Choosing a transformation which flips the X and Y axes
    (+landscape-mode, for instance) reverses the meaning of `rows'
    and `columns'.

    The number of pages per side is the product of the values of
    +rows and +columns.

+page-height  +page-width   /ah#  /aw#

    These options set the height and width, respectively, of the
    pages.  These values define the vertical and horizontal distance
    of the pages arranged in the grid defined by +columns and +rows.
    The default value of +page-height is 11in, the default value
    of +page-width is 8.5in.  These options are ignored unless
    +columns or +rows is set to a value greater than 1.  The location
    of a page within the grid is defined by +page-left-margin
    and +page-top-margin.  As for those options, the meaning of
    +page-height and +page-width is also affected by +transformation.


3.5.2 Arranging the pages
-------------------------

+page-list-file  /pp*

    Set the path name of the page list file (the value is a template,
    see below for details).  If the value is empty (which is the
    default), no page list file is used.  If a page list file is
    specified with +page-list-file, the pages are distributed to
    sides according to the contents of this file.

    For each side to be printed, there is one line in the file.  Each
    line contains one entry for each page per side (see +columns and
    +rows).  If there are R rows, the first R entries are for the
    first row, the next R entries are for the second row, and so on:

        +portrait-mode
        
        ÚÄÄÄ¿  ÚÄÄÄ¿  ÚÄÄÄ¿
        ³1 2³  ³1 2³  ³1 2³
        ÀÄÄÄÙ  ³3 4³  ³3 4³
               ÀÄÄÄÙ  ³5 6³
                      ÀÄÄÄÙ
        
        +landscape-mode
        
        ÚÄ¿  ÚÄÄÄ¿  ÚÄÄÄÄÄ¿
        ³2³  ³2 4³  ³2 4 6³
        ³1³  ³1 3³  ³1 3 5³
        ÀÄÙ  ÀÄÄÄÙ  ÀÄÄÄÄÄÙ

    Note that this is subject to +fold-other.

    An entry is either `-' to leave that position empty or a page
    index (the pages of the DVI file are assigned page indices
    sequentially, starting with 1 for the first page) to select this
    page into the row and column associated with the entry.  Entries
    are separated by spaces.

    Lines starting with `%' and empty lines are ignored.  You can put
    a comment after the last entry of a line by preceding the comment
    with at least one space and a `%' character.

    If a page list file is used, the +blank-pages and +page-shift
    options are ignored.

    Here's an example of a page list file:

        % Sample page list file
        % For use with +columns:2 +rows:1
        
        8 1             % Side 1
        2 7             % Side 2
        6 3             % Side 3
        4 5             % Side 4

+section-count  +section-size   /an#  /az#

    To produce a book or a booklet, use one of these options,
    together with the options for defining the locations of pages on
    sides (+rows, +columns, etc.).

    If +section-count or +section-size is set to a non-zero value,
    the pages are rearranged to make sheets which can be made into
    a booklet or a book consisting of several sections by cutting,
    folding and saddle-stitching in the middle.  To make a booklet,
    take the stack of sheets of one section, cut and sort it (if
    there are more than 2 pages per side), then fold it once.  Now
    you can saddle-stitch the stack in the middle.  To make a book,
    make a booklet from each section and bind the booklets into a
    book.

    The number of sections (booklets) is either set by +section-count
    (which defines the number of sections) or computed from the value
    of +section-size (which defines the number of booklet sheets
    per section, that is the number of pages per section divided
    by 4).  If both +section-count and +section-size are set to a
    non-zero value, +section-count supersedes +section-size.  A
    warning message is displayed if the values of +section-count and
    +section-size disagree.

    If +section-count or +section-size is set to a non-zero value,
    the driver assumes that you want to make a book or booklet.
    Therefore, it aborts with an error message if one of the
    following conditions is false:

    - A page list file must not be used (+page-list-file should have
      an empty value).

    - The number of columns of pages (+columns) must be even (and
      greater than one).

    The default value for +section-count and +section-size is 0.  If
    both +section-count and +section-size are set to 0, no book is
    produced.

    The last section can be smaller than the preceding sections of a
    book.  See +full-last-section for details.

+full-last-section  /ae+

    If the number of pages of a book isn't an integral multiple of
    the number of pages per section, there will be some empty pages
    in the last section.  By default (+full-last-section:off),
    the driver reduces the size of the last section to minimize
    the number of blank pages at the end of the section.  Use
    +full-last-section:on to make the last section the same size as
    the other sections, i.e., output blank pages as necessary.


3.5.3 Special effects
---------------------

+blank-pages  /ab#

    Insert blank pages at the beginning, shifting all selected
    pages.  The default value is 0, which means not to insert blank
    pages.  This option can be used for leaving room for a title
    page, without having to put a blank page into the DVI file (which
    can be quite difficult).  Note that +blank-pages modifies the
    way pages are arranged on sheets and therefore affects the page
    selection.  +blank-pages is ignored if +page-list-file is used.

+fold-other  /af+

    Use +fold-other:on to arrange the pages for folding the other
    way.  By default (+fold-other:off), the driver assumes that you
    want to get `left' and `right' pages.  However, a calendar, for
    instance, has `top' and `bottom' pages.  To achieve this effect,
    use +fold-other:on.

+page-shift  /as#

    Shift the pages to compensate for the paper thickness.  When
    making a booklet, `outer' pages are shifted away from the fold by
    the value of +page-shift, multiplied by the number of layers.
    The innermost pair of pages is not shifted.  To find the correct
    value of +page-shift, start at about 1.5 times (pi/2) the
    thickness of the paper.


3.5.4 Examples
--------------

To make a portrait-mode booklet by printing in landscape mode,
putting two A5 pages on an A4 side (no cutting is required), use the
following options:

    +columns:2 +rows:1 +section-count:1
    +page-width:149mm +page-height:210mm
    +landscape-mode +double-sided:short

If your printer does not support +double-sided:short, you have to
use +double-sided:odd, then reinsert the paper (turning around the
short edge, that is, upside down) and use +double-sided:even.  Use
+backside-offset-y to align the frontside and the backside.

To make a portrait-mode booklet by printing in portrait mode, putting
four A6 pages on an A4 side (requiring cutting all the sheets into
two), use the following options:

    +columns:2 +rows:2 +section-count:1
    +page-width:105mm +page-height:149mm
    +portrait-mode +double-sided:long

If your printer does not support +double-sided:long, you have to use
+double-sided:odd, then reinsert the paper (turn around the long
edge) and use +double-sided:even.  Use +backside-offset-x to align
the frontside and the backside.

Additionally, you should set +page-shift in all cases.  Adjust the
+page-width and +page-height values to control the distance between
the pages.


3.6 Magnification and resolution
--------------------------------

Some of the options described here are set in the configuration files
that come with the drivers.


3.6.1 Setting the resolution
----------------------------

+resolution  /r#

    Set the resolution.  +resolution-x sets the horizontal
    resolution, +resolution-y the vertical and +resolution:# both at
    once.  The default value is 300, dvidot uses the value set in
    the parameter file.  These values are in dots per inch (DPI).
    Make sure that the appropriate fonts are available!  A number of
    parameters can only be calculated when the resolution is known:
    the driver will only convert the values when all the options have
    been read, therefore the +resolution option doesn't have be the
    first one.  See also +font-resolution.  The configuration files
    that come with the drivers set +resolution appropriately.

    The following example sets the resolution to 180 DPI:

        +resol:180

+font-resolution  /rf#

    Set the font resolution, the argument is in DPI.  This option
    will usually be used together with +font-scaling.  The hori-
    zontal and vertical resolution can be set individually with
    +font-resolution-x and +font-resolution-y.  If +font-resolution
    is omitted, the value used for the font will be that set by
    +resolution.  The configuration files that come with the drivers
    set +font-resolution appropriately.

+graphics-resolution  /rg#

    Set the resolution for the graphics files, the argument is in
    DPI.  This option merely sets the values which will be used for
    @r in +graphics-files.  The horizontal and vertical resolution
    can be set individually with +graphics-resolution-x and
    +graphics-resolution-y.  If +graphics-resolution is omitted, the
    value used will be that set by +resolution.


3.6.2 Setting the magnification
-------------------------------

+magnification  /m#

    the magnification in the DVI file is replaced by # which can take
    any value from 100 to 16000.  The values are the same as those
    used for \mag, that is, the magnification multiplied by 1000
    (+magnification:1000 gives the normal size) or as h, 0 to 5, they
    represent \magstephalf, \magstep0 to \magstep5.  The values 6 to
    9 will be interpreted similarly.

    To multiply the magnification in the DVI file with a value,
    precede the value with a `*' character.

    If this option is used without an argument, the magnification of
    the DVI file will be used (this is equivalent to an argument of
    `*1000' or `*0').  Using the magnification of the DVI file is the
    default setting.

    Note that fonts in appropriate sizes are required.

    The following example replaces the magnification with sqrt(2):

        +mag:1414.21356

    The following example multiplies the magnification with sqrt(1.2):

        +mag:*h


3.7 Directory and file name options
-----------------------------------

The following options accept templates to specify a number of
different search paths for files.  See section 3.14 for details about
templates.  Some of the options described here are set in the configu-
ration files that come with the drivers.


3.7.1 Search paths
------------------

When using a search path for finding a file, the first successful
expansion of the template will be used.

+dvi-file  /pd*

    the template used when searching for the DVI file (input file).
    @i will be replaced with the name of the DVI file (the default ex-
    tension DVI has been already attached if necessary).  The default
    value is @i, telling the driver just to look for the specified
    file.  The configuration files change the setting of +dvi-file
    to seek DVI files in the current working directory and in the
    directories listed in the DVIDRVINPUT environment variable.

    The following example tells the driver to search the specified
    directory, d:\dvi, and d:\mytex:

        +dvi-f:{,d:\dvi\,d:\mytex\}@i

+font-files  /pf*

    the template used when locating font files (PK, PXL and VF
    files).  @f will be replaced with the name of the font.  dvidot
    reads the default value from the parameter file, the default
    value for all other drivers is

        \texfonts\pixel.lj\@Rrdpi\@f.{pk,pxl}

    which -- when used for finding the font `cmr10 scaled 1200' with
    +font-resolution:300 -- tries to open the files

        \texfonts\pixel.lj\360dpi\cmr10.pk

    and

        \texfonts\pixel.lj\360dpi\cmr10.pxl

    in this sequence.  However, the configuration files that come
    with the drivers change +font-files to use the DVIDRVFONTS envi-
    ronment variable.  fx.cnf, for instance, uses the template

        $DVIDRVFONTS:pixel.fx\@Rrdpi\@f{.pk,.pxl}

    To use VF files, specify the path of the VF files with
    +font-files or with +virtual-fonts.  Example:

        +font-files:$DVIDRVFONTS:{pixel.fx\@Rrdpi\@f{.pk,.pxl},vf\@f.vf}

+graphics-files  /pg*

    the template used when locating graphics files (MSP, PCX and BMP
    files).  @f will be replaced with the name of the picture.  The
    default value

        @PBf{@Ef,.msp,.pcx,.bmp}

    makes the driver look for the following files:

        name (@f)    ³ files
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
        test         ³ test.       test.msp    test.pcx    test.bmp
        test.ext     ³ test.ext    test.msp    test.pcx    test.bmp
        \g\test      ³ \g\test.ext \g\test.msp \g\test.pcx \g\test.bmp

    However, the configuration files that come with the drivers
    change +graphics-files to use the DVIDRVGRAPH environment vari-
    able:

        {,$DVIDRVGRAPH:}{@Rrdpi\,}@PBf{@Ef,.msp,.pcx,.bmp}

    The following example works like the default value, but also
    searches the directories given in the DVIDRVGRAPH environment
    variable:

        +graph.f:{,$DVIDRVGRAPH:}@PBf{@Ef,.msp,.pcx}

+response-files  /pr*

    the template used when searching for response files (@name).
    @f will be replaced with the name of the response file, with
    the default extension CNF applied.  The default value is
    {,$EMTEX:data\}@f, which makes the driver search the specified
    directory (or the current working directory, if the name of the
    response file doesn't specify a directory) and then the `data'
    subdirectory of the emTeX directory.

    The following example searches the specified directory, c:\emtex,
    and d:\mytex for response files:

        +response-files:{,c:\emtex\,d:\mytex\}@f

+virtual-fonts  /pv*

    the template for VF files (virtual fonts), in addition to
    +font-files.  @f will be replaced with the name of the font.
    If the template is non-empty, the driver will search for
    virtual fonts before searching a font in the font libraries
    (+font-libraries) and in single files (+font-files).  If you
    don't want to replace existing fonts with virtual fonts, you
    should use +virtual-fonts: (with an empty template), which is the
    default value, to speed up font search.

    In the following example, VF files are located in directory
    c:\fonts\vf, the file name extension is VF:

        +virt:c:\fonts\vf\@f.vf


3.7.2 Input files
-----------------

For input files, all expansions of the template will be used
successively.

+init-files  /pi*

    printer initialization files.  The files given by +init-files
    will be sent to the printer immediately after it has been reset.
    You may use a template for giving more than one file.

    The following example sends the files unidir.p6 and init.p6 to
    the printer:

        +init-f:unidir.p6,init.p6

+font-libraries  /pl*

    the template for the fonts libraries to be used.  Fonts are
    sought first in these libraries and then as single files.  Font
    libraries can be created with fontlib.  The default extension
    is FLI.  The configuration files that come with the drivers set
    +font-libraries appropriately, using the DVIDRVFONTS environment
    variable.

    The following example lets the driver look for the font libraries
    lj_base.fli and lj_more.fli in the directories given in the
    DVIDRVFONTS environment variable.  If this environment variable
    lists more than one directory, you'll probably get some warning
    messages about missing files:

        +font-lib:$DVIDRVFONTS:lj_{base,more}

+font-subst-files  /ps*

    the names of the font substitution files.  The default is no
    font substitution file.  You can use a template.  The driver
    searches font substitution files in the specified directory (or
    the current working directory, if the name doesn't specify a
    directory) and then in the `data' subdirectory of the emTeX direc-
    tory.  The default extension is SUB.

    The following example reads the three files circle.sub, sub1.sub,
    and sub2.sub:

        +f.subst:circle,sub1,sub2


3.7.3 Output files
------------------

For output files, only the first expansion of the template will be
used.

+mfjob-file  /pj*

    Name of the file created when missing fonts are to be gener-
    ated by calling MFjob.  See also +metafont-mode.  When calling
    a driver via the dvidrv.exe program, this option will be set
    automatically to the name of a temporary file.  The default value
    is {$TMP:,}dv@u.mfj, that is, a file named dv#.mfj is created
    under OS/2, where # is a number that is chosen by the driver
    to not overwrite an existing file.  The file will be created
    in the directory specified by the TMP environment variable.
    If TMP is not set, the file will be created in the current
    working directory.  Under DOS, the default value causes MFjob
    not to be called, as @u is used.  The file will be created only
    if there are missing fonts, a METAFONT mode has been set with
    +metafont-mode and a file name has been set with +mfjob-file.

+default-output-file  /po*

    this option sets the default name of the output file.  If the
    driver is called without an output file name, this name will be
    used.  Default value: no default output file.  You can use a
    template, but only the first expansion will be used.  This option
    is used only to set the default; to specify the output file name
    when running a driver, enter the file name directly without using
    this option.

    With the following example, output goes to LPT1 unless an output
    file name is given on the command line:

        +def.out:lpt1

+transcript-file  /pt*

    the name of the log file (transcript file).  The default is `@d',
    ie, the name of the driver with extension DLG (for instance,
    dviscr.dlg).  All output that follows the input of the files and
    options is written to this file.  It also contains the current
    settings of all the options for the run.  The +transcript-file:
    option suppresses the creation of a log file.  A log file can
    later be used as a response file to set up the same conditions
    again.  You can use a template, but only the first expansion will
    be used.

    In the following example, the name of the DVI file with file name
    extension DLO in the current working directory will be used for
    the log file:

        +tr.file:@Bi.dlo

+fontlib-file  /pw*

    Write a fontlib response file.  A text file containing the
    fontlib commands to insert the fonts used in the run into a font
    library will be generated.  To generate only this response file
    use the option +number-of-sides:0.  You can use a template, but
    only the first expansion will be used.

    For example, the fontlib call for

        +fontlib-file:new.cmd

    is

        fontlib /k new @new.cmd


3.8 Miscellaneous options
-------------------------

Options which don't fit any of the categories above are described
here.


3.8.1 Meta options
------------------

These options deal with options.

+options  //

    Prompt for options.  When +options is used the driver will prompt
    for further options, this can be useful when the options required
    exceed the permitted length of the command line.  This option is
    not supported by dvipm.

+unit  /u*

    This option sets the default dimension unit to be used when none
    is given.  The default is inch.  The following dimension units
    can be used (cf. The TeXbook p. 57)

    pt      point (1/72.27in)

    pc      pica (12pt)

    in      inch (default)

    bp      big point (1/72in)

    cm      centimeter

    mm      millimeter

    dd      didot point (1238/1157pt)

    cc      cicero (12dd)

    sp      scaled point (1/65536pt)

    px      Pixel (resolution independent)

    All these units must be entered in lowercase.  The +unit option
    affects all following options.

    The following example is INVALID, megameters are somewhat
    impractical:

        +unit:Mm


3.8.2 Memory management
-----------------------

+use-ems  /xe+

    Use expanded memory (EMS) under DOS.  The default setting is
    +use-ems:on, which enables usage of EMS.  +use-ems:off disables
    usage of EMS, data will be swapped to disk if there isn't enough
    main memory.  EMS 4.0 or later is required.

+use-xms  /xx+

    Use extended memory (XMS) under DOS.  The default setting is
    +use-xms:on, which enables usage of XMS.  +use-xms:off disables
    usage of XMS, data will be swapped to disk if there isn't enough
    main memory.


3.9 Additional options for dviscr and dvivik
--------------------------------------------

Unless otherwise noted, these options are available for both dviscr
and dvivik.


3.9.1 Configuration
-------------------

+adapter  /oa#

    Adapter setting for dviscr, the possible values are:

    0       automatic selection (default)

    1       CGA 640x200

    2       EGA 640x350 or 640x200

    3       VGA 640x480

    4       Hercules Graphics Card 720x348, not under OS/2

    5       GENOA SuperEGA 800x600, not under OS/2

    6       Paradise VGA 800x600, not under OS/2

    7       Video Seven VGA 800x600, not under OS/2

    8       Tseng Labs EVA 800x600, not under OS/2

    9       HP Vectra 640x400, not under OS/2

    10      MDS Genius (PRIMUS II) 728x1008, not under OS/2

    11      EGA 640x200, 16 colors

    12      EGA 640x350, 16 colors

    13      EGA 640x350, 16/64 colors

    14      VGA 640x480, 16 colors

    15      VGA 640x480, 16/64 colors

    16      VGA 640x480, 16/262144 colors

    17      EGA 640x350, black and white

    18      VGA 640x480, black and white

    19      Olivetti M24 640x400, not under OS/2

    20      Adapter Interface 1024x768 (8514/A), not under OS/2.
            HDILOAD or another program providing the Adapter
            Interface must be loaded.

    21      VESA 800x600, 16 colors, not under OS/2.  For some
            graphics adapters, a program providing the VESA BIOS
            Extensions (VBE) must be loaded.

    22      VESA 1024x768, 16 colors, not under OS/2.  For some
            graphics adapters, a program providing the VESA BIOS
            Extensions (VBE) must be loaded.

    23      VESA 1280x1024, 16 colors, not under OS/2.  For some
            graphics adapters, a program providing the VESA BIOS
            Extensions (VBE) must be loaded.

    Further adapter-specific modes may be used with the following
    extension of this option:

        +adapter:M:W:H:AX:BX

    where M is a number which describes the adapter and display
    combination:

    100     EGA with monochrome display

    101     EGA with 16 color display

    102     EGA with 64 color display

    103     VGA with analogue color display,

    W is the screen width in pixels (320 to 1024), and H is the
    screen height in pixels (200 to 1024).

    The graphics mode is set by loading registers AX and BX with
    the arguments AX and BX before calling interrupt 10H.  AX and
    BX must be given in hexadecimal.  `:BX' can be omitted if BX is
    to be set to zero.  The colons may be replaced with semicolons
    if desired (however, semicolons cannot be used as arguments of
    batch files).  If (W/8)*H exceeds 65536 then H will be reduced to
    65536/(W/8).  In consequence, 1024x768 is not supported.  You are
    responsible for entering the correct values, the manual for your
    adapter can sometimes give further help.  Example: the graphics
    mode selected by +adapter:13 can be represented as

        +adapter:102:640:350:0010

    and mode +adapter:7 is the same as

        +adapter:103:800:600:6f05:62

    Here's a list of values (without warranty) for some graphics
    adapters:

    Acumos AVGA2, AVGA3                         /oa103:800:600:58
    Advance Logic AL2101                        /oa103:800:600:2B
    Ahead V5000                                 /oa103:800:600:71
    ATI VGAWONDER, Graphics Ultra etc.          /oa103:800:600:54
    Chips and Technologies                      /oa103:800:600:6A
    Cirrus Logic CL-GD 500/600                  /oa103:800:600:64
    Cirrus Logic GD 5422                        /oa103:800:600:58
    Compaq VGA                                  /oa103:800:600:59
    CTI                                         /oa103:800:600:6A
    Diamond Stealth                             /oa103:800:600:4F02:0102
    Everex                                      /oa103:800:600:70:02
    Genoa 5xxx, Sigma VGA                       /oa103:800:600:29
    Genoa 6xxx                                  /oa103:800:600:6A
    MXIC MX 68010                               /oa103:800:600:55
    NCR 77C22                                   /oa103:800:600:58
    OAK Technologies OTI-067, OTI-077, OTI037C  /oa103:800:600:52
    OAK Technologies OTI037C w/ NEL BIOS        /oa103:800:600:5B
    Orchid Prodesigner                          /oa103:800:600:29
    Paradise                                    /oa103:800:600:58
    Poach                                       /oa103:800:600:6A
    Primus                                      /oa103:800:600:2A
    Realtek RT 3106                             /oa103:800:600:1F
    S3                                          /oa103:800:600:4F02:0102
    Tecmar                                      /oa103:800:600:16
    Trident 8900                                /oa103:800:600:5B
    Trident 9400 CXi                            /oa103:800:600:6A
    Tseng ET-3000, ET-4000                      /oa103:800:600:29
    V7 Mirage                                   /oa103:800:600:6A
    VEGA                                        /oa103:800:600:29
    VESA compatible adapters                    /oa103:800:600:4F02:0102
    Video 7 SVGA                                /oa103:800:600:62
    WD90C11                                     /oa103:800:600:5C
    Western Digital                             /oa103:800:600:58

    If you spot something wrong in this table, please send the
    correct values to the author.

+color  /oc#

    Set the colors to be used by dviscr (only with EGA or VGA).  The
    possible values are 0 to 15, the default is +color:2 (green).
    You can set different colors for the various screen elements:

    +color:p#  /ocp:#
            paper border

    +color:r#  /ocr:#
            ruler

    +color:s#  /ocs:#
            status line

    If you omit the letter specifying the screen element (`p', `r',
    and `s'), the color will be used for all screen elements.

    The following colors are available:

    1       blue

    2       green

    3       cyan

    4       red

    5       magenta

    6       yellow

    7       white

+home-x  +home-y  /hx#  /hy#

    Set the initial position on the side to be displayed in the top
    left corner of the screen.  A new page will be displayed in this
    position and pressing the <Home> key will cause the current side
    to be displayed in this position.  +home-x:0 +home-y:0 is the top
    left-hand corner of the sheet.  +home-x:1in +home-y:1in is the
    default setting.

+inverse  /oi+

    Inverse display.  Use +inverse:off (default) to display black on
    a white background, use +inverse:on to display white on black
    background.

+zoom  /o#

    Reduce the size of the displayed side by using gray scales
    (dviscr).  A rectangle of X x Y pixels will be displayed as one
    pixel on the screen.  +zoom:# sets both X and Y, +zoom-x sets X
    alone and +zoom-y sets Y alone.  An EGA (with 16 color display)
    or a VGA adapter is required.  If both X and Y are 1, there is no
    gray scale display.  X and Y can take values from 1 to 8.  The
    implementation is optimized for +zoom-x values of 1, 2, 3, 4 and
    8.  Setting +zoom-x to 5 or 7 makes the driver almost unusably
    slow.  If +scaling:1 is set (no scaling) and gray scale is
    enabled with +zoom but the adapter does not support gray scales,
    the +zoom values are used for scaling instead, that is, +zoom:3
    is the same as +zoom:1 +scaling:3.

    Example:

        +z.x:4 +z.y:2

+ruler  /or+

    Enable the ruler (default is no ruler).

+status-line  /os+

    Enable status line (default).  If the status line is disabled,
    there will be a beep at the beginning and end of text or numeric
    input.

+ruler-unit  /ou*

    Select the dimension for the ruler and the status line (default
    is pt).

+scaling  /s#

    Reduce the size of the output page; this allows more of the side
    to be seen on the screen.  The pixels in a rectangle of width
    +scaling-x pixels and height +scaling-y pixels will be displayed
    as a single pixel.  +scaling:# sets both X and Y to the same
    value.  Possible values range from 1 to 8.  If fonts in suitable
    resolutions are available then it is better to change the
    resolution with +resolution (by using a different configuration
    file) as reduced characters are not pretty.  Even better, use
    gray scaling -- see +zoom, but only with an EGA or VGA card and a
    16 (or 64) color display.  If gray scaling is not possible, then
    scaling can be set with +zoom, too.

    The following example halves the resolution (both X and Y):

        +scaling:2

    The following example reduces the width to 1/4 and halves the
    height:

        +s.x:4 +s.y:2   


3.10 Additional options for dvipm
---------------------------------

Note that some settings can be changed only by using the menus and
dialog boxes.


3.10.1 Configuration
--------------------

+bitmap-memory-limit  /om#

    Maximum size in Kbytes of the temporary bitmaps.  The default
    value is 512, that is, at most 512 Kbytes will be used for tempo-
    rary bitmaps.  Values between 0 and 65535 can be set.  If your
    machine has much memory, you can improve the speed by increasing
    this value.  If your machine has little memory, you can improve
    the speed by decreasing this value.

+home-x  +home-y  /hx#  /hy#

    Set the initial position on the side to be displayed in the top
    left corner of the screen.  A new side will be displayed in this
    position and pressing the <Home> key will cause the current side
    to be displayed in this position.  +home-x:0 +home-y:0 is the top
    left corner of the sheet.  +home-x:1in +home-y:1in is the default
    setting.

+ruler-unit  /ou*

    Select the dimension for the ruler and for displaying the cursor
    position (default is pt).

+scaling  /s#

    Reduce the size of the displayed page, this allows more of the
    side to be seen in the window.  The pixels in a rectangle of
    width +scaling-x pixels and height +scaling-y pixels will be
    displayed as a single pixel.  +scaling:# sets both X and Y to
    the same value.  Possible values range from 1 to 8.  If fonts in
    suitable resolutions are available then it is better to change
    the resolution with +resolution (by using a different configura-
    tion file) as reduced characters are not pretty.

+zoom  /o#

    Reduce the size of the displayed side by using gray scales.
    A rectangle of X x Y pixels will be displayed as one pixel on
    the screen.  +zoom:# sets both X and Y, +zoom-x sets X alone
    and +zoom-y sets Y alone.  If both X and Y are 1, there is no
    gray scale display.  X and Y can take values from 1 to 8.  The
    implementation is optimized for +zoom-x values of 1, 2, 4, 6 and
    8.  Setting +zoom-x to 5 or 7 makes the driver almost unusably
    slow.

    Example:

        +z.x:4 +z.y:2


3.11 Additional options for dvidot when printing on a dot matrix printer
------------------------------------------------------------------------

dvidot has two principal modes of operation: printing on a dot matrix
printer and creating bitmap files.  The mode is selected by the param-
eter file.  This section describes the options applying to printing
on a dot matrix printer.


3.11.1 Options for all parameter files
--------------------------------------

+close  /os#

    Close and reopen the output file after printing # sheets at
    a time.  For instance, this is useful for use with printer
    spoolers.  +close:0 (the default setting) disables this feature,
    that is, the output file will be closed once at the end of the
    print job.  Prior to closing the output file, the printer will
    be reset.  After reopening the output file, the printer will be
    reinitialized.  This effectively splits the output of dvidot into
    several print jobs, allowing printing to start while more pages
    are being output.

+double-sided:long  +double-sided:short  /d:l  /d:s

    Double-sided printing, the printer automatically prints on both
    sides of the paper.  +double-sided:long is used for long-edge
    binding (the sheets are bound along the length of the sheet),
    +double-sided:short is used for short-edge binding (the sheets
    are bound along the width of the sheet).  The +copy-file and
    +copy-sheets options work as expected with +double-sided:long and
    +double-sided:short.  This option cannot be used with all param-
    eter files (in fact, there is currently no parameter file which
    enables +double-sided:long or +double-sided:short).

+final-formfeed

    If +final-formfeed:on is active, a formfeed will be sent to the
    printer after printing the last sheet.  This is the default.
    +final-formfeed:off suppresses the final formfeed.  That may be
    desired if the operating system automatically appends a formfeed.

+final-reset  /oe+

    Reset printer after each print job.  This is the default.  You
    can suppress resetting the printer by using +final-reset:off.

+initial-formfeed

    If +initial-formfeed is active, a formfeed will be sent to the
    printer before printing the first sheet.  +initial-formfeed:off
    suppresses the initial formfeed.  This is the default.

+pause  /oa+

    Pause between printing sheets and wait for keyboard input to
    allow for changing paper.  The page number of the side to be
    printed will be displayed in brackets preceding the prompt.
    When you type <Return>, the next sheet will be printed.  If you
    type <A><Return>, all following sheets will be printed without
    pausing.  If you type <Q><Return>, printing will be stopped.

+xon-xoff  /ox+

    Use XON/XOFF flow control for COM1 to COM4 or use the BIOS for
    LPT1 to LPT4.  Output to COM1 to COM4 will be sent directly to
    the port.  If XON/XOFF protocol is to be used then the output
    file must be given as COM1, COM2, COM3, or COM4.  Output to LPT1
    to LPT4 will be done via the BIOS, not via DOS.  To use the BIOS
    to output to the parallel port, the output file must be given
    as LPT1, LPT2, LPT3, or LPT4.  +xon-xoff will be ignored for
    any other output file (for example, AUX, PRN, file.prn).  If
    +xon-xoff:off is entered or the output is not to COM1 to COM4 or
    LPT1 to LPT4, then output will performed using DOS functions.
    This option is unnecessary under OS/2 and is not supported.


3.11.2 Options for all parameter files but itoh.dot and aiw.dot
---------------------------------------------------------------

+slow  /s+

    Printer slower, but with better quality.  Depending on the param-
    eter file, +slow:on causes dvidot to make two passes per line of
    output (fx80.dot, for instance), to use unidirectional print mode
    (fx80l.dot, for instance), or to tell the printer to use more ink
    (bj300h.dot, for instance).

    When making two passes per line of output, every line will be
    printed twice, the first time printing dots 1, 3, 5, and so
    on and the second time printing dots 2, 4, 6, and so on.  The
    default setting (+slow:off) prints about twice as fast but with
    poorer quality on some antique printers (FX-80, for instance)
    that find it difficult to fire a needle on two consecutive
    positions.


3.11.3 Options for the parameter files itoh.dot and aiw.dot
-----------------------------------------------------------

+form-length  /hf#

    Set the page length.  For page ejects to work properly the page
    length must be set.  If the page length is set to 0 (0in, for ex-
    ample, the default) the length defined by +height is taken as the
    page length.

+slow  /s+

    Slow mode.  By selecting +slow:on printing will be unidirectional
    (itoh.dot sets also incremental print mode); the default,
    +slow:off, sets bidirectional printing (itoh.dot sets also logic
    seek mode).


3.12 Additional options for dvidot when generating graphics files
-----------------------------------------------------------------

dvidot has two principal modes of operations: printing on a dot
matrix printer and creating bitmap files.  The mode is selected by
the parameter file.  This section describes the options applying to
generating graphics files.


3.12.1 Controlling the bitmap file
----------------------------------

+inverse  /oi+

    Inverse output.  Use +inverse:off (default) to display black on
    a white background, use +inverse:on to display white on black
    background.

+minimize  /om+

    Create the smallest picture possible.  The size of the
    rectangular clipping region around the picture will be reduced
    to eliminate (almost) all white space:  the clipping rectangle
    will always be set so that the picture touches the top, bottom
    and left-hand edges but there may be some blank pixels between
    the rightmost point of the picture and the right-hand edge of
    the rectangle to make the width an integral multiple of 8, 16
    or 32 pixels (see parameter file).  Zero and positive values
    of +left-margin and +top-margin are ignored; by setting these
    values negative, however, you can bring the left-hand or top edge
    (or both) of the clipping rectangle inwards to cut off unwanted
    parts of the picture.  The default is +minimize:off: the file
    will contain a picture of height set by +height and width set by
    +width.


3.13 Additional options for dvihplj
-----------------------------------


3.13.1 General options
----------------------

+close  /os#

    Close and reopen the output file after printing # sheets at
    a time.  For instance, this is useful for use with printer
    spoolers.  +close:0 (the default setting) disables this feature,
    that is, the output file will be closed once at the end of the
    print job.  Note: # is given as number of sheets to ensure that
    both the frontside and the backside are printed on the same
    sheet if double-sided printing is in effect (+double-sided:long
    or +double-sided:short).  Prior to closing the output file, the
    printer will be reset.  After reopening the output file, the
    printer will be reinitialized.  This effectively splits the
    output of dvihplj into several print jobs, allowing printing to
    start while more pages are being output.  See also +clear-fonts.

+delete-fonts  /oz+

    Delete temporary printer fonts.  The default is
    +delete-fonts:on.  Use +delete-fonts:off to suppress deletion of
    temporary fonts; don't forget to adjust +memory to reflect the
    memory used by the temporary fonts.

+double-sided:long  +double-sided:short  /d:l  /d:s

    Double-sided printing, the printer (HP LaserJet III D, for
    instance) automatically prints on both sides of the paper.
    +double-sided:long is used for long-edge binding (the sheets are
    bound along the length of the sheet), +double-sided:short is used
    for short-edge binding (the sheets are bound along the width of
    the sheet).  The +copy-file and +copy-sheets options work as
    expected with +double-sided:long and +double-sided:short.

+final-formfeed

    If +final-formfeed:on is active, a formfeed will be sent to the
    printer after printing the last sheet.  This is the default.
    +final-formfeed:off suppresses the final formfeed.  That may be
    resired if the operating system automatically appends a formfeed.

+final-reset  /oe+

    Reset printer after each print job.  This is the default.  You
    can suppress resetting the printer by using +final-reset:off.

+font-offset  /of#

    Set the initial value for font ID numbers.  The default is 0,
    acceptable values are 0 to 32736.  The fonts downloaded by
    dvihplj to the printer will be given numbers from # to #+31.
    This option allows the user to avoid overwriting fonts which
    have already been downloaded which the user does not want
    deleted.  However, dvihplj will delete all temporary fonts unless
    +delete-fonts:off is given.

+initial-formfeed

    If +initial-formfeed is active, a formfeed will be sent to the
    printer before printing the first sheet.  +initial-formfeed:off
    suppresses the initial formfeed.  This is the default.

+initial-reset  /oi+

    Reset printer before starting the print job.  This is the
    default.  You can suppress resetting the printer by using
    +initial-reset:off.

+manual-feed

    Feed paper from manual input.  +manual-feed is a shorthand for
    +source:2.

+source

    Select the paper source.  With +source:0, which is the default
    setting, the selection of the paper source is left to the
    printer, depending on +paper.  Other settings are 1 through 6.
    The meaning of those numbers depend on the printer model; see the
    user's manual of the printer for details.  See also +manual-feed.

+paper

    Select the paper size.  Valid arguments are:

    A3      A3 (297mm x 420mm)

    A4      A4 (210mm x 297mm)

    B5      B5 envelopes (176mm x 250mm)

    C5      C5 envelopes (162mm x 229mm)

    Com-10  Com-10 business envelopes (4.125in x 9.5in)

    DL      DL envelopes (110mm x 220mm)

    Exec    Executive (7.25in x 10.5in)

    Ledger  Ledger (11in x 17in)

    Legal   Legal (8.5in x 14in)

    Letter  Letter (8.5in x 11in)

    Monarch
            Monarch letter envelopes (3.875in x 7.5in)

    The argument is case-independent.  If this option is used without
    argument (+paper -- this is the default), the +width and +height
    options are used for setting the size of the paper.  If this
    option is used with one of the above arguments, the +width and
    +height options are ignored by dvihplj.  Moreover, on the HP
    LaserJet series II and later (or if +set-paper:on is set), this
    option selects the paper tray -- the printer asks you to insert
    another paper supply if the selected paper size is not available.

+set-paper

    If the default value +set-paper:off is active, dvihplj does not
    for all printer models send the paper size selected with +paper
    to the printer.  With +set-paper:on, dvihplj always sends the
    paper size selected with +paper to the printer.  This can be
    useful if you are using a HP DeskJet 540, for instance.

+pause  /oa+

    Pause between printing sheets and wait for keyboard input to
    allow for changing paper.  The page number of the page to be
    printed will be displayed in brackets preceding the prompt.
    When you type <Return>, the next sheet will be printed.  If you
    type <A><Return>, all following sheets will be printed without
    pausing.  If you type <Q><Return>, printing will be stopped.

+printer-resolution  /og#

    Set printing resolution of printer.  The default setting is 0,
    which causes the printing resolution to be chosen according to
    the printer model:

        +printer-model ³ Resolution
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄ
        deskjet        ³ 300
        deskjet500j    ³ 300
        deskjet850     ³ 300
        kyocera        ³ 300
        laserjet       ³ 300
        paintjet       ³ 180
        quietjet       ³ 192
        thinkjet       ³ 192

    You can use +printer-resolution to choose a different
    resolution.  You should also set +resolution when setting
    +printer-resolution.

+xon-xoff  /ox+

    Use XON/XOFF flow control for COM1 to COM4, use the BIOS for out-
    put to LPT1 to LPT4.  See dvidot's +xon-xoff option for details.


3.13.2 Selecting the printer model
----------------------------------

+printer-model  /op*

    Select the printer model.  This option tells dvihplj for which
    printer model to generate output.  The following settings are
    available (additional options are required for settings marked
    (*)):

        +printer-model ³ Printer model
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
        deskjet        ³ HP DeskJet (500, 550, etc.)
        deskjet500j    ³ HP DeskJet 500J (Japanese version)
        deskjet850     ³ HP DeskJet 850
        kyocera        ³ Kyocera F-1010
        laserjet       ³ HP LaserJet+ (and later models)
        paintjet       ³ HP PaintJet (*)
        quietjet       ³ HP QuietJet (*)
        thinkjet       ³ HP ThinkJet (*)

    The default is +printer-model:laserjet.  The argument is
    case-independent.

    For +printer-model:paintjet, you have to set the resolution to
    180 DPI and to use correct fonts, for instance, by using the
    p6l.cnf configuration file.

    For +printer-model:quietjet and +printer-model:thinkjet, you have
    to set the resolution to 192 DPI or 192x96 DPI, respectively, and
    to use correct fonts.


3.13.3 Using additional features of a printer
---------------------------------------------

+compression  /or#

    Set graphics compression mode.  You can set values in the
    range -1 to 2.  The value 0 causes graphics data to be sent
    uncompressed.  The value 1 causes graphics data to be sent either
    uncompressed or run-length encoded, depending on what method
    yields less data.  The value 2 causes graphics data to be sent
    uncompressed or TIFF 4.0 compressed, depending on what method
    yields less data.  The value -1 (default) lets dvihplj choose the
    compression mode automatically based on the printer model:

        +printer-model ³ compression mode
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
        deskjet        ³ 2
        deskjet500j    ³ 2
        deskjet850     ³ 2
        kyocera        ³ 0
        laserjet       ³ 0
        paintjet       ³ 1
        quietjet       ³ 0
        thinkjet       ³ 0

    If your printer model supports compression, you can decrease the
    amount of output data by using +compression:1 or +compression:2.
    The HP LaserJet III, for instance, supports +compression:2.

+download-limit

    Limit the size of download characters.  Character bigger than
    this many bytes of memory (8 pixels are packed in one byte) are
    not downloaded to the printer.  dvihplj uses graphics mode for
    printing big characters.  You might want to use this option to
    save printer memory when printing big characters which are used
    once or rarely.  The default is +download-limit:32767.  You can
    use values between 0 (don't download any character) and 32767.

+draft

    Use +draft:on to print in draft mode (EconoMode) to save toner
    or ink.  This option does not affect the resolution.  Currently,
    only the HP LaserJet 4L, 4ML, 4P and 4MP printers (and newer
    models of the DeskJet) support draft mode.  The default is
    +draft:off.

+fonts-per-side  /ow#

    Maximum number of fonts per output page.  If more than this many
    fonts are required per output page, error message 2502 will be
    issued and the run aborted.  The default is 16.  Newer printers
    support more than 16 fonts per output page; if you are using such
    a printer, you can use set a bigger value for +fonts-per-side
    to avoid error 2502.  You should enter this option when
    using built-in printer fonts.  The maximum value is 32767.
    +fonts-per-side:0 disables both checking the number of fonts per
    page and checking the number of fonts per job.

+job-offset  /oj+

    Job offset.  Some printers can offset sheets sideways in the
    output tray.  +job-offset:on will cause the output position to
    be switched to the alternate offset so that the results of a
    sequence of print jobs can be separated more easily.

+memory  /om#

    Printer memory size.  This sets the available memory on the
    printer in Kbytes: the default is 394.  When dvihplj needs
    more printer memory than specified with the +memory option,
    the print job is aborted with fatal error 2501.  If this value
    is set to 0 then there will be no test for memory overflow.
    If fonts are permanently downloaded then this value must be
    appropriately reduced.  +memory does not affect optimization or
    any other property of the output.  This option will be ignored
    if +printer-model:deskjet, +printer-model:deskjet500j, or
    +printer-model:deskjet850 is set.

    The following example tells dvihplj that there are 1500 Kbytes of
    printer memory available:

          Example:    +mem:1500


3.13.4 Solving compatibility problems
-------------------------------------

+full-page-bitmap  /ob+

    If +full-page-bitmap:on is active, the sides will be printed
    using a full-page bitmap.  If +full-page-bitmap:off is set,
    download fonts will be used.  +full-page-bitmap:on may be
    required if your printer is not sufficiently compatible
    to the LaserJet+.  The options +printer-model:deskjet,
    +printer-model:deskjet500j, and +printer-model:deskjet850 set
    +full-page-bitmap:on.

+clear-fonts  /oc#

    Delete all temporary fonts after every # pages.  This may help
    when there is not enough printer memory for holding all required
    fonts, but requires more time.  Default is 0: don't delete
    fonts.  +clear-fonts:0 may be required if your printer is not
    sufficientlycompatible to the LaserJet+.

+optimize-graphics  /oo+

    Optimize graphics output.  If +optimize-graphics:on is active
    (default), bytes of zeros at the start and end of graphics
    rows and -- if +compression:0 and +printer-model:laserjet or
    +printer-model:kyocera is set -- wide gaps in graphics rows will
    be not transferred.  If +optimize-graphics:off is set, only
    bytes of zeros at the end of graphics rows will be omitted.
    +optimize-graphics:off may be required if your printer is not
    sufficiently compatible to the HP LaserJet+.

+negative-top-offset  /ov+

    Setting +negative-top-offset:off may fix vertical placement
    of characters which don't extend above the base line with
    some printers (Toshiba PageLaser6, for instance).  If
    +negative-top-offset:on (default) is used, the Top Offset parame-
    ter of down load characters whose pixels are entirely below the
    base line is negative.  With +negative-top-offset:off, dvihplj
    will fill the character to the base line to make Top Offset 0.
    This requires more memory.


3.14 An introduction to templates
---------------------------------

The earlier versions of the drivers used $s and $r to insert the
values of the font resolution and the PXL magnification into font
filenames; this facility has now been extended and the drivers use
templates to construct filenames from the parameters they are given,
such as the name and the resolution of a font.  Note that the earlier
$s and $r are no longer valid and must be replaced by @RVr and @Rr
respectively.  The template can be a constant, i.e., the file name
does not depend on any of the parameters, or it can evaluate to
more than one filename which will then be used in sequence.  The
evaluation of a template is called its expansion.

A template which is not constant contains one or more template
characters which are comma (,), dollar sign ($), at sign (@) and
left and right braces ({}).  A template which contains a dollar sign
or a comma may expand to more than one filename.  If these template
characters are to appear as literal characters then they must be
preceded by the at sign (@) -- a literal dollar sign must be written
`@$'.

Multiple expansions are necessary when a font, or other file, can be
in one of several different directories; each expansion is evaluated
and the result is used to search for the file required, if the search
fails, the next part of the template is expanded and the process
continues until the file is found or there are no further expansions.


3.14.1 The simplest example of a template -- a constant template
----------------------------------------------------------------

The template

    dviscr.dlg

which is intended for the +transcript-file option, simply contains
the filename: the expansion does not depend on any parameters and is
just this filename.


3.14.2 A simple example of a template
-------------------------------------

In the template

    @d.dlg

`@d' is replaced by the name of the driver; if this is dvihplj then
this template will expand into `dvihplj.dlg'.  Every driver has this
template as its default setting for the +transcript-file option as
the driver name is known by the time the template is expanded.


3.14.3 Template parameters
--------------------------

These are the template parameters, any of these parameters in a tem-
plate will be replaced by the value given in the table below.

@d      replaced by one of the following driver names: dvihplj,
        dviscr, dvivik, dvipm, dvidot.

@f      replaced by the font name or the graphics filename; this pa-
        rameter is to be used in conjunction with the +font-files and
        +graphics-files options.

@i      replaced by the name of the DVI file.

@p      magstep: 0 to 9, h for magstephalf or u for unknown -- for
        use with the +font-files option.

@m      METAFONT mode -- see the description of the +metafont-mode
        option.

@b      base resolution of the fonts in DPI -- see the description of
        the +font-resolution option.

@r      font resolution in DPI, a decimal fraction -- for use with
        the +font-files option.

@g      magnification, a decimal fraction -- for use with the
        +font-files option, for example, 1.2

@u      a number to make the file name unique -- for use with the
        +mfjob-file option only

These parameters can be modified by inserting one or more letters
between the `@' and the parameter letter.  For instance, the earlier
$s, which was replaced by the PXL magnification of a font, must
now be written @RVr.  The modifiers for the various parameters are
described below.


3.14.4 Forming multiple expansions with a list
----------------------------------------------

Many of the driver options require a list of files, for instance, the
+font-libraries option takes a list of font library filenames.  The
simplest way to do this is by entering a list of names separated by
commas but this is not always very convenient as it requires a lot of
typing and the length of a template is limited to 127 characters.

Because of this limitation, this example does not contain the usual
set of font libraries:

    +font-lib:c:\texfonts\fx_base.fli,c:\texfonts\fx_more.fli

Note that earlier version of the drivers used semicolons as
separators, in this version the names are separated by commas.
Spaces are not allowed in templates as they are used to separate op-
tions in the command line.


3.14.5 Forming multiple expansions with alternatives
----------------------------------------------------

It is clear from the preceding example that the expansions have quite
a lot of text in common.  Templates therefore allow common text to
be factored out with the differing parts presented as a series of
alternatives enclosed in braces.  The example above may be expressed
in this way as follows:

    +font-libraries:c:\texfonts\fx_{base,more}.fli

In expanding this template, the alternatives are selected in order
starting with the first after the opening brace.  The template is
evaluated with this choice and the result used by the driver; if
the driver requests another candidate, the template is evaluated a
second time using the second alternative which (in this example)
lies between the first and second commas.  A third expansion would
be constructed using the third alternative which appears after the
second comma and before the closing brace.

Any number of alternatives may appear between the opening and closing
braces.  The text of an alternative may also be null as in `{}' or
`{,a}': in the first case the expansion is empty, in the second case
the first choice is empty, the second consisting only of `a'.  It
it also possible to have only one choice as in {abc} which always
evaluates as `abc' -- the braces in this case are not needed.
Naturally the choices need not have the same length as, for example,
in:

    +font-libraries:c:\texfonts\lj_{base,m1,m2,m3}.fli

A simple list of filenames separated by commas is a special case
of a set of alternatives.  The driver automatically encloses a tem-
plate in opening and closing braces so the list appears as a list of
alternatives.  If only one filename appears then it is a constant
choice as shown above in `{abc}'.


3.14.6 Multiple sets of alternatives
------------------------------------

When searching for font files it is useful to be able to construct a
pattern with more than one set of alternatives in it.  With templates
you can not only do this but you can also nest alternatives.  The
expansion of such a template consists of all possible combinations in
lexicographical order, that is, with the rightmost alternative in the
template changing most rapidly.

An example will best clarify this:  the template

    {1,2}{1,a{1,2}}

will give the following sequence of expansions

    11
    1a1
    1a2
    21
    2a1
    2a2

The template

    {0,1,2,3,4,5,6,7,8,9}{0,1,2,3,4,5,6,7,8,9}{0,1,2,3,4,5,6,7,8,9}

will expand into all the three digit numbers from 000 to 999 in in-
creasing numerical order.

An example of this facility in use:

    +font-files:{c:\texfonts\,d:\myfonts\,}@f{.pk,.pxl}

Note the empty alternative in the first pair of braces, this will
have the effect of searching the current directory for the fonts if
they are not found in either c:\texfonts or d:\myfonts.  This may
also be written

    +font-files:{c:\texfonts\,d:\myfonts\,.}@f{.pk,.pxl}

This is not the best way of handling alternative directories, in the
next section the advantages of keeping directory names in environment
variables rather than explicitly in options will be pointed out.


3.14.7 Environment variables
----------------------------

The names of directories are more conveniently kept in environment
variables so that, when the disk is reorganized it is not necessary
to edit all the configuration files.  To further support this use of
environment variables, they may also appear in templates.  The name
of the variable is sandwiched between a dollar sign ($) and a colon
(:) as in $DVIDRVFONTS: for instance.  The name of an environment
variable to be used in a template may not contain any of the special
template characters, that is, @ { , or } (at sign, comma and opening
and closing braces) -- this may be changed in a future release as
@d would be very useful in this regard, $@d: would expand into the
driver's special environment variable (DVIFX, DVILQL etc).  The envi-
ronment variable is treated as if it was an alternative enclosed in
braces, the list of directories the variable contains (here separated
by semicolons, not commas) are entered into the expansion one at a
time in the order they appear in the variable.  If a directory name
in the environment variable does not end in `:', `/' or `\' then a
`\' is automatically appended.  Empty directory positions in the
list, for instance the two in

    SET PATH=C:\DOS;;\D:\BIN;

will be ignored -- a template containing $PATH: set as above would
expand in exactly the same way if the SET command was

    SET PATH=C:\DOS;\D:\BIN

The contents of the environment variable may include template
parameters (@b and @r are likely candidates) but alternatives are not
allowed.

Please note that $EMTEX: is a special case, to be described below.

An example of the use of an environment variable in a template:

    +response-files:$PATH:@f

The response file @f will be searched for in all the directories
in the PATH variable -- note that `\' will be appended wherever
necessary.  If the file should be sought first in the current direc-
tory, the template should be extended to

    +response-files:{,$PATH:}@f

which is the default setting.  If PATH has the value `c:\dos;;\;f:'
and the response file name (@f) is `test.res' then the template will
expand to the following sequence of pathnames:

    test.res
    c:\dos\test.res
    \test.res
    f:test.res

that is, {,$PATH:}@f is evaluated in the same way as
{,c:\dos,,\,f:}@f, the construction $PATH: being replaced by the
value of PATH.

Appending ! or !! to a directory name in the environment variable
enables subdirectory search.  If ! is appended, that directory and
one level of subdirectories are searched; if !! is appended, that
directory and all levels of subdirectories are searched.  Directories
are visited before their subdirectories; no other search order is
defined.


3.14.8 The emTeX directory ($EMTEX:)
------------------------------------

EMTEX is a pseudo environment variable, expanding to the path name of
the emTeX directory.  As with real environment variables, a backslash
is added if required.  If the EMTEXDIR environment variable is set,
$EMTEX: is treated like $EMTEXDIR:.  Otherwise, the default value
`\emtex' is used.  That is, $EMTEX: can be used even if EMTEXDIR is
not set.  Therefore, it is recommended to use $EMTEX: instead of
$EMTEXDIR: in templates.


3.14.9 Template parameter modifiers
-----------------------------------

Template parameters may have their expansion modified by inserting
one or more characters from the set shown below between the @ and the
parameter letter.  The modifiers are:

0-99 _

    Padding a parameter out to a given width with `0' or `_'.
    A number from 0 to 99 will cause the parameter to be filled
    from the left with `0' or `_' -- the number of positions to be
    filled is given by the number's value.  A number appearing with
    a numeric parameter will fill with zeros but appearing with
    a non-numeric parameter will fill with underscores.  Use the
    underscore modifier to fill a numeric parameter with underscores
    instead of zeros.

    Examples:

        @r    ³ @4r   ³ @4_r      @f       ³ @5f
        ÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ    ÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ
        1     ³ 0001  ³ ___1      a        ³ ____a
        300   ³ 0300  ³ _300      abc      ³ __abc
        20000 ³ 20000 ³ 20000     abcdefgh ³ abcdefgh

F R T

    rounding and truncating real numbers

    F       taking the fractional part of the number (may be empty)

    R       rounding the number to get the integer part

    T       truncating the number to get the integer part

.0-99

    Decimals.  The number will be rounded to this many decimals.
    Note: The period must not be used immediately following the @, as
    `@.' has a special meaning.  Specify a field width instead, for
    instance `@0.2r'.

    Examples:

        @r     ³ @0.3r   ³ @0.2r  ³ @0.1r ³ @0.0r ³ @7.1r   ³ @R.3r
        ÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ
        300.75 ³ 300.750 ³ 300.75 ³ 300.8 ³ 301   ³ 00300.8 ³ 301.000
        300.74 ³ 300.740 ³ 300.74 ³ 300.7 ³ 301   ³ 00300.7 ³ 301.000
        300    ³ 300.000 ³ 300.00 ³ 300.0 ³ 300   ³ 00300.0 ³ 300.000

P B E N

    splitting path and file names A pathname consists of three parts:
    the directory (including drive), the base name and the extension;
    the base name and the extension are separated by a dot.  For exam-
    ple:

        Pathname      ³ Directory ³ Basename ³ Extension
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄ
        d:\test\a.dvi ³ d:\test\  ³ a        ³ dvi
        xxx           ³           ³ xxx      ³
        xxx.zzz       ³           ³ xxx      ³ zzz
        c:xxx         ³  c:       ³ xxx      ³
        a.b.c         ³           ³ a.b      ³ c

    Without a modifier, @f and @i will be replaced by the full
    pathname of the file; using a modifier allows you to replace or
    omit parts of the name.  The modifiers below will cause the full
    pathname to be replaced by:

    P       the directory portion of the pathname

    B       the basename

    E       a dot followed by the extension

    N       the basename, a dot (only if there is an extension) and
            the extension.

    More than one of these modifiers can be used with a single param-
    eter, in which case they will be applied in the order P, B, E --
    @BEf will be expanded as if written @Bf@Ef.  If none of these
    modifiers appear, the parameter will be replaced by the unchanged
    pathname (PBE will end with a dot if there is no extension).

    If an @f or @Pf parameter has a non-empty a directory part when
    evaluated and it is not at the start of the expansion, that
    is, preceded by at least one character, then that expansion
    is silently ignored.  This is done to avoid undesirable or
    nonsensical expansions which would otherwise arise from templates
    such as

        {c:\fonts\,}@f

    In this example, if @f expands to \ec\emr10 (non-empty directory
    part) then the expansion

        c:\fonts\\ec\emr10

    will be discarded and only the expansion

        \ec\emr10

    will be used.  If, however, @f expands to emr10 (filename only)
    then the two expansions

        c:\fonts\emr10
        emr10

    will be used.  Examples:

        @f    ³ @Pf ³ @Bf ³ @Ef ³ @BEf ³ @Nf
        ÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄ
        b     ³     ³ b   ³ .   ³ b.   ³ b
        b.e   ³     ³ b   ³ .e  ³ b.e  ³ b.e
        p\b   ³ p\  ³ b   ³ .   ³ b.   ³ b
        p\b.e ³ p\  ³ b   ³ .e  ³ b.e  ³ b.e

M V

    Multiplication by a constant.  M multiplies a numeric parameter
    by 1000 and V multiplies by 5.  This allows the generation of
    directory or file names which depend on the font magnification as
    PXL font names do, for instance

        @r  ³ pxl@RVr
        ÄÄÄÄÅÄÄÄÄÄÄÄÄ
        300 ³ pxl1500

    or names which depend in the magnification:

        @g   ³ @Mg
        ÄÄÄÄÄÅÄÄÄÄÄ
        1.44 ³ 1440

    If more than one M or V modifier appears on the same parameter,
    all but the rightmost one will be ignored.

    The result is undefined on overflow (product greater than
    65535.99998).

X Y

    horizontal or vertical value.  The resolution can be different
    on the horizontal and vertical axes, these modifiers allow the
    correct value to be selected with the @b or @r parameters.  @Xb
    or just @b will select the value set by the +font-resolution-x
    option while @Yb will select that set by +font-resolution-y.  If
    more than one X or Y modifier it used with the same parameter,
    all but the rightmost one will be ignored.


3.14.10 Default extension
-------------------------

To add an extension to a file name, unless the file name already has
an extension, you can use `@.'.  For instance,

    @f@.{msp,pcx,bmp}

creates the following file names:

    filename     ³ filename.grf
    ÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄ
    filename.msp ³ filename.grf
    filename.pcx ³
    filename.bmp ³

`@.' works this way:

- If the expansion produced so far doesn't contain a `.' following
  the last `:', `\' or `/' (or if the expansion contains a `.'
  but not any of those characters), the file name doesn't have an
  extension.  In this case, `@.'  will be replaced by a period and
  expansion continues (with the extension).

- If the file name has an extension (each `.' (if any) is followed
  by `:', `\' or `/'), expansion stops at `@.' (omitting the default
  extension).

Currently, `@.' does not work inside {...}.


3.14.11 Summary
---------------

@[0-99][_][FRT][PBEN][MV][XY](dfipmbrsg)


    0-99    pad out with 0 (numbers) or _ (other parameters)

    _       pad out with _

    .0-99   decimals (@g and @r)

    F       fractional part

    R       integer part (round)

    T       integer part (truncate)

    P       path: directory part

    B       base name

    E       extension

    N       as BE but no dot if there is no extension

    M       multiply by 1000

    V       multiply by 5

    X       select horizontal value (default, if Y does not appear)

    Y       select vertical value

    d       driver name (string)

    f       font or picture name (string)

    i       DVI filename (string)

    p       magstep (0..9, h, u=unknown) (string)

    m       METAFONT mode (string)

    b       basic font resolution (fraction)

    r       font resolution in DPI (fraction)

    g       magnification (fraction)

    u       number to make file name unique, for +mfjob-file (integer)

{a1,a2,a3}

    alternatives

$env:

    environment variables

@@ @, @{ @} @$

    special characters in templates

@.

    default extension


3.14.12 Further examples
------------------------

The examples show some uses of @g.

    @g  ³ mag@RMg ³ mag@9.3_g
    ÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄ
    1.2 ³ mag1200 ³ mag____1.200


4 Managing fonts
================

The dvidrv drivers will work with the following font file types:

    Extension  ³  ID  ³ Description
    ÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
    PXL        ³ 1001 ³ (32-bit words)
    PXL        ³ 1002 ³ (8-bit words)
    PK         ³   89 ³ (packed)

The font files do not have to have one of these extensions as their
format is determined by their contents.  PK font files with an ID of
87 can NOT be used!

The PXL file formats are obsolescent, you should use PK files instead
of PXL files.

In addition font libraries -- a dvidrv feature -- can be used.
These contain several font files saving disk space and processing
time.  By gathering font files into libraries the number of files in
directories is reduced.  Disadvantages are the size of the resulting
libraries and the amount of time spent in updating fonts.  For more
information see the fontlib documentation.


4.1 Specifying font size (resolution)
-------------------------------------

You may need to specify a font size when the driver can't find a font
or when you are creating a font substitution file.  The font size
is given in dots per inch (DPI) and, for TeX magsteps, will have
decimals after the point.  To avoid the calculation and entry of long
decimal numbers, there is a more convenient method of specifying
magnifications: just append a colon and the magnification step (0
to 9, or h for 0.5) to the font size.  For instance, 100:3 is an
abbreviation for 172.8 (100 * 1.2 ^ 3) and 300:h will be converted
to 328.63353.  You can also write only the colon followed by the
magnification step without an explicit font size.  In this case,
the font resolution set with the +font-resolution option will be
magnified.  This is especially convenient in font substitution files
to specify a font size independent of the device (and its resolution).


4.2 Font substitution file format
---------------------------------

A font substitution file gives a list of fonts which can be used
to replace those called for in a DVI file: the names of the font
substitution files can be set with the +font-subst-files option
though the drivers will run without one.  A font substitution file
can contain comments which are lines starting with `%'.


4.2.1 Substitution with and without batch mode
----------------------------------------------

A font substitution file has two parts only one of which is
required.  The first replaces ALL matching fonts while the second
describes what is to be done when a font file cannot be found while
+batch-mode is active.  The two parts are separated by the line

    $b

If the font substitution file contains the first part only, `$b' can
be omitted.

ALL the rules in the first part are applied one after the other with
the result of one rule being passed on to the next one.  Rules which
do not match remain unused.

The second part only has effect if +batch-mode is active and then
only when a font cannot be found.  The substitutions in this part are
applied in turn to the original font name and size with the result
of one substitution not being carried forward to the next.  After
each trial substitution the resulting font name and size are searched
for and the process ends when the search succeeds.  If the search is
unsuccessful then the next rule is tried; if all rules fail then the
program ends with an error message.


4.2.2 Rule lines
----------------

Each line of a font substitution file contain one substitution rule
if it isn't a comment line or the line `$b': The font file name or
the size (or both) appear to the left of `->' while the name or the
size to be substituted appears on the right; this may be further
followed by an option.  To use built-in printer fonts, `=>' is used
instead of `->', see below for details.  You can choose from one of
the following formats:

    font -> font [option] [comment]
    size -> size [option] [comment]
    font size -> font size [option] [comment]

Font names may contain special characters, see below.  The size is
specified in dots per inch (DPI); you can use a magnification step
using preceded by a colon, for instance, `:2' or `300:1'.  The charac-
ter `*' stands for an arbitrary size if used to the left of `->'.  To
the right of `->', `*' stands for the size of the original font.


4.2.3 Options in font substitution rules
----------------------------------------

At most one of the following options can be used for each
substitution rule:

/b      All characters of the font will be replaced by black
        filled rectangles.  If there's no font file, a TFM file is
        sufficient.

/r      All characters of the font will be replaced by black
        rectangle outlines.  If there's no font file, a TFM file is
        sufficient.  dvidot and dvihplj treat /r like /b and print
        black filled rectangles instead.

/w      The font is made invisible, i.e., a font file is still
        required (a TFM file is sufficient) but the characters of the
        font will be replaced by white space.  This feature can be
        used for the invisible SliTeX fonts.

/d      All characters from the font are discarded entirely, there
        won't be white space for the characters.  This results in
        wrong positions of other objects.  Therefore, warning message
        1211 will be displayed.  No font file is required.

Rules which don't include an option don't change the mode set by
options of rules which matched previously.  That is, you cannot put a
font back into the default mode (printing characters) after applying
an option.


4.2.4 Matching font names
-------------------------

Three special characters can be used in font names: `*' must be given
at the end of a font name and causes the remaining characters of the
name to be ignored.  `*' in the replacement name is replaced with the
characters that were matched by `*' in the original font name.  `@'
matches (in the original font name) any single character.  You cannot
use `@' in the replacement name.  `?' also matches (in the original
font name) any single character.  In the replacement font name, `?'
is replaced by the character matched by the corresponding `?' in the
original font name (the replacement name must contain the same number
of question marks as the original name).  Note that while `@' and `?'
may have name characters following them, `*' may only appear as the
last character.  Here is a concocted example which shows the effect
of each character:

    aaa?bb@cc?dd* -> x?y?z*

This rule will replace the font name `aaa1bb2cc3dd456' by
`x1y3z456'.  This does NOT match the font name `aaabb2cc3dd456'.


4.2.5 Using built-in printer fonts
----------------------------------

dvihplj supports using built-in printer fonts.  A font substitution
file is used for mapping TeX fonts to built-in fonts.  To map a TeX
font to a built-in font, a different type of rule line is used:

    font [size] => pcl: <selection>

Following the `pcl:' keyword, the PCL commands to select the built-in
font are listed, separated by blanks.  The `Esc (' or `Esc )' prefix
used in font selection commands must be omitted.

You can use `*' in place of a specific size on the left hand side of
the `=> pcl:' part of the rule.  If `*' is used for the size, it can
also be used in a selection value.  In this case, the numeric part of
the selection value will be multiplied by the magnification of the
font.  Example:

    trr10u * => pcl: 10U s1P s*10V s0S s0B s5T

This rule causes dvihplj to replace all occurrences of the
font `trr10u' with the built-in font that is selected with
`<ESC>(10U<ESC>(s1p??v0s0b5T'.  The height of the font (shown as ??)
is replaced by 10 times the magnification of `trr10u' in the DVI
file.  This makes sense for scalable fonts only.

Note that a TFM file is required for each built-in font.  Built-in
printer fonts can be used with +transformation:0 only.  For the
HP LaserJet III and later models (such as the HP LaserJet 4),
+transformation:0 through +transformation:3 are supported.
+full-page-bitmap:on also disables built-in printer fonts.

If the TFM file contains parameters for selection of a PCL font,
those parameters are used first.  Then, the font selection commands
from the font substitution file are used.

dvihplj can use built-in fonts without a font substitution file if
the TFM files contain PCL font selection information.


4.2.6 Example
-------------

This example file shows some applications of font substitution files:

    %
    % Example font substitution file
    %
    am* -> cm*               % replace am fonts by cm fonts
    longfontname -> lfn      % change name
    305 -> 300               % change size
    600 -> 300:4             % change size
    cmr12 :0 -> cmr10 :1     % cmr12 scaled 1000 -> cmr10 scaled 1200
    i* -> * /w               % invisible SliTeX fonts
    fancy -> fancy /b        % replace characters by rectangles
    dummy -> dummy /d        % discard characters
    
    $b                       % rules for +batch-mode are following
    
    * * -> * :0              % keep name, size  := +font-resolution
    * * -> cmr10 :0          % name := cmr10, size := +font-resolution
    * * -> * * /r            % replace by rectangles, call MFjob


4.3 Font search rules
---------------------

1.  The font size is replaced by the closest available size,
    according to +font-size-tolerance and +font-sizes.  The font
    name and size are converted according to the rules in the first
    part of the font substitution file -- ALL rules are applied one
    after the other.  If the font size has been changed by the font
    substitution process, it will again be replaced by the closest
    available size.

2.  If +change-mode is active, you have a chance to change the name
    or size of the font, to enter a different font name or to enter a
    file name.

3.  If the /d option is set for the font, no font will be sought; all
    characters of the font will be omitted.

4.  The font is sought according to the values set by the
    +virtual-fonts, +font-libraries and +font-files options.  If a
    font is not found and the /b, /r or /w option is set for the
    font, then a TFM file is sought.  If a font is not found, dvihplj
    tries to load a TFM file for a built-in font.  The TFM file must
    include information for PCL font selection.

5.  If +batch-mode is active and a font substitution file has a
    second part (after `$b'), the name/size resulting from (1) above
    is converted using one of the rules, the size replaced by the
    closest size according to +font-size-tolerance and +font-sizes
    and this name and size used for a search according to the values
    set by the +virtual-fonts, +font-libraries and +font-files op-
    tions.  If /b, /r or /w is set for the font, additionally a TFM
    file will be sought.  All this is done for each rule in turn.

6.  The font is marked for generation by MFjob and METAFONT.

7.  If batch mode is active (+batch-mode option) and there is no font
    substitution file with a second part, the following rules will be
    used instead following the procedure in (5) above:

        * * -> * * /r
        * * -> * * /d

8.  If batch mode is active and the font is still not found, the
    driver stops with a fatal error message.  This can only happen if
    you have changed the rules for +batch-mode, as the last default
    rule uses /d.

9.  If the font is not found, the user is asked for another font
    name, size or file name -- see below.

If the search fails and batch mode is not active (+batch-mode is the
default), the user is asked for help, displaying the font name and
the size of the form

    font<xxxx>

where xxxx is the font size (DPI).  Replacing the size with
the closest available font size according to the settings of
+font-size-tolerance and +font-sizes has already taken place.

You should then enter a font name, a font size or a file name.  More-
over, you can use one of the options for replacing characters with
rectangles or white space or for omitting characters.  Moreover, you
can activate +batch-mode, +change-mode and +interactive-mode.  You
can enter multiple values in one line, the values must be separated
by blanks.  After reading the values given in a line of input, the
font will be searched again using the changed values.  If the line
ends with `&', the search after reading this line will be suppressed.

The following values can be entered:

name

    choose a new font name.  `name' must not contain the characters
    `\', `/', `.', and `:'

size

    choose a new size, (new xxxx value of `font<xxxx>').  The new
    size will not be replaced with the closest available size.
    Examples:

    300     300 DPI

    :2      scaled 1440  (1.44 * +font-resolution)

    204:h   204 DPI magnified 1.2^0.5 (= 233.47081)

    See `Specifying font size (resolution)'

file_name

    choose a complete file name (the input contains one of the
    characters `\', `/', `.', or `:').  The driver will try to
    read this file (ignoring +virtual-fonts, +font-libraries and
    +font-files).  Therefore, you should enter the complete path
    name, including the extension

empty_line

    search.  If you don't want to change a value when using
    +change-mode, just hit the return key

+

    multiply the size by 1.2

-

    divide the size by 1.2

/b

    replace all the characters in the font by a black block.  A font
    file is still required, a TFM file is sufficient

/r

    replace all the characters in the font by a rectangle outline.  A
    font file is still required, a TFM file is sufficient.  dvihplj
    and dvidot cannot print rectangle outlines, these drivers will
    treat /r like /b

/w

    make all the characters in the font invisible.  A font file is
    still needed but the characters therein are not printed.  A TFM
    file is sufficient.  This is useful in analyzing unusual effects

/d

    all characters from the font are discarded entirely, there
    won't be white space for the characters.  This results in wrong
    positions of other objects.  Therefore, warning message 1211 will
    be displayed.  No font file is required

$a

    apply +batch-mode to the current font.  If you have changed the
    name or size of the font, the changes will be ignored.  The
    remaining values on the input line are ignored.  +batch-mode or
    +interactive-mode will be used for the next font, depending on
    the current mode.  If you want to apply +batch-mode to all remain-
    ing fonts, use `$b'

$b

    activate +batch-mode for this and all remaining fonts.  If you
    have changed the name or size of the font, the changes will be
    ignored.  As no further questions will be asked, you won't be
    able to turn off +batch-mode

$c

    activate +change-mode for the next and all remaining fonts

$i

    activate +interactive-mode.  If +change-mode was active, you
    won't be asked before the next (and all remaining fonts) will be
    sought

Examples:

cmr10 :1

    use cmr10 scaled 1200

- -

    decrease size by factor 1.44

d:\myfonts\xyzzy.pk

    use this font file

cmr10 300 /r

    use rectangles for cmr10.tfm at 300 DPI

$b

    activate +batch-mode

+ &

    Increase size by factor 1.2, ask again

If +interactive-mode is active, all missing fonts are marked for gen-
erating with MFjob and METAFONT, even if you have entered a replace-
ment font.  The original, missing font will be generated.  Your input
doesn't influence which fonts will generated in which sizes.

If +change-mode is active, missing fonts will not be marked for gener-
ating with MFjob and METAFONT.


4.4 Generating missing fonts automatically with MFjob and METAFONT
------------------------------------------------------------------

Missing fonts can be generated in the required magnifications from
their METAFONT sources.  The following command line options are
required:

+batch-mode

    Automatically replace missing fonts.  You can use
    +interactive-mode but then you will be prompted for a replacement
    font for each missing font.  If +change-mode is active, missing
    fonts will not be generated automatically.  The default setting
    is +batch-mode

+metafont-mode

    METAFONT mode for the output device.  This option is set in the
    configuration files that come with the drivers

+mfjob-file

    Name of the MFjob file.  Under DOS, this option is set by the
    dvidrv.exe program.  Under OS/2, the default value can be used

If these options are correctly set -- and if there are fonts missing
-- the driver will create a file (with the name specified by
+mfjob-file) which will contain commands for MFjob (version 1.1m or
later) which are required for generating the missing fonts.  Then,
the driver will ask the following question (unless +ask-mfjob:off is
set):

    Warning 1209: do you want to call MFjob to generate # missing fonts now?
    Type Y, N, or ?:

If you type N, computing (printing or output to a file or to the
screen) will continue -- but with replaced fonts.  If the MFjob job
file isn't deleted by dvidrv (or your batch file), you can generate
the missing fonts by calling MFjob after printing (not recommended)
or viewing the DVI file.

If you type Y (or if +ask-mfjob:off is set), the action taken by the
driver depends on the operating system and on the +call-mfjob option:
Under DOS (or if +call-mfjob:off is set under OS/2), the driver will
stop with return code 8 (which can be checked with IF ERRORLEVEL).
If the driver was started by dvidrv, MFjob will be called by dvidrv,
then the driver again.  If +call-mfjob:on (the default value) is set
under OS/2, the driver directly calls MFjob, deletes the MFjob file
and reloads the DVI file.

If you type ?, the driver displays a list of the fonts to be gener-
ated.  The list includes names and magnifications of the fonts.

The MFjob job file will look like this:

    input [dvidrv];
    {
    driver=dvidot;
    mode=lqlores[180 180];
    output=pk[$DVIDRVFONTS:pixel.p6l\@Rrdpi\@f{.pk,.pxl}];
    {font=cmr10; mag=0.5;}
    {font=cmbx10; mag=0.5;}
    }

Here's a short explanation:

input [dvidrv]

    insert declarations from dvidrv.mfj

driver=

    name of the driver, used for replacing @d

mode=

    mode and resolution (set with +metafont-mode and +font-resolution)

output=

    path for output files (set with +font-files)

font=

    name of the font

mag=

    magnification of the font

Keep in mind that MFjob will use only the FIRST expansion of the
template given in the output= declaration.  In the example above, the
font files cmr10.pk and cmbx10.pk will be created in the FIRST direc-
tory listed in the DVIDRVFONTS environment variable, under directory
pixel.p6l\#dpi (# will be replaced by 90).  The FIRST extension from
the list of alternatives will be used.

You should ensure that the first directory set by +font-files is
writable.  You can create an separate directory for automatically
generated fonts -- this directory should be listed first.

Under DOS, it is recommended to use the program `dvidrv', which takes
care of setting +mfjob-file to a unique file name (of a non-existent
file) to prevent problems with multiple users (network!)  working in
the same directory.  dvidrv will also call MFjob and -- after generat-
ing the fonts -- the driver again.

dvidrv will create the temporary MFjob file in the directory given
by the TMP environment variable (use SET TMP=F:\, for instance).  If
TMP isn't set, the root directory of the current drive will be used,
which must be writable.

As an alternative to dvidrv, you can use the following batch file,
but it doesn't work when running multiple drivers concurrently in the
same directory:

    @echo off
    :loop
    dviscr @lj /fl:-1 %1 %2 %3 %4 %5 %6 %7 %8 %9 /pj:dvihplj.mfj
    if errorlevel 9 goto end
    if not errorlevel 8 goto end
    mfjob dvihplj.mfj
    if not errorlevel 1 goto loop
    :end

The following options also affect automatic generation of missing
fonts:

+ask-mfjob

    Select whether to ask or not for confirmation before running
    MFjob.

+call-mfjob

    Under OS/2, select whether to run MFjob directly or to stop with
    a special return code.  This option is ignored under DOS.


4.5 Using built-in printer fonts
--------------------------------

dvihplj can use built-in fonts unless the entire page is printed
as bitmap (+full-page-bitmap).  The simplest way to use built-in
fonts is to use TFM files which include information for selecting
PCL fonts.  When such TFM files are available, dvihplj will
automatically use these fonts.  Suitable TFM files are available
for anonymous ftp on CTAN hosts (such as ftp.shsu.edu) in directory
/texarchive/fonts/ljmetrics.

Moreover, you can select built-in fonts by adding special rules to
the font substitution file.


5 Using dviscr and dvivik
=========================


5.1 Keyboard functions for dviscr and dvivik
--------------------------------------------

Note that it is impossible to go outside the `sheet' defined by
+width and +height.  You can use the following keys, upper case and
lower case isn't distinguished:

<Ctrl>+<C>  <Q>

    exit from the program

<left arrow>

    move the window half the screen width to the left (for smaller
    movements, see <F> and <C>)

<right arrow>

    move the window half the screen width to the right (for smaller
    movements, see <F> and <C>)

<up arrow>

    move the window half the screen height upwards (for smaller
    movements, see <F> and <C>)

<down arrow>

    move the window half the screen height downwards (for smaller
    movements, see <F> and <C>)

<4>

    move the window to the left by the screen width

<6>

    move the window to the right by the screen width

<8>

    move the window upwards by the screen height

<2>   <spacebar>

    move the window downwards by the screen height

<Home>

    move the window to the initial position (chosen with +home-x and
    +home-y options or <H>)

<7>

    move the window to the top left-hand corner of the page

<End>

    move the window to the bottom left-hand corner of the page
    (+home-x option or <H>)

<1>

    move the window to the bottom left-hand corner of the page

<Ctrl>+<left arrow>

    move the window to the left margin

<Ctrl>+<right arrow>

    move the window to the right margin

<PageUp>   <9>   <F7>

    to the previous page

<PageDn>   <3>   <F8>

    to the next page

<Ctrl>+<PageUp>

    to the first page

<Ctrl>+<PageDn>

    to the last page

<I>

    reversed image toggle

<D>

    refresh the screen image

<H>

    make the current position the home position (see +home-x,
    +home-y, <Home> and <End>)

<F>

    this reduces the window movement caused by the arrow keys; it has
    6 steps

<C>

    this increases the window movement caused by the arrow keys; it
    has 6 steps

<G>

    go to one of the pages selected for display.  Enter a number from
    1 to the number of selected pages -- this page will then be dis-
    played.

<O>

    return to the previously displayed page -- to be used after a
    <G>, <P>, <S>, <Ctrl>+<PageUp> or <Ctrl>+<PageDn> command.  The
    driver holds up to the last 20 pages displayed.  The page is dis-
    played so that the point marked by the ruler or the middle of the
    page appears in the same position on the screen.

<P>

    display a page with a given page number, the page number must be
    entered.  The page with this page number is first sought starting
    from the current page going towards the end of the file, if it
    isn't found then the search restarts at the beginning of the
    file.  Page numbers can contain *, for example, 1.*.5

<R>

    toggle the ruler display

<Ctrl>+<R>

    toggle the scale on the ruler

<S>

    search for text: the search starts at the beginning of the
    current page (or the point at which the search last stopped).
    Pages are then sought starting at the current page and moving
    towards the end of file.  If this fails then the search starts
    again at the beginning of the file.  The search can be terminated
    by pressing the Esc key.  If no text is entered, the text from
    the last search is used again.  The search is case sensitive,
    hyphens and spaces are ignored.  The text can also include
    accented characters.  If the text contains an illegal character,
    for instance, `\' can't appear in it, the driver beeps.  The
    ruler is placed on the reference point of the first character of
    the text.

<W>

    toggle the effect of the arrow keys -- either the window or the
    ruler (if present) is moved.  After enabling the ruler with <R>,
    the arrow keys move the ruler.  This function affects the four
    arrow keys, <Ctrl>+<left arrow>, <Ctrl>+<right arrow>, <Home> and
    <End>.  The other keys continue to move the window.  The effect
    of <F> and <C> is also changed, altering the rate at which the
    ruler is moved around independently of the setting for the window
    movement.

<U>   <Ctrl>+<U>

    change the dimension unit: <U> moves forward through the usual
    list of 10, <Ctrl>+<U> moves backward.  These dimension units
    are used in the status line and the ruler display.  See also
    +ruler-unit.

<+>   <->

    change the gray scale display or scaling (zoom).  If possible,
    a gray scale is used, otherwise scaling.  The relation between
    the values set by +zoom-x, +zoom-y or +scaling-x, +scaling-y
    is preserved.  This means that a scaling of +scaling-x:7
    +scaling-y:8 cannot be changed.  <+> increases the size of the
    picture, <-> reduces it.

<Alt>+<G>   <Alt>+<S>

    change the gray scale setting or scaling (zoom).  One or two
    digits in the range 1 to 8 can be entered; these are taken to
    be the new factors for the gray scale (<Alt>+<G>) or scaling
    (<Alt>+<S>).  If only one digit is given then it is taken as both
    the X and Y value (like +zoom and +scaling).  If two digits are
    entered then these are used as the X and Y factors (like +zoom-x
    and +zoom-y or +scaling-x and +scaling-y).

<T>

    dviscr and dvivik can change the transformation dynamically
    by following <T> by a digit from 0 to 7 and <Enter>.
    This is, however, not possible if +font-resolution-x and
    +font-resolution-y were used to set different values and you wish
    to switch between transformations 0, 2, 5 or 7 and 1, 3, 4 or
    6.  Moreover, you cannot change the transformation when making
    a book, that is, when +section-count or +section-size has a
    non-zero value.

<K>

    this toggles the coordinates used for the arrow keys between
    screen coordinates and transformed coordinates (if the display
    is rotated (do this on your own risk)).  When <K> is pressed the
    arrow keys are transformed, pressing it again returns to the
    initial state.

For functions <+>, <->, <Alt>+<G>, <Alt>+<S>, and <T> the midpoint
of the screen (or, if the ruler is enabled, the point marked by the
ruler) is kept in the same position on the screen.

Rotations are also made around this point, reflections put this point
on the reflection axis and the size is changed with this point at the
centre.  If this causes the window to fall outside the page then the
window is moved as necessary so that it lies wholly within the page
(if possible).


5.2 Entering numbers
--------------------

Numbers are displayed in the status line, if it is enabled.  Errors
can be corrected with the backspace key or left arrow key, Esc ends
an incorrect entry, Enter accepts the number.

If no status line (see +status-line:off) is displayed, numbers must
be entered blind.  An initial beep shows that entry may begin (an
initial (optional) sign followed by digits only), backspace, left
arrow, Esc and Enter have the same effect.  An illegal input causes a
deeper beep.  After pressing Enter, a higher tone is sounded.


5.3 Understanding the status line
---------------------------------

The status line displays the following information:

1.  At the left-hand end the step selected by <F> and <C> is dis-
    played.

2.  To the right of this is either `R' (ruler moves), `W' (window
    moves) or, if there is no ruler, nothing.

3.  A little bit further right if gray scaling is possible, `Gxy'
    appears otherwise `Sxy'.  These are the values set by +zoom-x,
    +zoom-y, +scaling-x and +scaling-y -- and altered by <+>, <->,
    <Alt>+<G> and <Alt>+<S>.

4.  The side number (the first side selected is side 1) appears in
    the middle of the line together with the page number.  For exam-
    ple,

        5:      10.7

    shows side 5.  The first page on side 5 has page number 10.7.

5.  To the right of this the coordinates of the top left-hand
    corner of the window are shown (if transformed, this is not
    necessarily the top left-hand corner of the screen: for example,
    in transformation 1 the coordinates are those of the bottom
    left-hand corner of the screen).  The position display

        x=0pt y=0pt

    is the top left-hand corner of the sheet.  If the ruler is
    graduated then the distance between two (short) gradations is
    displayed as well.  The gradation is chosen to make this a read-
    able distance.  Every tenth gradation is somewhat longer than the
    others.

6.  A `W' is displayed near the right-hand end of the line if
    warnings messages have occurred while dviscr or dvivik was in
    graphics mode.

7.  A `*' is displayed at the right-hand end of the line while the
    picture is being built up or while a text search is in progress.

The status line can be removed by the option +status-line:off.


6 \special
==========

The drivers take note of all \special's beginning with `em:'; blanks
may appear between `em:' and the following keyword (`graph', `point',
`line', `linewidth', `pcl' or `pclfile').

Any \special's which do not start with `em:' are silently ignored.

The drivers can understand the following \special's:

\special{em:graph xxx}

Insert the graphics file xxx at this place.  The upper left corner
of the picture is located at the reference point of a character were
it to appear here.  You can use MSP (MS Paint under Windows 1.x and
2.x), PCX (Paintbrush) and black and white BMP files.  4 color CGA
mode PCX files cannot be used.  Run length encoded BMP files cannot
be used.  All non-white pixels of a PCX file are printed (assuming
the standard palette).  For efficiency reasons, usage of MSP files
(Windows 2.x) is recommended.  The width of the picture must not
exceed 32760 pixels, the height must not exceed 32766 pixels.
Example (the size of the picture is 21pt by 23pt):

    \begin{center}
    \begin{picture}(21,23)
      \put(0,23){\special{em:graph dvitrans.2}}
    \end{picture}
    \end{center}

If a graphics file is not found while +batch-mode is active, the
picture will be omitted and warning message 1303 will be displayed.
If a graphics file is not found while +batch-mode is not active, you
will be prompted for the name of the graphics file.  If you enter /d,
the picture will be omitted.  If +change-mode is active, you will be
prompted for a file name for each \special{em:graph} command before
the driver tries to open the graphics file.  If +omit-graphics:on is
in effect, \special{em:graph} is ignored.

\special{em:point n[,[x],[y]]}
\special{em:line a[h|v|p],b[h|v|p][,width]}
\special{em:linewidth width}
\special{em:moveto}
\special{em:lineto}

With these commands lines can be drawn at any desired angle.  A point
n (1 to 32767) is defined with \special{em:point n} and gets the
coordinates of the reference point.  If x or y or both are specified,
these values override the coordinates of the reference point.  For
instance,

    \special{em:point 1,10pt}

defines point 1 10pt to the right of the left margin and with the Y
coordinate of the reference point.

\special{em:point n} commands can be positioned using the LaTeX
picture environment.  For plain TeX, see page 389 of The TeXbook.
Two such points can be joined by a line: \special{em:line a,b,width}
joins the points numbered a and b with a line `width' thick -- the
width can be given in any unit acceptable to the +unit option except
px.  The point numbers can have `h', `v' or `p' appended showing how
the end of the line should be cut.  `p' causes the line to be cut
perpendicular to its direction, `h' make a horizontal cut and `v' a
vertical cut.  `p' is used as default if no cut mode is specified.
Note that a horizontal line cannot have a horizontal cut nor vertical
line a vertical one!

Example:

    \special{em:line 1,2v,4pt}

Points need not be defined before the lines which refer to them.
Point and line definitions are local to the current page.

If a number of lines with the same width are to be drawn,
\special{em:linewidth width} can be used to set the default
width for all subsequent lines without a `width' argument --
\special{em:line a,b}.  The initial setting of the default width
is 0.4pt; any \special{em:line a,b} appearing BEFORE a `linewidth'
special will have this width.  To avoid errors, the required line
width should be set before each picture composed of lines.

There are other commands for line drawing.  \special{em:moveto}
sets the current (drawing) point to the coordinates of the ref-
erence point without drawing a line: \special{em:lineto} draws
a line between the current point and the reference point, the
reference point then becomes the current point.  A polygon can
be drawn with one \special{em:moveto} and a number of subsequent
\special{em:lineto} commands.  The width of the line will be that set
by \special{em:linewidth width}.

\special{em:pcl string}

This command is ignored (without warning message) by all drivers
except dvihplj.  All blanks directly following em:pcl are skipped.
The remaining characters are copied unmodified into the output after
moving the cursor to the reference point.  The following example
prints a gray rectangle of height and width 0.5in:

    \special{em:pcl ^^1b*c15g360h360v2P}

\special{em:pclfile name}

This command is ignored (without warning message) by all drivers
except dvihplj.  The file `name' is copied unmodified into the output
after moving the cursor to the reference point.  dvihplj seeks the
file with the specified name only, that is, in the current working
directory if no absolute path name is given.  Example:

    \special{em:pclfile myfile.pcl}


7 Miscellaneous topics
======================


7.1 General notes
-----------------

If the DOS versions of the drivers run out of memory, expanded
memory (EMS 4.0) and extended memory will be used.  If there is no
or not enough expanded memory or if usage of EMS and XMS has been
disabled (see +use-ems:off and +use-xms:off), a temporary file will
be created.  You can select the directory used for the temporary
file by setting the TMP environment variable.  If TMP isn't set, the
temporary file will be created in the root directory of the current
drive.  Normally, the temporary file will be deleted automatically.
The name of the temporary file starts with `dv' followed by a number.

The driver dvidot (as well as dviscr and dvivik if +zoom is used)
will not print characters which have a pixel row falling above the
top paper edge.

Fonts may only contain characters with codes in the range 0 to 255.

The width of a character may not exceed 32760 points and the height
32766.  If a character needs more than 32000 bytes of memory (say,
504x507 points) the driver slows down noticeably.

If MS-DOS or PC-DOS issues a printer timeout error in the middle of
printing then you should type this command to remove timeout checks:

    mode lpt1,,p                                    (DOS 2.x and 3.x)
    mode lpt1 retry=r                               (DOS 4.0 or later)

where lpt1 is to be replaced by the correct printer port
designation.  You may want to use the +xon-xoff:on option when print-
ing to the ports LPT1 to LPT4.

The text of error messages is read from the file dvidrv.err.  This
file must be in the `data' subdirectory of the emTeX directory.  This
file has been created to save memory, not so that the user can change
the messages.


7.2 Output with the +verbosity:4 option
---------------------------------------


7.2.1 dvihplj
-------------

At the end of each page: <a+b,c,d>

a       is the memory used for fonts

b       is the memory used for this page

c       is the number of fonts defined so far

d       is the number of fonts used on this page


7.2.2 All drivers
-----------------

At the end of the program the memory usage, for example

    page buffers            4       40024

This means that 4 page buffers using a total of 40024 bytes were
used.  This memory usage table will also be printed (without
+verbosity:4) if there is not enough memory.


7.3 Return codes (ERRORLEVEL)
-----------------------------

The following return codes are passed to the parent process:

0       No errors

1       Bad argument

2       Bad \special command

8       Fonts are to be generated

9       Error (dvidrv.exe program)

100     Not enough memory

101     Not enough memory or disk space

200     Bad DVI file

201     Bad font file or font not found

202     Bad graphics file or graphics file not found

203     Bad VF file

204     Other error

254     Internal error

You can use IF ERRORLEVEL in batch files to check the return code.


7.4 Known bugs
--------------

Old versions of DR-DOS 5.0 will not allow output directly to a paral-
lel port (for example, PRN) -- you must use option +xon-xoff:on (use
the BIOS for output) together with LPT1 to LPT4, or COM1 to COM4.

There seems to be a bug in the Video 7 PM driver which causes dvipm
to abort.

Virtual fonts currently cannot reference themselves directly or indi-
rectly at a different size.

dvipm doesn't reclaim all memory when opening a new DVI file.  If
dvipm runs out of memory after opening several DVI files, restart
dvipm.


8 Installation of the printer drivers and the screen previewers
===============================================================

1.  Unpack the ZIP archive files as explained in install.eng.

2.  Copy the base fonts for your printer to the hard disk as
    explained in install.eng.

3.  Set the following environment variables:

    DVIDRVINPUT
            search path for DVI files

    DVIDRVFONTS
            search path for font files

    DVIDRVGRAPH
            search path for graphics files

    EMTEXDIR
            the emTeX directory

    For example, this can be done by

        set dvidrvinput=c:\emtex\doc;c:\emtex\doc\english
        set dvidrvfonts=c:\texfonts
        set dvidrvgraph=c:\emtex\doc
        set emtexdir=c:\emtex

    Note that the environment variables should not contain
    whitespace.  When using `Cut & Paste' blanks may sneak in at the
    end of the lines.

    All these lines should be put in the file autoexec.bat
    (config.sys for OS/2).  \emtex\bin\set_tex.bat or
    \emtex\bin\set_tex.cmd can be used as models, or modified and
    called by autoexec.bat.  If you don't want to set the environment
    variables (or if you cannot), you have to insert the desired
    directories into the configuration files (*.cnf).

    To let MFjob call mf386.exe instead of mf.exe, use

        set mfjobopt=/3

    This is highly recommended.

4.  To use dviscr under OS/2 or if you use dvipm and want the VGA or
    8514/A palette to be modified for better gray scaling, you should
    insert the line

        IOPL=YES

    into config.sys (if not already done).  If you don't need the
    spooler of OS/2 1.x, you should disable it.  Under OS/2 2.x,
    you can tell the spooler to print while receiving data from an
    application program.  This setting is recommended.

    Several OS/2 environment variables (and the value of LIBPATH)
    should be supplemented in config.sys.  This is done by appending
    the additional pathname to the end of the appropriate line of
    config.sys, separated with a semicolon from the previous value.
    A semicolon at the end of the line is optional.

    The HELP environment variable should be supplemented with
    \emtex\help for dvipm on-line help.  The HELP environment vari-
    able must be set in config.sys.  Example:

        SET HELP=C:\OS2\HELP;C:\EMTEX\HELP

    Moreover, you should supplement the BOOKSHELF environment vari-
    able with \emtex\book\english to be able to view the dvidrv
    on-line documentation by typing

        view dvidrv

    Example:

        SET BOOKSHELF=C:\OS2\BOOK;C:\EMTEX\BOOK\ENGLISH

    To use dvipm, the files dvipmres.dll, emdll1x.dll, emdll1x2.dll,
    emdll2x.dll and emx.dll must be in directories specified by the
    LIBPATH entry in config.sys.  Add c:\emtex\dll and c:\emx\dll
    (insert the correct drive letter) to LIBPATH.  Example:

        LIBPATH=C:\OS2\DLL;C:\OS2\MDOS;C:\OS2\APPS\DLL;C:\EMTEX\DLL;C:\EMX\DLL

    When using OS/2 1.x, you should modify vp.cmd to run dvipm16.exe
    (or dvipm167.exe to take advantage of the math coprocessor if you
    have one) instead of dvipm.exe.

    Reboot to make the changes to config.sys take effect.

5.  Now the following batch files can be used:

    v       screen previewer (dviscr)

    vs      screen previewer (dviscrs)

    vp      screen previewer for Presentation Manager (dvipm)

    prthpdj
            printer driver (dvihplj: HP DeskJet, 300 DPI)

    prthpdjh
            printer driver (dvihplj: HP DeskJet, 600 DPI)

    prthplj
            printer driver (dvihplj: HP LaserJet+, 300 DPI)

    prthpljh
            printer driver (dvihplj: HP LaserJet IV, 600 DPI)

    prtp6l  printer driver (dvidot p6l: P6 with 180 DPI)

    prtp6m  printer driver (dvidot p6m: P6 with 360x180 DPI)

    prtp6h  printer driver (dvidot p6h: P6 with 360 DPI)

    prtmx   printer driver (dvidot mx80: EPSON MX-80)

    prtfx   printer driver (dvidot fx80: EPSON FX-80)

    prtfxl  printer driver (dvidot fx80l: EPSON FX-80, draft)

    prtlql  printer driver (dvidot lql: EPSON LQ, 180 DPI)

    prtlqm  printer driver (dvidot lqm: EPSON LQ, 360x180 DPI)

    prtlqh  printer driver (dvidot lqh: EPSON LQ, 360 DPI).  Note:
            not all LQ printers support 360 DPI

    prtsty  printer driver (dvidot sty800: EPSON Stylus 800)

    prtbj10e
            printer driver (dvidot bj10eh: Canon BJ-10e)

    prtbj300
            printer driver (dvidot bj300h: Canon BJ300)

    prtitoh
            printer driver (dvidot itoh: C.ITOH 8510A)

    prtaiw  printer driver (dvidot aiw: Apple Imagewriter)

    prtfaxwk
            printer driver (dvidot faxworks: FaxWorks for OS/2)

    pcxdj   create graphics files (parameters: dj.cnf)

    pcxlj   create graphics files (parameters: lj.cnf)

    pcxljh  create graphics files (parameters: ljh.cnf)

    pcxp6l  create graphics files (parameters: p6l.cnf)

    pcxp6m  create graphics files (parameters: p6m.cnf)

    pcxp6h  create graphics files (parameters: p6h.cnf)

    pcxfx   create graphics files (parameters: fx.cnf)

    pcxito  create graphics files (parameters: ito.cnf)

    pcxfax  create graphics files (parameters: fax.cnf)

    If you have a version of DOS prior to 3.3, then you should change
    the first line of these batch files from

        @echo off

    to

        echo off

    The batch files v.cmd, v.bat and vs.bat are preconfigured
    to use the configuration file lj.cnf (LJ fonts).  vp.cmd is
    preconfigured to use the configuration file p6l.cnf (P6L fonts).
    To use a different configuration file, change the batch files or
    give the name of the configuration file on the command line, for
    instance:

        v @p6l mytext

    If you don't have the correct fonts for a printer driver, you can
    in some cases (marked * in the following table) use other fonts
    by scaling these.  This results in some loss of quality except
    for very low resolutions.  When using dviscr or dvipm, better
    enable gray scaling.  Example: Use

        @p6m +zoom-x:2

    instead of

        @p6l_p6m

    for dviscr and dvipm.  The following configuration files are
    available:

        File name    ³ Resolution ³ Fonts ³ Font resolution
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
        bj.cnf       ³   360      ³  BJ   ³      360
        fax.cnf      ³ 204x196    ³  FAX  ³    204x196
        faxl.cnf    *³ 204x98     ³  FAX  ³    204x196
        fx.cnf       ³ 240x216    ³  FX   ³    240x216
        ito.cnf      ³ 160x144    ³  ITO  ³    160x144
        lj.cnf       ³   300      ³  LJ   ³      300
        ljh.cnf      ³   600      ³  LJH  ³      600
        mx.cnf       ³ 120x216    ³  MX   ³    120x216
        mx_fx.cnf   *³ 120x216    ³  FX   ³    240x216
        mxl_fx.cnf  *³ 120x72     ³  FX   ³    240x216
        sty.cnf      ³   360      ³  STY  ³      360
        p6h.cnf      ³   360      ³  P6H  ³      360
        p6l.cnf      ³   180      ³  P6L  ³      180
        p6l_p6h.cnf *³   180      ³  P6H  ³      360
        p6l_p6m.cnf *³   180      ³  P6M  ³    360x180
        p6m.cnf      ³ 360x180    ³  P6M  ³    360x180
        p6m_p6h.cnf *³ 360x180    ³  P6H  ³      360
        qj.cnf       ³   192      ³  QJ   ³      192
        tj.cnf       ³ 192x96     ³  TJ   ³    192x96
        tj_qj.cnf   *³ 192x96     ³  QJ   ³      192

    The configuration files marked with * use scaled fonts, see
    +font-scaling.

    To use the executables which exploit the math coprocessor, add
    the character `7' to the program name used in the batch files.
    To use the coprocessor version of dviscr, for instance, replace
    dviscr with dviscr7 in v.bat (or v.cmd).  Of course that won't
    work unless there is in fact a coprocessor (such as 8087 and
    80387) installed in your computer.

6.  Adjust the margins.  Refer to the description of the +left-margin
    and +top-margin options for the method for adjusting margins.
    You should insert the settings into the appropriate batch files,
    not into the configuration files as the margins depend on the
    printer not on the fonts.

7.  If you are using a NEC P7, EPSON FX-100 or another wide printer,
    change the batch files prt*.cmd and prt*.bat for the bigger paper
    width.  Replace fx80 with fx100, replace p6l, p6m and p6h with
    p7l, p7m and p7h, respectively, replace lql, lqm and lqh with
    lqwl, lqwm and lqwh, respectively.

8.  After moving and resizing the dvipm windows, save the settings.


9 Explanation of warning and error messages
===========================================

When you get the error message `[cannot open dvidrv.err]', the file
dvidrv.err (which contains the messages) couldn't be found.  You'll
find the text of the message in this list using the message number
produced by the driver.


9.1 Warning messages
--------------------

If the verbosity, see +verbosity, is set to a lower number than that
given in brackets, then that warning message will be suppressed.

If the warning message is marked with [F] then the warning is sup-
pressed when the option +font-load-limit:-1 is chosen.

If the warning message has a driver name in brackets then it applies
only to that driver.

#1 and #2 stand for variable fields in the message.

All warning messages have the format

    Warning 1xxx: ...

In the following only the number and the message are given.

1000: argument `#1' of option `#2' is not a valid number

    The numeric argument #1 of the option #2 is not valid for the op-
    tion or an unacceptable size is given in response to a prompt for
    a font file name.

1001: invalid number or unit of measure in argument `#1' of option `#2'

    The argument #1 of the option #2 is an illegal number or the unit
    is not acceptable.  Note that you have to enter units using lower
    case letters.

1002: argument `#1' of option `#2' is too long

The argument #1 of the option #2 is too long.

1005: argument `#1' of option `#2' is not a valid page number

The argument of +first-page or +last-page isn't acceptable.

1008: ambiguous option: #1. Matching options are:

    The input #1 is ambiguous: there is more than one option matching
    your input #1.  A list of all matching options is displayed.

1009: unknown option: #1

The option #1 does not exist.

1010: argument `#1' of option `#2' is not a valid unit of measure

    The option +unit or +ruler-unit is given with an unacceptable or
    misspelt unit, #1.  Acceptable units are pt, pc, in, bp, cm, mm,
    dd, cc, sp and px.  You have to use lower case letters.

1016: output file name ignored due to error in input file name

    The input file was not found.  To avoid the output file name
    to be taken as input file name, the output file name has been
    ignored.

1017: too many file names: `#1'

    There are too many arguments which do not begin with `-', `+' or
    `/' and are therefore taken to be file names.  Depending on the
    driver, only 1 or 2 file names can be given.  You can give 1 file
    name for the previewers (dviscr, dvivik and dvipm).  You can give
    1 or 2 file names for the printer drivers dvidot and dvihplj.
    Note that you must not insert blank spaces between the name of an
    option and the argument of that option.

1018: input file `#1' not found: #2

    The DVI file #1 cannot be found.  DVI files are sought using the
    template set with the +dvi-file option.  The default (without
    using a configuration file) is to search the current working di-
    rectory.  The configuration files that come with dvidrv cause DVI
    files to be sought in the current working directory and in all
    directories listed in the DVIDRVINPUT environment variable.  #2
    gives the reason for the failure to open the file.

1019: cannot create output file `#1'

    The output file cannot be opened: the file name is invalid, the
    directory doesn't exist or you don't have write access to the di-
    rectory or the output file already exists and has read-only mode.

1020: template too long

    The template argument to an option is too long.  Templates may
    contain up to 127 characters.

1021: missing template

    A template must be given to some options.  Note that you must not
    insert blanks between an option and its argument.

1022 environment variable `#1' contains whitespace

    The value of the environment variable #1 contains space or tab
    characters.  To avoid problems, you should edit the SET statement
    used for setting that environment variable.

1023: cannot nest response files

    A response file cannot contain calls to other response files.

1024: response file `#1' not found

    The @responsefile cannot be found.  Response files are sought
    using the template set with the +response-files option.  The
    default is to search the current working directory and the `data'
    subdirectory of the emTeX directory.  Set the EMTEXDIR environ-
    ment variable to define the emTeX directory, which is `\emtex'
    by default.  The default extension for response files is CNF.
    Note that the configuration files that come with the drivers have
    names ending in `.cfg'.

1025: argument `#1' of option `#2' is invalid

    The argument #1 of option #2 is not valid.

1026: +section-count overrides +section-size

    If both +section-count and +section-size are used with a non-zero
    value and the values don't match, +section-count takes precedence
    over +section-size.

1100: preamble data doesn't match postamble data:                          [2]
      pre.#1=#2, post.#1=#3

    The value #1 in the preamble differs from the value in the
    postamble.  Has somebody been meddling with this DVI file? The
    value given in the preamble will be used.

1200: checksum does not match                                            [2,F]
      font file #1: #2
      input file #3: #4

    The font file #1 does not match the TFM file.

1201: wrong design size                                                  [2,F]
      font file #1: #2
      input file #3: #4

    The font file #1 does not match the TFM file.

1202: wrong magnification                                                [2,F]
      font file #1: #2
      input file #3: #4

    The font file #1 does not match the TFM file.

1203: character #1: pixel width off by #2                                [3,F]

    The width of the character #1 (decimal) differs from the width
    calculated from the TFM file by more than 3, namely by #2 (always
    a signed number).  If #2 is positive then the pixel width is the
    larger, if #2 is negative then the TFM width is the larger.  This
    warning appears usually when the font file does not match the TFM
    file used by TeX, in particular, when the font is loaded with the
    wrong magnification.

1204: `#1' is not a usable font file                                       [3]

    In searching for a font file, the file #1 has been found.  This
    file, however, does not look like a font file.  After issuing the
    warning, the next step in the search, described above, is taken.

1205: font #1 [#2] not found

    No suitable file for font #1 can be found.  For further
    explanation see `Font search rules'.  See also the installation
    instructions.

1206: +batch-mode: font #1 replaced by #2                                  [1]

    While +batch-mode was active, font file #2 has been used for font
    #1 as a suitable file cannot be found.

1207: cannot open font library file `#1'

    A font library file (see +font-libraries option) could not be
    found.  Maybe you have given too many names (be careful with
    $env:!).  Note that the configuration files (such as lj.cnf)
    specify a font library file (lj_more.fli, to continue the exam-
    ple) for local fonts.  You'll get warning 1207 if that file does
    not exist.  To create a dummy file, run

        fontlib /c lj_more

    in your font directory using an appropriate font library name.

1208: font #1 replaced by #2 (deviation: #3%)                               [1]

    The size of font #1 has been replaced by the closest available
    font size by applying +font-size-tolerance and +font-sizes.  The
    deviation of size is #3%.

1209: do you want to call MFjob to generate #1 missing fonts now?

    #1 have been marked to be generated.  You can choose to call
    MFjob and METAFONT to generate those fonts, but that can take
    some time.  To generate the fonts, type Y.  To view or print the
    document using replaced fonts, type N.  To get a list of the
    fonts to be generated, type ?.

1210: #1 is not a usable TFM file

    The file #1 is not a TFM file.

1211: font #1 not loaded -- output will be distorted

    Font #1 was not loaded as /d has been given for that font in a
    font substitution file or as you have entered /d.  The positions
    of other objects are wrong because characters from this font are
    omitted entirely.

1212: TFM file for font `#1' not found

    You have told the driver to use TFM files and the driver could
    not find a TFM file for font #1.  The word space parameter, which
    is used for rounding pixel positions, will be estimated by the
    driver.  See +use-tfm-files.

    The drivers use the same method as emTeX for locating TFM files.

1213: font file `#1': PXL file formats are obsolete, use PK instead

    As the PXL file formats are obsolescent, you should use PK files
    instead of PXL files.  If you have the METAFONT sources for the
    font or can otherwise recreate the font with GFtoPK, you should
    do so.  Use PXtoPK only if there is no other way for creating a
    PK file for the font.

1300: `#1' is not a usable graphics file

    When searching for a graphics file, the file #1 has been found.
    This file is, however, not a valid graphics file.  After this
    warning has been issued, the search will continue according to
    the rules described above.

1301: graphics file #1 (graph #2; #3 DPI) not found

    The graphics file #1 cannot be found -- the command is
    \special{em:graph #2}.

1302: graph #1 omitted                                                     [1]

    The picture #1 is not printed because you have entered /d.

1303: +batch-mode: graphics file #1 (#2 DPI) not found                     [1]

    The graphics file #1 with a resolution of #2 DPI was not found
    and -- due to +batch-mode -- omitted.

1400: undefined point: #1

    The point #1 is not defined though it is used in
    \special{em:line}.  Define all points used in \special{em:line}
    commands.

1401: duplicate point number: #1

    The point #1 has been declared more than once in a
    \special{em:point #1}.  Point numbers have to be unique for each
    page.

1402: bad line omitted: #1,#2

    The line with the endpoints #1 and #2 cannot be drawn.  For in-
    stance, horizontal lines cut horizontally cannot be drawn.

1403: missing moveto

    A \special{em:lineto} has appeared without a preceding
    \special{em:moveto}.

1500: printer not ready. R)etry or A)bort?

    The printer is not ready.  Type an `A' to abort the run, `R'
    to try again after fixing the problem (for instance, lack of
    paper).  (Used only with +xon-xoff:on and LPT1 to LPT4.)

1501: 1 warning message was not displayed in graphics mode     [dviscr,dvivik]
1502: 1 warning message was not displayed in graphics mode, see #2
1503: #1 warning messages were not displayed in graphics mode
1504: #1 warning messages were not displayed in graphics mode, see #2

    There were #1 warning messages while the display was in graphics
    mode.  Please check the transcript file #2 for warning messages.

1505 Page width reduced from #1px to #2px                             [dvidot]

    The page width has been reduced from #1 px to #2 px due to
    restrictions of dvidot or of the printer, set in the dvidot param-
    eter file.


9.2 Fatal errors (2xxx)
-----------------------

All fatal errors have the format

    *** Fatal error 2xxx: ...

In the following only the number and ... will be shown.

2000: out of memory

There is not enough memory to run.  Further information is given
showing how much memory was used by what.  In some cases, this error
can be prevented by using +font-load-limit:-1.

2001: cannot open #1 file `#2'

    File #2 not found.

2002: cannot create file `#1'

    The file cannot be opened: the file name is invalid, the direc-
    tory doesn't exist or you don't have write access to the direc-
    tory or the output file already exists and has read-only mode.

2003: cannot write to file `#1'

    While writing to #1 an error was noted; a possible reason for
    this error is that the disk is full.  If #1 is a device such as
    PRN, see help.eng for help.

2004: invalid scale factor

    A font or virtual font is bad.

2005: cannot use XON/XOFF flow control

    XON/XOFF flow control cannot be used as the port does not exist.

2006: serial interface time-out

    When using the XON/XOFF flow control, 60 seconds has elapsed
    since an XOFF was received without an XON.

2007: out of string space

    Internal table overflow, no remedy possible (besides trying to
    print the text in smaller chunks).

2008: cannot open temporary file `#1'

    The drivers use (due to lack of memory) a temporary file, which
    couldn't be opened.  Change the TMP environment variable.

2009: temporary file write error (disk full?)

    Out of disk space for temporary file or some other problem.  By
    setting the TMP environment variable move the temporary file to a
    drive with enough storage space.

2010: printer not ready, aborted by user

    You entered `A' after receiving warning 1500.

2011: cannot read from console

    You have started the driver (under OS/2) using detach or you have
    entered Ctrl-Z or the driver cannot read from standard input for
    another reason.

2012: out of virtual memory

    More virtual memory is required than the driver can manage.

2013: cannot read file `#1'

    An error occurred while reading file #1.

2014: cannot make book due to missing or wrong parameters

    If +page-list-file is used, +section-count and +section-size
    must not be used.  If +section-count or +section-size are used,
    +columns must have an even value.

2015: recursive search: too many directories

    The number of directories which can be handled by the drivers for
    the ! and !! suffixes in environment variables used by $ENV: in
    templates is limited.  That limit has been exceeded.

2100: corrupt DVI file (undefined font)
2101: corrupt DVI file (no font selected)
2102: corrupt DVI file (DVI file ended prematurely)
2103: corrupt DVI file (position stack overflow)
2104: corrupt DVI file (position stack underflow)
2105: corrupt DVI file (bad postamble)
2106: corrupt DVI file (postamble not found)
2107: corrupt DVI file (illegal command in postamble)
2108: input file is not a DVI file
2109: corrupt DVI file (unexpected set_char command)
2110: corrupt DVI file (unexpected fnt_num command)
2111: corrupt DVI file (unexpected bop command)
2112: corrupt DVI file (unexpected eop command)
2113: corrupt DVI file (unexpected rule command)
2114: corrupt DVI file (unexpected motion command)
2116: corrupt DVI file (unexpected post_post command)
2117: corrupt DVI file (unexpected pre command)
2118: corrupt DVI file (invalid command)
2119: corrupt DVI file (back pointer does not point to bop)
2120: corrupt DVI file (more pages than claimed in postamble)

    Bad DVI file.

2121: character number #1 out of range

    An attempt is being made to set a character with a code outside
    the acceptable range (0-255).

2122: page too complex

    A side may contain up to 65536 objects (characters, rules, lines,
    pictures).  You have succeeded in exceeding this limit.

2124: too many points

    You have exceeded the maximum number of \special{em:point},
    \special{em:moveto}, or \special{em:lineto} commands per page.

2125: too many lines

    You have exceeded the maximum number of \special{em:line},
    \special{em:moveto}, or \special{em:lineto} commands per page.

2126: IVD files not supported yet

    The current version of the drivers cannot handle IVD files.  Use
    ivd2dvi to convert the IVD file into a DVI file.  Alternatively,
    use TeX--XeT instead of TeX-XeT.

2131: erroneous \special{#1}: undefined keyword

    After `em:' there is a unknown keyword in \special argument #1.

2132: erroneous \special{#1}: bad parameter

    The \special declaration #1 an unacceptable parameter (for in-
    stance, \special{em:point 0}).

2200: +batch-mode: font #1 not found

    If +batch-mode is active and when a font cannot be found after
    all the search rules have been tried, the program terminates with
    this message.

2201: font file error PK01
2202: font file error PK02
2203: font file error PK03
2204: font file error PK04

    Bad PK font file.

2205: font #1 too big (#2 characters)

    This font has too many characters.

2206: character number #1 not supported

    This version of the driver can only handle character codes from
    0 to 255; a character with a code outside this range has been
    encountered.

2207: font file `#1' ended prematurely

    Bad font file: too short!

2208: font file `#1' disappeared

    The font file #1 cannot be opened although it was there
    initially.  Perhaps the diskette has been swapped.

2209: undefined character #1 in font #2

    Trying to use a character which is not in the font file.

2210: character too big

    A character is too big.

2211: character too big for scaling

    A character is too big to scale (!)

2213: `#1' is not a font library file

    The file selected by the option +font-libraries is not a font
    library file.

2214: use `fontlib /2 /b#1 #2' to convert font library

    The font library file #2 must be converted to the new font
    library format by using fontlib.  You should also use the
    /ffontlist option when running fontlib.

    Please use the new library files (such as lj_base.fli) instead of
    the old ones as the Computer Modern font sources and the METAFONT
    modes have changed.  Old-format font library files (triggering
    error 2214) were made before those changes.

2215: cannot run MFjob, error code=#1

    The driver cannot run mfjob.exe.

2216: MFjob failed

    MFjob reported an error.

2217: cannot handle more than 255 fonts

    The number of fonts is limited to 255.

2220: corrupt TFM file `#1'

    The TFM file #1 is bad.

2301: graphics file `#1' ended prematurely

    Bad graphics file: too short!

2302: graphics image too big

    The picture is too wide.

2303: graphics image too big for scaling

    The picture is too big to scale (!)

2400: syntax error in font substitution file `#1', line #2

    Line #2 in the font substitution file #1 has an error.

2401: missing parameter file name                                     [dvidot]

    dvidot expects the name of a parameter file as its first argument.

2402: parameter file `#1' not found                                   [dvidot]

    dvidot cannot find the parameter file #1.  The first argument on
    the command line must be the name of a parameter file.

2403: invalid parameter file (#1)                                     [dvidot]

    #1 is a number showing the type of error found.

2404: incompatible parameter file, use makedot to convert             [dvidot]

    The parameter file cannot be used with this version of dvidot.
    Use makedot for converting the parameter file.  See makedot.doc
    for details.

2405: expression evaluation stack overflow                            [dvidot]

    Bad parameter file: there's too complex an arithmetic expression.

2406: cannot compute checksum beyond end of header                    [dvidot]

    Bad parameter file: the checksum has to be computed for bytes
    outside the header.

2407: output file doesn't allow random access                         [dvidot]

    Computing the checksum requires reading the output file.
    Therefore you cannot send output to a device.

2408: cannot read output file                                         [dvidot]

    There was an error while reading the output file for computing
    the checksum.

2409 cannot perform vertical motion (#1 dots)                         [dvidot]

    An attempt was made to perform a finer vertical motion than
    allowed by the parameter file's value of VMU=.  This should not
    happen because makedot rejects invalid settings of VMU=.

2410: invalid page dimensions

    The values of +width or +height are too small or too big.  The
    upper limit for +height is 10917 pixels in the 16-bit versions
    of the drivers.  The 32-bit versions support bigger values.  In
    particular, you need dvihplj3.exe to print on A4 paper at 1200
    DPI.

2501: printer memory overflow                                        [dvihplj]

    Calculation shows that the printer's memory is now full.  Set
    the +memory option to the correct value or split the text into
    smaller pieces.  (+clear-fonts:1 may help.)

2502: too many fonts per side                                        [dvihplj]

    There are more fonts required on this page than the printer can
    handle -- split up the text or use +clear-fonts:1.  You can use
    the +fonts-per-side option to set the number of fonts per side
    supported by your printer or to disable checking the number of
    fonts per side.

2503: too many fonts                                                 [dvihplj]

    There are more fonts required in the text than the printer can
    handle -- split up the text or use +clear-fonts:1.  You can turn
    off checking the number of fonts by using the +fonts-per-side:0
    option.

2504: value field in pcl: specification too long

    The maximum length for a PCL font selection string in a font
    substitution file has been exceeded.

2505: resolution must be a multiple of #1

    For the HP DeskJet, the resolution set with +printer-resolution
    must be a multiple of 300.

2511: page width exceeds #1px

    The width of the page set by the +width option may not exceed
    (converted) #1 px.

2520: graphics mode not supported                                     [dviscr]

    There is no graphics adapter card or the card present is not
    supported by this driver.  Perhaps the graphics adapter card is
    supported by dviscr but dviscr doesn't correctly identify the
    card.  Please try to tell dviscr about the adapter type by using
    the +adapter option (for instance, +adapter:16 for a VGA with a
    color display).

2602: corrupt VF file (premature end of DVI commands)
2604: corrupt VF file (stack underflow)
2608: corrupt VF file (bad preamble)
2611: corrupt VF file (unexpected bop command)
2612: corrupt VF file (unexpected bop command)
2616: corrupt VF file (unexpected post_post command)
2617: corrupt VF file (unexpected pre command)
2618: corrupt VF file (invalid command)
2621: corrupt VF file (unexpected fnt_def command)
2622: corrupt VF file (unexpected post command)
2643: corrupt VF file (invalid command)

    Bad VF file.

2603: VF file too complex: stack overflow

    A virtual font can use a further virtual font which can, in its
    turn, use a further virtual font, and so on.  This error message
    is issued when this nesting is excessive or is in an endless loop.

2640: input stack overflow

    A virtual font can use a further virtual font which can, in its
    turn, use a further virtual font, and so on.  This error message
    is issued when this nesting is excessive or is in an endless loop.

2641: input stack underflow

    Bad VF file.

2644: character number #1 out of range

    A character code in a VF file is unacceptable.

2645: virtual font #1 too big (#2 characters)

    The virtual font #1 contains too many characters.

2701: #1(#2): syntax error in page list file

    There's a syntax error in line #2 of file #1 given by
    +page-list-file.

2702: #1(#2): page index out of range

    A page index given in line #2 of file #1 given by +page-list-file
    is too small or too big.


9.3 Internal errors (3xxx)
--------------------------

All internal errors have the format

    *** Internal error 3xxx

or

    *** Internal error 3xxx: ...

If an internal error occurs, please tell the author.  Please make
copies of all files in use (DVI, MSP, PXL, PK, FLI, VF, SUB, log
files) and make a copy of the error message.  Please also make a note
of the arguments used.


10 History
==========

Items marked with `***' are VERY IMPORTANT!


Version 1.5a (09-Apr-1994)
--------------------------

*** Options now have long names, some options have been renamed.

*** Options now use templates instead of lists of directories.

*** File names which are too long are truncated according to the 5+3.3 rule,
    that is, the first 5 characters and the last 3 characters of the base name
    and the first 3 characters of the extension are taken.  lcirclew10.pk, for
    instance, is transformed into lcircw10.pk.  Under OS/2, the drivers
    attempt to open a file using the long file name, first.  Then, the
    truncated file name is used.  Under DOS, only the truncated file name is
    tried.  If the file is not found, the 8.3 rule is applied after the 5+3.3
    rule, that is, the first 8 characters of the base name and the first 3
    characters of the extension are taken.

*** $ENV: in templates now supports ! and !! for recursive search of
    subdirectories.

*** New previewer: dvipm for OS/2 Presentation Manager.

*** New version of emdll1x.dll and emdll1x2.dll.  If you have copied these
    files from \emtex\dll to another directory, you should copy the new
    versions now.  There are three new dynamic link libraries: emdll2x.dll,
    dvipmres.dll and emx.dll.

*** dvipm.exe is now a 32-bit program; the 16-bit version has been renamed to
    dvipm16.exe.  Please delete \emtex\dvipm32.exe.

*** The settings saved by previous dvipm versions are not loaded.  To delete
    the old settings, do the following:

        File->Settings->Save
        File->Settings->Remove
        File->Settings->Save

*** dvimsp has been replaced by dvidot.

*** dvidrv.exe is no longer used under OS/2.  If you are using your own
    *.cmd files, please remove `dvidrv' from those batch files.

*** +font-files can now be used to read VF files.  +virtual-fonts is needed
    only if you want to replace existing fonts with VF files.

*** The +double-sided:printer option (/dp) has been renamed +double-sided:long
    (/dl).  +double-sided:short (/ds) has been added.

*** New method for arranging pages on a sheet.  The following options have
    been removed:

        +first-sub-page
        +show-sub-pages
        +sub-page-index
        +sub-page-slots
        +sub-page-x
        +sub-page-y
        +sub-pages-per-side

    The following options have been added:

        +backside-offset-x
        +backside-offset-y
        +blank-pages
        +columns
        +fold-other
        +full-last-section
        +page-height
        +page-list-file
        +page-shift
        +page-width
        +rows
        +section-count
        +section-size

*** The meaning of the +left-margin and +top-margin options has been changed.
    The +adjust-left-margin and +adjust-top-margin options no longer exist.
    The +page-left-margin and +page-top-margin options have been added.

*** Option +graphic-files renamed to +graphics-files.

*** The .DOT files of previous beta test versions can no longer be used with
    dvidot 1.5a.  makedot cannot directly convert between the format used by
    previous beta test versions and the new format: You have to recreate your
    own .DOT files from the text files.

*** Font searching completely rewritten.

*** New directory structure: *.cnf, *.dot, *.sub files, dvidrv.err and
    fontlist have been moved to \emtex\data.  The environment variable
    EMTEXDIR can be used to tell the drivers where to find that directory.
    $EMTEX: is used in templates to specify the emTeX directory.  $PATH: is no
    longer used.

*** dvihplj: New +printer-model option for selecting the printer model
    (replaces the +deskjet, +kyocera, +laserjet, +paintjet, +quietjet, and
    +thinkjet options of previous test releases and the /od and /ok options of
    dvihplj 1.4d).

*** dvipm: The +inverse option is no longer available; the setting of the
    Reverse menu option is saved with the settings, instead.

*** Font substitution files are now also sought in the `data' subdirectory of
    the emTeX directory; the default extension is .sub.

*** Support for DOS switch character, add EMTEXSWCHAR environment variable.

*** When seeking a font, the drivers try all known sizes (+font-sizes) which
    are within the font size tolerance (+font-size-tolerance).

*** The format of the text format of dvidot parameter files has changed.  See
    makedot.doc.

-   Virtual memory is used under DOS.  The drivers can use EMS (+use-ems), XMS
    (+use-xms), and a temporary file (environment variable TMP).

-   /mh is now the same as /m1095.445115, not /m1095

-   Missing fonts can be generated automatically with MFjob.

-   Missing font libraries now cause a warning message rather than a fatal
    error with program termination.

-   Support long file and blanks in file names under OS/2.  To enter a file
    name which contains blanks, enclose it in double quotes: `test file.dvi'.

-   TFM files can now be read, see +tfm-files.

-   dvipm: File->New closes the DVI file.  Really.

-   dvipm: `What dialog' renamed `Status Window Options'.

-   dvipm: Display information on an object in the View window double
    clicking on the object.

-   dvipm: +titlebar-icons (/ot+) option removed.

-   dvipm: Internal error 3020 when switching DVI files removed.

-   dvipm: Several palette problems fixed.  8514/A palette can now be changed.

-   dvipm: Fonts are reused when opening a new DVI file.

-   dvipm: File->Reload tries to keep the selected page.

-   dvipm: Automatic reloading of the DVI file if it is changed by another
    program.

-   dvipm: Additional pushbuttons in the Font dialog.

-   dvipm: Print all the pages.

-   dvipm: Support display modes with more than 16383 colors (65536 colors,
    for instance).

-   dvipm: +gray-bitmap-size (/og#) replaced with +bitmap-memory-limit (/om#).
    The default value is 512, that is, 512 Kbytes will be used for temporary
    bitmaps.  Therefore, much less memory is used now.

-   dvipm: The meaning of the Ctrl key has been reversed for the arrow keys:
    move by 8 pixels without Ctrl, by 1 pixel with Ctrl.

-   dvipm: Obey +magnification when loading another DVI file.

-   dvipm: New Information window which shows information about the DVI file.
    (Quite preliminary.)

-   dvipm: The background colors are now set in the View Options dialog box.

-   dvipm.exe is now a 32-bit program; the 16-bit version has been renamed to
    dvipm16.exe.

-   dvihplj: The +printer-resolution:600 option now switches the printer to
    600 DPI mode and selects 1/600in as unit of measure.

-   dvihplj: Characters at the left margin are no longer omitted.

-   dvihplj: New +fonts-per-side option (renamed from +fonts-per-page of
    previous test releases).

-   dvihplj: Disable checking of number of fonts per page and number of fonts
    per job if +fonts-per-side:0 is used.

-   dvihplj: Support built-in fonts.

-   dvihplj: `=> pcl:' in font substitution files.

-   dvihplj: \special{em:pclfile ...}

-   dvihplj: New +paper option for specifying the paper size.

-   dvihplj: Clip graphics and rules to avoid omission by the printer.

-   dvihplj: New +draft option for saving toner.

-   dvihplj: Support the HP DeskJet 500J.

-   dvihplj: New options for tuning the output: +full-page-bitmap,
    +optimize-graphics, +compression, +negative-top-offset, +close,
    +download-limit, and +delete-fonts.

-   dvidot: New options: +final-reset and +close.

-   dvidot: New parameter files: fx80l, fx100l, sty800, bj10eh, and bj300h.

-   dvidot now supports printers where the graphics resolution exceeds the
    resolution of paper motion.

-   dvidot and dvihplj: New options +initial-formfeed and +final-formfeed.

-   dviscr: Under OS/2, dviscr now automatically treat an SVGA as VGA.

-   dviscr: +adapter:20 added (Adapter Interface, 8514/A).

-   New configuration files: ljh.cnf (600 DPI with LJH fonts), bj.cnf (360 DPI
    for Canon BubbleJet printers).

-   New batch files: prthpljh.cmd and prthpljh.bat for the HP LaserJet
    IV at 600 DPI.

-   New METAFONT mode in local.mf and modes.mfj: canonbj.

-   Internal error 3028 while reading VF files fixed.

-   New options: +page-list-file, +section-count and +section-size.

-   +max-drift is set in the configuration files.

-   Don't display warning message 1201 for DVI files created by groff.

-   Big characters can now be transformed (rotated).

-   Add +call-mfjob option (/fj+).  Under OS/2, this option is used to
    disable the automatic call of MFjob.

-   texput.dvi is no longer used if the answer to the question for an input
    file is empty.

-   \special{em:message} has been removed.

-   \special{em:graph xxx} can insert BMP files.

-   \special{em:graph xxx}: ignore everything after comma.

-   The maximum number of input pages has been increased from 1364 to 65535.

-   You can now use TFM files with less than 6 font parameters, as they
    are generated, for instance, by bm2font.

-   The number of objects on a page now limited to 65536 (this reduces the
    number available under OS/2 but increases the number under DOS).

-   The dvidrv documentation is now available as OS/2 on-line book.


Version 1.5b (21-Jun-1994)
--------------------------

-   Executables which exploit the math coprocessor are now included.

-   For +font-load-limit:-1, dvihplj 1.5a used TFM files for missing fonts
    even if the TFM files were not for built-in printer fonts.

-   dvihplj has new options for selecting the paper source: +source and
    +manual-feed.

-   Transformation of big characters with +transformation:3 or
    +transformation:6 caused internal errors or crashes.

-   dviscr did not accept the +ruler option.

-   dviscr did not completely suppress the status line for +status-line:off

-   Input and output now works even if running a driver under Emacs under
    OS/2.

-   Rules protruding over the top edge of the paper are no longer omitted in
    gray scaling mode; other objects, however, are still omitted.  This also
    applies to dvidot and dvihplj.

-   dvidot: TRAILER is now written at the end of the file.

-   dvipm: Pictures were sometimes mirrored.


Version 1.5c (22-Jul-1994)
--------------------------

-   Several bugs have been fixed.

-   Due to a bug, the directory ".." was not allowed in path names.

-   Files with names that contain two or more dots can no longer be read and
    written under DOS.

-   dvipm: Optionally reload all fonts when loading a DVI file; doing this is
    recommended after creating new font files with bm2font.

-   dvipm: File->Print_all_pages works now.

-   dvidrv.exe: Pass -pj:filename instead of -pj=filename to the program; this
    enables usage of batch files.


Version 1.5d (30-Aug-1994)
--------------------------

-   Warn about usage of PXL files.  The PXL file formats are obsolete.

-   Warn about whitespace in environment variables used by templates.

-   +backside-offset-x and +backside-offset-y are now also defined for
    +double-sided:even and +double-sided:odd.

-   dvipm: Ask for confirmation before printing when the printer resolution
    does not match the resolution used by dvipm.

-   dvipm: You can now copy from the Messages window to the clipboard.

-   dvipm: `Change printer' has been renamed to `Print options'.  There are
    new settings available.

-   dvipm: Several printing problems solved.

-   dvipm now checks whether the correct version of dvipmres.dll is installed.


Version 1.5e (01-Sep-1994)
--------------------------

-   dvidot 1.5d could not use old DOT files (created by makedot 1.2b or
    lower).

-   Gray scaling did not work in dvipm 1.5d.


Version 1.5f (14-Sep-1994)
--------------------------

-   The drivers no longer crash for `EMM386 FRAME=NONE'.

-   dvipm now switches to the original size and turns off reverse display for
    printing.

-   In dvipm, the Page Down and Page Up keys optionally display the next or
    previous, respectively, page when invoked at the end or beginning,
    respectively, of a page.

-   The Options menu of dvipm is now also available while a DVI file is
    loaded.

-   More printing problems of dvipm have been resolved.


Version 1.5g (10-Oct-1994)
--------------------------

-   Spacing was wrong for magnified documents (that is, +magnification or \mag
    unequal 1000).

-   Improve memory management for virtual fonts.

-   +magnification without argument disables overriding the magnification in
    the DVI file, +magnification:*x multiplies the magnification in the DVI
    file with x.

-   Fix several problems related to changing options in dvipm while a DVI file
    is loaded.

-   Fix and speed up text search of dvipm and dviscr.


Version 1.5h (19-Mar-1995)
--------------------------

*** Executable files have been moved from \emtex to \emtex\bin.  You should
    uninstall any installed dvidrv package using the remove.exe tool and add
    \emtex\bin to your PATH.

*** emx.dll is now shipped in emxrsx.zip and has been moved from \emtex\dll
    to\emx\dll.

*** Font configuration files (such as lj.cnf) now use other font library
    files, for instance, lj_base and lj_more.  There are new configuration
    files and new batch files such as dj.cnf, prthpdj.bat, and pcxdj.bat for
    the HP DeskJet.

*** METAFONT modes and the sources of the Computer Modern fonts have been
    changed; you should delete all old font files to avoid mixing old fonts
    with new fonts.

-   +batch-mode is the default setting now.

-   The default font substitutions performed by +batch-mode have been changed:
    The drivers now always replace characters with rectangles if a TFM file
    can be found.  Substitution of missing fonts by other fonts is no longer
    done.  There are two advantages: First, a bug is no longer triggered,
    which causes wrong character placement if a font is substituted by a font
    of a different design size (for instance, msbm7 by cmr10).  This wrong
    character placement is not limited to the replaced font.  Second, the
    drivers no longer abort due to missing characters if an 8-bit font is
    replaced with a 7-bit font (for instance, a PostScript font with cmr10).

-   The +tfm-files (/pm) option has been removed.  The drivers now use the
    same scheme (environment variables TEXTFM and EMTEXDIR) as emTeX for
    locating TFM files.

-   $ENV: in templates no longer supports ! and !! for recursive search of
    subdirectories as the sole option which used that feature, +tfm-files, has
    been removed.  (! and !! have been added again in 1.5i.)

-   dviscr now supports the following 16-color VESA modes: 640x480, 800x600,
    1024x768, and 1280x1024.  Use the +adapter option as these graphics modes
    are not selected automatically.

-   dvidot did not correctly render the bottom of the page under certain
    circumstances when creating a .bmp file.

-   In dvipm, job properties can now be set even for FxPrint.

-   Some printing problems of dvipm have been resolved.

-   Problems with transformation of big characters have been solved.

-   dvihplj now sets the printer to 192x192 DPI graphics resolution if
    +printer-model:quietjet is used.


Version 1.5i (13-Apr-1995)
--------------------------

-   ! and !! are supported in templates (subdirectory search was removed in
    version 1.5h).

-   dviscr no longer hangs OS/2.

-   Various problems of dviscr's new VESA modes fixed.

-   +font-size-tolerance now applies also to font libraries.

-   Several small flaws removed.

-   You can choose whether dvipm should use GpiBitBlt or GpiDrawBits for
    printing.


Version 1.5j (19-Apr-1995)
--------------------------

-   Another VESA problem of dviscr fixed.

-   Don't override command line options with values from environment variables
    (such as DVIDRV) when reloading the DVI file.


Version 1.6a (25-Jun-1995)
--------------------------

-   The default extension CNF is used for response files.

-   New +ask-mfjob option to select whether the drivers should ask or not
    before running MFjob to automatically compute missing fonts.

-   Try to solve the rounding problems of automatic font generation by
    looking also for a size off by 1 in certain cases (for instance,
    cmr10<464.49887> will be sought both in dpi464 and dpi465).

-   Printing with dvipm works.

-   dvipm can load and save options.

-   New batch files: prtbj10e.bat, prtbj10e.cmd, prtbj300.bat, prtbj300.cmd,
    prtfaxwk.cmd, pcxfax.bat, and pcxfax.cmd

-   dvidot: New parameter file: faxworks.


Version 1.6b (04-Jul-1995)
--------------------------

-   dviscr: The +color option now gets written correctly to the transcript
    file.

-   dvipm: Add dialog box for selecting the pages to be printed.  Add
    quick file menus.


Version 1.6c (07-Aug-1995)
--------------------------

-   Letter case is now ignored for font names in font libraries.

-   faxworks.dot has been fixed, prtfaxwk now prints in the correct size.

-   The default output file of prtfaxwk is now LPT3 instead of PRN.

-   prtmx.bat and prtmx.cmd were missing.

-   2a4_a4.cnf etc. now set +magnification relative to \magnification of
    the DVI file.

-   @i in templates (except for the +dvi-file option) will now be replaced
    with the truncated name (5+3.3 or 8.3) of the DVI file if the name has
    been truncated.

-   A magnifying glass has been added to dvipm.  For now, it just magnifies
    the displayed bitmap (instead of displaying the original unscaled bitmap).

-   dvihplj: New +set-paper option.


Version 1.6d (23-Aug-1995)
--------------------------

-   The fixed version of faxworks.dot was not shipped with dvidot 1.6c,
    therefore prtfaxwk still printed in the wrong size with dvidot 1.6c.

-   dvipm: The View window will optionally not be cleared while reloading the
    DVI file.

-   dvipm: You can drag the contents of the View window with the mouse while
    pressing the first mouse button.


Version 1.6e (09-Sep-1995)
--------------------------

-   If there is at least one completely unused section when using
    +section-count, +full-last-section:on will be set automatically.

-   dvipm: The current gray scaling and reduction factors are used for saving
    the +zoom and +scaling options.

-   dviscr: The /ocp# option now sets the color of the page border only.


Version 1.6f (09-Apr-1996)
--------------------------

-   Various virtual font bugs have been fixed.

-   prtbj10e and prtbj300 now use bj.cnf instead of p6h.cnf.

-   prtsty now uses sty.cnf instead of p6h.cnf.

-   Rounding of coordinates for \special{em:line ...} etc. has been improved.

-   Properly handle very long \special commands.

-   dvipm: gray scaling 1x1 through 8x8 can now be selected directly (Ctrl+1
    through Ctrl+8).

-   dvihplj: can use 600 DPI on the DeskJet 850c (no configuration file and no
    METAFONT mode provided for now).  Sorry, this does not work on the DeskJet
    600 and DeskJet 660.

-   dvihplj: support +draft for newer DeskJet models.

-   dviscr: Reference card \emtex\doc\dviscr.dvi contributed by Roger de Reus.


Version 1.6g (04-Mar-1997)
--------------------------

*** Support added for automatically generating EC fonts; support for
    automatically generating DC fonts has been removed.

-   +blank-pages did not work correctly when making a book.

-   Various bug fixes.

-   dvihplj: Support 600 DPI on the DeskJet 600 (and other models); prthpdjh
    added (using ljh.cnf).

-   dvipm: New menu item Edit->End for moving to the end of the page.

-   dvipm: The space and backspace keys can be used for scrolling.

Version 1.6h (02-Jul-1998)
--------------------------

-   Yet another virtual font bug has been fixed (set_rule).

-   dvihplj: 32-bit version (dvihplj3.exe) supplied.  This executable uses
    the math coprocessor; if your machine doesn't have a math coprocessor,
    you'll have to install emxrt.zip (see \emx\doc\emxrt.doc).

-   dvihplj: Support 1200 DPI; however, dvihplj3.exe is required for
    printing on A4 paper.

-   dvidot: New parameter file: sty800.

(09-Jul-1998)
-------------

-   dviphlj32.exe renamed dvihplj3.exe; no longer dumps core when trying to
    print to a device under DOS

                  -------- End of DVIDRV.DOC -------------