## Slide 1: Effects of Winglets on Drone Propellers
By Zander Farr

## Slide 2: Project Outline
My goal is to design and manufacture a propeller that reduces wing vortices to increase efficiency and noise reduction.
Study the effects of blade count, winglets, and geometry on a propeller’s overall noise production, thrust and efficiency.
This was achieved by advancing knowledge in SolidWorks, fabrication, 3D printing, data collection and analyses.

## Slide 3: Propeller Noise and Efficiency
Propeller noise is a growing concern in urban and military environments. With a growing network of package delivery by drone producing a propeller that mitigates noise production is crucial.
The main factor contributing to noise production is blade tip vortices. As a propeller rotates, pressure differences between the upper and lower surfaces of the blades create vortices.
The rapid mixing of these pressures creates turbulent flow and pressure fluctuations resulting in a high pitch noise.

## Slide 4: Winglets
Winglets are small vertical extensions designed to reduce drag by reducing vortices.

## Slide 5: Forces on an Airfoil
As a propeller rotates the blades experience a wide variety of forces
Drag force is the resistive force experienced by the blade.
Thrust force is the forward pushing force allowing acceleration
Lift is the upward force generated by a propeller, this is what allows us to get and stay airborne.
Torque is the twisting force that the propeller exerts on the engine shaft as it rotates.

## Slide 6: Winglets Simulations

## Slide 9: Computational Fluid Dynamics (CFD)
The Continutiy Equation:
  Based on the Conservation of Mass: Mass can neither be created nor destroyed
  The continuity equation relates the fluids density, velocity and flow rate across different points in a system.
The Navier Stokes Equation:
  Conservation of Momentum in fluid mechanics: The rate of change of momentum of the fluid is equal to the sum of all external forces acting on the fluid.
The Energy Equation:
  First Law of Thermodynamics in fluid dynamics states that in a closed system the total energy of a fluid remains constant over time.

## Slide 10
Forces acting on an infinitesimal fluid element
Meshing in CFD

## Slide 11: Experimental Setup
Data collection was achieved using CoolTerm, Betaflight and Room EQ Wizard (REW).
CoolTerm communicates with serial devices like Arduino. Used to display loadcell readings onto my computer and save thrust data into text files.
Betaflight controlled the motor speed (RPM).
Room EQ Wizard is an open-source acoustic measurement software used to read decibel and hertz data.

## Slide 12: How does the Trust Stand Work?

## Slide 13: Wiring and Code

## Slide 14: Setup
Make sure the battery is charged above 14.8 volts.
Check that all connections (FC/ESC stack and Arduino) are secure.
Start CoolTerm, BetaFlight, and REW on your computer.
Connect each device to the correct port:
  Betaflight: USB-C to computer
  Microphone: USB to computer
  Arduino: USB-C to computer
Connect the battery to the multimeter and the multimeter to the ESC.
Wait for the flight controller to play its tune, indicating proper power.
Press the reset button on the Arduino to tare the load cell.
In CoolTerm, disconnect from the Arduino port.
Select Connection > Capture to Text/Binary File, then click Start.
Name the file (e.g., RPM) and save it to a folder specific to the blade being tested.
  Example: "500RPM" saved to Propeller with Winglet – Raw Thrust Data.

## Slide 15: Meaurements
In BetaFlight, connect to the computer and open the Motors tab.
Accept the motor warning and adjust the slider to the desired RPM.
Start CoolTerm to record load cell readings. Let it run for 30 seconds.
Simultaneously, open REW and record a 10-second audio spectrum (decibel level and hertz).
During the 30-second interval, note the amperage from the multimeter and the voltage from BetaFlight.
After 30 seconds, stop CoolTerm by clicking Stop under Capture to Text/Binary File.
Repeat the entire process for each RPM in the test range. Save all data accordingly.

## Slide 16: Flow Simulation Vs Experimental
This is the single winglet simulation thrust data (blue line) and the single winglet experimental data (orange line) compared to each other to determine if the thrust stand produces accurate data.
Chart: Thrust Vs. Angular Velocity
| 25000 | 24500 | 24000 | 23500 | 23000 | 22500 | 22000 | 21500 | 21000 | 20500 | 20000 | 19500 | 19000 | 18500 | 18000 | 17500 | 17000 | 16500 | 16000 | 15500 | 15000 | 14500 | 14000 | 13500 | 13000 | 12500 | 12000 | 11500 | 11000 | 10500 | 10000 | 9500 | 9000 | 8500 | 8000 | 7500 | 7000 | 6500 | 6000 | 5500 | 5000 | 4500 | 4000 | 3500 | 3000 | 2500 | 2000 | 1500 | 1000
 | 8.2866 | 7.8171 | 7.7458 | 6.9765 | 7.0474 | 6.9588 | 6.5347 | 6.0928 | 5.9657 | 5.4277 | 5.3148 | 5.014 | 4.8135 | 4.548 | 4.2502 | 4.0598 | 3.753 | 3.8861 | 3.6907 | 3.034 | 2.9284 | 2.9608 | 2.5629 | 2.4499 | 2.1044 | 2.0671 | 1.8738 | 1.6771 | 1.5131 | 1.4078 | 1.3078 | 1.1674 | 1.0355 | 0.93245 | 0.82987 | 0.77828 | 0.62054 | 0.55294 | 0.4858 | 0.37709 | 0.30525 | 0.26496 | 0.21094 | 0.15749 | 0.12138 | 0.078781 | 0.049173 | 0.025907 | 0.011585
 | 3.7808 | 3.5323 | 3.3742 | 3.1987 | 3.0327 | 2.901 | 2.7171 | 2.4402 | 2.2958 | 2.1143 | 1.9426 | 1.7415 | 1.6093 | 1.4544 | 1.3284 | 1.202 | 1.0803 | 0.97588 | 0.92639 | 0.76057 | 0.67629 | 0.58975 | 0.50193 | 0.42914 | 0.36863 | 0.29695 | 0.23302 | 0.1831 | 0.143 | 0.099892 | 0.069964 | 0.042109 | 0.019398 | 0.0076392

## Slide 17: Thrust Values
RPM | Winglet | Gemfan Hurricane | Double Winglet | Simulation Winglet
500 | 0.003965166 | 0.001779467 | 0.003700808 | 
1000 | 0.007639168 | 0.010119977 | 0.007129865 | 0.011584624
1500 | 0.019398039 | 0.022275365 | 0.018104772 | 0.025907058
2000 | 0.042108784 | 0.043404597 | 0.039301391 | 0.049172086
2500 | 0.06996392 | 0.075244938 | 0.065299426 | 0.078779681
3000 | 0.099892419 | 0.120752044 | 0.093232592 | 0.121376527
3500 | 0.143003728 | 0.172760687 | 0.133469669 | 0.157492345
4000 | 0.183102907 | 0.226970512 | 0.170895436 | 0.210940448
4500 | 0.233022399 | 0.285474314 | 0.217486796 | 0.264956712
5000 | 0.296948702 | 0.381992092 | 0.277151132 | 0.305245363
5500 | 0.368634099 | 0.475359901 | 0.344057263 | 0.377084595
6000 | 0.429140522 | 0.563623091 | 0.400529723 | 0.485788738
6500 | 0.501928636 | 0.649266114 | 0.468465054 | 0.552929212
7000 | 0.589752196 | 0.773578913 | 0.550433417 | 0.62053267
7500 | 0.676294516 | 0.897259594 | 0.631205961 | 0.778269435
8000 | 0.760565823 | 1.029802389 | 0.709858899 | 0.829860793
8500 | 0.926386862 | 1.180737966 | 0.86462465 | 0.932436356
9000 | 0.975876744 | 1.308830121 | 0.910815041 | 1.035456846
9500 | 1.080290545 | 1.499355114 | 1.008267574 | 1.167423078
10000 | 1.202029934 | 1.698757402 | 1.121890598 | 1.307819336
10500 | 1.328360838 | 1.841126278 | 1.239799021 | 1.407731627
11000 | 1.454351395 | 2.05212197 | 1.357389787 | 1.513036633
11500 | 1.609337756 | 2.246934867 | 1.502043208 | 1.677031376
12000 | 1.741461871 | 2.451213459 | 1.625358608 | 1.873808377
12500 | 1.942629356 | 2.6529994 | 1.813114257 | 2.067028655
13000 | 2.114305542 | 2.913540231 | 1.973344792 | 2.104386091
13500 | 2.295784432 | 3.153805585 | 2.142724484 | 2.449860638
14000 | 2.440177182 | 3.380480379 | 2.27749057 | 2.562871381
14500 | 2.717050184 | 3.614084498 | 2.535904448 | 2.928401599
15000 | 2.90103235 | 3.953785639 | 2.707620523 | 2.960726525
15500 | 3.032736874 | 4.169029462 | 2.830544306 | 3.033944701
16000 | 3.198654765 | 4.558850176 | 2.985400452 | 3.690660919
16500 | 3.374184996 | 4.725742964 | 3.149228082 | 3.752947729
17000 | 3.532281552 | 5.064136754 | 3.296784341 | 3.886070102
17500 | 3.78079694 | 5.44922295 | 3.528731208 | 4.05978448

## Slide 18: Decibel Readings

## Slide 19: Frequency Spectrum

## Slide 20: Power Consumption
Power Consumption (N/watt) |  |  | 
RPM | Winglet | Double Winglet | Purchased
2000 | 0.416424 | 0.211196 | 0.209502
3000 | 0.28414 | 0.192359 | 0.223466
4000 | 0.165761 | 0.1352 | 0.152296
5000 | 0.130394 | 0.102534 | 0.130472
6000 | 0.090739 | 0.095689 | 0.104757
7000 | 0.082279 | 0.074647 | 0.092448
8000 | 0.073912 | 0.062707 | 0.083825
9000 | 0.063716 | 0.060685 | 0.070511
10000 | 0.054961 | 0.050581 | 0.069288
11000 | 0.050356 | 0.046047 | 0.061929
12000 | 0.04582 | 0.041672 | 0.057348
13000 | 0.042193 | nan | 0.053712
14000 | 0.039535 | nan | 0.048686
15000 | 0.038179 | nan | 0.046644
Propeller efficiency is measured in N/Watt because this tells us how
efficiently we are producing our electrical energy into useful thrust.
With losses like drag, mechanical inefficiencies, and motor performance
makes it difficult to obtain theoretical values for efficiency calculations.

## Slide 21: Conclusions
This project aimed to explore the effects of winglet design on propeller performance with a specific focus on noise reduction and efficiency.
The winglet results demonstrated a noise decrease between 3-8 decibels compared to standard propellers. Which corresponds to a 30%-60% noise reduction.
This reduced noise production while maintaining optimal thrust and efficiency values shows great potential in military and urban applications.
The efficiency values can also be improved with better fabrication techniques and further design refinements.
The field of aerodynamics will be forever changing as we discover more effective ways to achieve flight.

## Slide 22: Questions?