## Slide 1: Radioactivity of Building Materials
Helaina Hale

## Slide 2: Recap of Experiment
Studying radioactivity of building materials using gamma-ray spectroscopy
  Determine what nuclides are present in each sample
  Source Activity for nuclides identified
  Estimation of dose rate from given elements

## Slide 3: Expected Spectrums
Th-232
K-40
Ra-226
U-238

## Slide 4: Background Spectrums

## Slide 5: Building Material Spectrums
Portland Cement
Brick
Granite

## Slide 6: Results

## Slide 7: Resulting Spectrums
Chart: Building Material Spectrums
1460.8 keV (K-40)

## Slide 8: Portland Cement
Chart: Portland Cement Background Subtracted Spectrum

## Slide 9: Portland Cement (0.009 kg)
Nuclide | Measured Activity | Absolute Activity | Dose Rate
Pb-212 | 0.025 ± 0.001 cps | 0.0227 ± 0.0151 Bq | 1.1214 x 10-22 J/kg 1.1214 x 10-22 Gy 1.1214 x 10-22 rem
K-40 | 0.0025 ± 0.0020 cps | 0.056 ± 0.002 Bq | 3.204 x 10-22 J/kg 3.204 x 10-22 Gy 3.204 x 10-22 rem

## Slide 10: Brick
Chart: Brick Background Subtracted Spectrum

## Slide 11: Brick (0.0081 kg)
Nuclide | Measured Activity | Absolute Activity | Dose Rate
Pb-212 | 0.0085 ± 0.0005 cps | 0.0189 ± 0.0011 Bq | 3.204 x 10-23 J/kg 3.204 x 10-23 Gy 3.204 x 10-23 rem
K-40 | 0.0001 ± 0.0021 cps | 0.009 ± 0.0189 Bq | 1.1214 x 10-23 J/kg 1.1214 x 10-23 Gy 1.1214 x 10-23 rem

## Slide 12: Granite
Chart: Granite Background Subtracted Spectrum

## Slide 13: Granite (0.0075 kg)
Nuclide | Measured Activity | Absolute Activity | Dose Rate
K-40 | 0.0029 ± 0.0017 cps | 0.0264 ± 0.0155 Bq | 1.4418 x 10-20 J/kg 1.4418 x 10-20 Gy 1.4418 x 10-20 rem

## Slide 14: Material Estimations
Absolute activity for samples
Measured activity estimates gammas/s
Use standard weight to estimate absolute activity and average amount in home
Upscale number of gammas
Estimate home and human square footage
Divide gammas going in by fraction to obtain gammas/s interacting
Multiply energy by gammas/s interacting
Number gammas/standard weight (J/kg)
Estimate yearly dose

## Slide 15: Setbacks
Equipment issues
  Equipment arrival time
  Computer quality
  Access to only one MCA
Conflicting schedules
  PHY-331 occurring simultaneously

## Slide 16: Achievements
Nuclides identified in given building materials
Measured Activity calculations
Absolute activity calculations (estimated)
Dose rate calculations (estimated)

## Slide 17: Additional Comments Personal Experience
Expansion of research
  Separate experiment to determine photopeak detection efficiency of well-detector
  Contribution of other materials
Experience independently working towards deadline
Overcoming setbacks/challenges
Enhanced technical writing and speaking skills
Lab experience and further understanding of atomic and nuclear physics

## Slide 18: Questions?

## Slide 20: Material estimations
10 80lb bags of Portland cement (Home foundation)
  K-40: 1.16 x 10-19 J
  Pb-212: 4.07 x 10-20 J
1000 Bricks (Home build)
  K-40: 1.98 x 10-20 J
  Pb-212: 5.67 x 10-20 J
Granite countertop and island
  K-40: 1.96 x 10-18 J
  K-40: 3.27 x 10-18 J