## Slide 1: Material Comparison for Drone Propeller Efficiency
Jeffrey DeSarro

## Slide 2: Milestones
Measure reference blade
Transfer measurements of reference blade to SolidWorks 2024 software
3D print blades of different types of materials: PLA plastic, Carbon Fiber, Fiberglass Filled Nylon
Test out 3D printed blades
Determine which material is the most efficient

## Slide 3: Measurements from Reference Blade

## Slide 4: Efficiency
Measure input power (electrical power) and output power (mechanical power)
Input Power = Voltage x Current
Output Power = Torque x Angular Velocity
________________
Input Power
Output Power
Efficiency =
Angular Velocity =
_______________
60
2 x π x RPM
Torque = Thrust x Propeller Radius
X 100%

## Slide 5: Solidworks Designs: Design 1

## Slide 6: Solidworks Designs: Design 2

## Slide 7: Solidworks Designs: Design 3

## Slide 8: Solidworks Designs: Design 4

## Slide 9: Results: PLA Plastic
Measured Values:
Voltage: 17.74 V
Amperage: 0.86 A
Thrust: 0.06063022936 N
Radius of blade: 0.2984252 in
RPM: 5000
Calculated Values:
Angular Velocity: 523.5987756 rad/s
Torque: 0.01809358832
Efficiency Output: 9.473780692
Efficiency Input: 15.2564
Efficiency: 0.6209709166

## Slide 10: Results: Carbon Fiber
Measured Values:
Voltage: 17.74 V
Amperage: 0.94 A
Thrust: 0.06640145729 N
Radius of blade: 0.2984252 in
RPM: 5000
Calculated Values:
Angular Velocity: 523.5987756 rad/s
Torque: 0.01981586817
Efficiency Output: 10.37556431
Efficiency Input: 16.6756
Efficiency: 0.6222003593

## Slide 11: Results: Fiberglass Filled Nylon
Measured Values:
Voltage: 17.74 V
Amperage: 0.53 A
Thrust: 0.04139502715 N
Radius of blade: 0.2984252 in
RPM: 5000
Calculated Values:
Angular Velocity: 523.5987756 rad/s
Torque: 0.01235331926
Efficiency Output: 6.468182837
Efficiency Input: 9.4022
Efficiency: 0.6879435491

## Slide 12: Comparison of Results
PLA Plastic: 62.1%
Carbon Fiber: 62.22%
Fiberglass Filled Nylon: 68.8%
Overall, the fiberglass filled nylon was the most efficient out of the 3 materials tested