11/6/83
 
 
 
 
 
 
 
                    MATLAB Installation Guide
                         November, 1983
 
 
                           Cleve Moler
                 Department of Computer Science
                    University of New Mexico
 
 
 
     The MATLAB tape is usually in one of two formats --  a  UNIX
"tar" tape, or a "generic" tape with the following parameters:
 
          9 track
          1600 bits per inch
          no label
          80 characters per record
          1600 characters per block
          18 files in ASCII, followed by 18 files in EBCDIC
 
     There are 36 files on the generic tape.  The  names  of  the
first 18, and their approximate sizes, are:
 
          1.  INSTALL       1100 lines
          2.  MAT           3900 lines
          3.  LIB           3339 lines
          4.  HELPER.66       75 lines
          5.  HELPER.77      120 lines
          6.  HELP           750 lines
          7.  SYS.UNIX       900 lines
          8.  SYS.VMS        260 lines
          9.  SYS.TSO        200 lines
         10.  SYS.CMS        350 lines
         11.  SYS.DEC10      250 lines
         12.  SYS.CDC        200 lines
         13.  SYS.PRIME      350 lines
         14.  DOC           3960 lines
         15.  DEMO            21 lines
         16.  DOC.NROFF     3250 lines
         17.  MAT.SNGL      3850 lines
         18.  LIB.SNGL      3339 lines
 
where a line is one 80 character record.
 
     The first 18 files are  in  the  ASCII  character  set.  The
remaining 18 files are copies of the first 18 in EBCDIC.
 
     INSTALL is this document.  You can skip over it if you  have
this hard copy.
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 2
 
 
 
     MAT, LIB, one of the versions  of  HELPER  and  one  of  the
versions  of SYS together constitute the complete source code for
the double precision version of MATLAB.
 
     The subroutines in MAT make up the parser  and  interpreter.
They  include  a  COMMON statement which can be changed to change
the amount of memory allocated to variables.
 
     The subroutines in LIB  include  modified  versions  of  the
necessary  routines from LINPACK, EISPACK and the BLAS.  These do
not contain any COMMON statements and do not have to  be  changed
if the size of the stack is changed.
 
     There are two  versions  of  HELPER,  the  subroutine  which
manages  the  help facility.  The version in HELPER.66 is written
in Fortran 66 and uses sequential i/o. The version  in  HELPER.77
is  written in Fortran 77 and uses character variables and direct
access i/o. If your  system  supports  both  versions,  you  will
probably  want  to  choose  the direct access one -- it should be
much faster. If you choose the direct access  version,  you  will
have  to  run a preprocessor named HELPSET, which is also in file
HELPER.77.
 
     HELP is the source text for the help facility.  It  is  read
by  the  sequential version of HELPER, or preprocessed by HELPSET
into two files which are then read by the direct  access  version
of  HELPER.   HELP  is also included as an appendix in the User's
Guide.
 
     The subroutines in one of the versions of SYS may have to be
modified for your particular operating system.  They involve file
access and floating point word format.  I have included  versions
that  should  work  on several different operating systems.  Pick
the version that is closest to  your  own  system  and  make  any
changes you need.  There are no machine dependent constants.
 
     DOC is a report entitled "MATLAB Users' Guide".   It  should
be printed on a nice printer with upper and lower case; there are
66 lines per page.  Make as many copies as  you  need,  or  order
copies from us at New Mexico.
 
     DEMO  contains  a  demonstration  exec  file  which  can  be
accessed by the exec command in MATLAB. On most systems, all that
is required is EXEC('DEMO') or EXEC('DEMO',7).  On some  systems,
like  TSO  and  NOS,  it will be necessary to attach file DEMO to
unit 2 and then EXEC(2) or EXEC(2,7).
 
     DOC.NROFF is the input to the UNIX  text  processing  system
that  was used to produce DOC.  This may be useful if you want to
print the users' guide in a different format.
 
     MAT.SNGL and LIB.SNGL are the single precision  versions  of
MAT  and LIB.  It is suggested that these be used only on systems
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 3
 
 
 
with long  words  (48  bit  floating  point  fraction)  or  small
memories.
 
     The first thing to worry about is the character set. The use
of an upper-lower case character set is highly desirable, but not
essential.  Read the tape and look at the first 50 or so lines of
MAT.  This  is  the  subroutine  MATLAB,  a  listing  of which is
included in this document. Check the comments near the  beginning
to  see  if  the special characters are ok.  The ones we have had
trouble with include:
        SEMI ;   BSLASH    COLON :   LESS <   GREAT >
Any characters which are not ok should be changed in the  comment
and  in the data statement which follows. The alternate character
set includes the lower case letters as well  as  substitutes  for
some of the special characters, such as  and :, which are not on
some terminals.  Do  not  worry  too  much  about  the  alternate
character  set  now.   These data statements in subroutine MATLAB
are  the  only  place  in  the  source  code  where  the  special
characters  occur.   (If  you  want to get fancy, there is a data
statement involving BEL in subroutine ERROR near the end of  file
MAT.   Change  1H-blank  to  1H-control G to get your terminal to
ring its bell for any error.)
 
     The files DOC and  HELP  are  full  of  special  characters,
including
          <   >   \   !   :   ;      
If they are not ok, I hope it is not too difficult  to  fix  them
up.
 
     I have used several FORTRAN  constructions  which  are  only
semi-standard, and which may have to be changed for some systems:
  Single quote (') in FORMATS instead of a tribute to Hollerith.
  Entire arrays initialized in DATA statements.
  Use of END= in READ statements.
I have not asked PFORT to tell me what else is non-standard.
 
     Some interactive FORTRAN systems use column 1  for  carriage
control and others don't.  If your system does not, edit file MAT
and delete all "1X," .  There are 131 occurrences.
 
     The main program in file SYS simply  calls  MATLAB.  It  may
have  to  be  modified  to  control the printing of underflow and
overflow  messages.   The  ground  rules  are:   Underflows   are
possible,  but  are  harmless  if  they  are quietly set to zero.
Overflows are error conditions.  It would  be  nice  to  print  a
message and continue.
 
     A listing of a typical version of SYS, using some Fortran 77
for  clarity,  is included in this document.  I hope it is fairly
easy to see what the various subroutines do and how they have  to
be  revised  for  your  system. Please send me copies of versions
appropriate for your system.
 
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 4
 
 
 
     The amount of memory required can be  altered  by  a  global
text  edit  on  MAT which changes the matrix element stack length
from 5005 to something else.  Be sure to get the statement
          VSIZE = 5005
in the subroutine MATLAB.  With this setting of the stack length,
MATLAB  requires  about  a 300K byte region on an IBM system. The
length has to be reduced somewhat to get MATLAB to fit into a 64K
word  region on a CDC system.  Since each matrix element occupies
two double or single precision words, an increase of 1000 in  the
stack length requires an additional 16K bytes or 2000 words.
 
     It is possible to  get  by  with  less  memory  if  you  use
overlays.  The simplest way to do this is the following.
 
                   ROOT
                     
      -------------------------------
                               
     S0    S1    S2    S3    S4    S5
 
Only ROOT plus one of the segments  S0  through  S5  need  be  in
memory at any one time.  The segments do not call each other, but
return to the root.  All the relevant calls are near the  end  of
subroutine  MATLAB  in  the  root.  There are five labeled COMMON
blocks which are shared by the root and all  the  segments.   The
various segments consist of:
 
      ROOT:
        MAIN        MATLAB      STACK1
        PRINT       PRNTID      FUNS
        STACKP      ERROR       FILES
        HELPER      PYTHAG      FORMZ
        FLOP        PROMPT
        Plus everything in file LIB not mentioned below.
 
      S0:
        PARSE       COMAND      CLAUSE
        EXPR        TERM        FACTOR
        STACKG      STACK2      GETSYM
        GETLIN      GETCH       GETVAL
        EDIT        XCHAR
 
      S1:
        MATFN1      WGECO       WGEFA
        WGESL       WGEDI       WPOFA
        RREF        HILBER
 
      S2:
        MATFN2      CORTH       COMQR3
        HTRIDI      HTRIBK      IMTQL2
 
      S3:
        MATFN3      WSVDC
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 5
 
 
 
      S4:
        MATFN4      WQRDC       WQRSL
 
      S5:
        MATFN5      MATFN6      MAGIC
        SAVLOD      RAT         USER
        PLOT
 
If you have enough room, combine ROOT and S0.   With  more  room,
combine  ROOT,  S0  and  S5.   If you use some overlay structure,
please send me a description of how it is done on your system.
 
     In  case  anybody  needs  to  know,  here  are  the  changes
necessary  to  convert from double to single precision.  They can
all be safely accomplished by simple global text changes in  MAT,
LIB and an appropriate version of SYS.
 
      DOUBLE PRECISION   REAL
      DOUBLE-            REAL-
      DSQRT              SQRT
      DLOG               ALOG
      DEXP               EXP
      DSIN               SIN
      DCOS               COS
      DATAN              ATAN
      DABS               ABS
      DMAX1              AMAX1
      DMIN1              AMIN1
      IDINT              IFIX
      DSIGN              SIGN
      DMOD               AMOD
      D0                 E0
      D1                 E1
      D2                 E2
      D9                 E9
 
 
     Here are some additional comments that apply  to  individual
systems.
 
 
VAX UNIX.
 
     If you have read the "tar" format tape, see file README  and
the makefile.  Ignore the rest of this section.
 
     It is essential to change the single backslash  in the data
statement  near  the  beginning of file MAT to a double backslash
.  If this is not done, the F77 compiler  produces  an  obscure
error message about "dataalpha" being too long.
 
     Increase the size of the stack  to  take  advantage  of  the
virtual  memory.  Eliminate  all the "1X," in formats. Change the
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 6
 
 
 
statement CASE = 0 in MATLAB to CASE = 1 to get lower  case  file
names.   All  these  changes  can be accomplished by applying the
following ed or vi commands to file MAT.
 
        1,$s///g
        1,$s/5005/50005/g
        1,$s/1X,/0X,/g
        1,$s/CASE = 0/CASE = 1/
        1,$s/BEL/1H /BEL/1H^G/
        1,$s/LCT(2) = 25/LCT(2) = 25000/
 
     The compilation should suppress warnings about  initializing
non-character   variables  with  Hollerith  and  should  use  the
Berkeley version of  the  i/o  support  routines.   This  can  be
accomplished with:
 
      % f77 -w66 mat.f lib.f helper.f sys.f -lI77uc
 
     Gary Klimowicz and Lee Ward of UNM have developed a overflow
fault  handler  for use with VAX UNIX.  A copy of their C program
in included in SYS.UNIX and on the "tar" tape.
 
 
 
VAX VMS
 
     SYS.VMS contains an extra subroutine for proper handling  of
floating point overflow.  The main program includes a call to the
system which initializes this handling.
 
     Integer overflow is expected in the the print routine and in
random  number  generator.   The integer overflow messages can be
turned off by
 
     FORTRAN/NOCHECK  MAT.FOR,LIB.FOR
 
 
 
IBM (TSO)
(Thanks to Jack Dongarra at Argonne.)
 
     The main program in SYS.TSO includes the  appropriate  calls
to the IBM system utility ERRSET that turns off verbose underflow
and overflow messages.
 
     Unfortunately, TSO does not have  a  mechanism  for  opening
files during execution.  It is necessary to use file numbers with
SAVE, LOAD and EXEC.
 
     We have to specify LRECL=80 for terminal input on unit 5  to
get  blanks  added to input lines.  It is a good idea to set up a
clist something like the following.
 
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 7
 
 
 
      FREE FILE(FT05F001 FT06F001 FT09F001 FT01F001 FT02F001)
      FREE ATTRLIST(AT80)
      ATTR  AT80 LRECL(80) BLKSIZE(80) RECFM(F)
      ALLOC FILE(FT05F001) DA(*) USING(AT80)
      ALLOC FILE(FT06F001) DA(*)
      ALLOC FILE(FT09F001) DA('MATLAB.HELP.DATA')
      ALLOC FILE(FT01F001) DA(SAVLOD.DATA)
      ALLOC FILE(FT02F001) DA('MATLAB.DEMO.DATA')
      CALL 'MATLAB.LOAD(MATMOD)'
 
With this arrangement, the DEMO file can be executed by  exec(2).
 
 
 
IBM (CMS)
(Thanks to Jack Dongarra at Argonne and David Gay at MIT.)
 
     Entering a blank line  in  response  to  the  MATLAB  prompt
generates  an  end-of-file  from  terminal  input  (Fortran  unit
FT05F001). This results in a call from GETLIN to FILES with LUNIT
=  -5.  The terminal is "rewound" and control eventually returned
to PARSE which prints another prompt.  I hope this works.
 
     An assembly language routine used to attach files with names
generated  by  MATLAB  to  Fortran  unit  numbers  is included in
SYS.CMS.
 
 
 
DEC-10
(Thanks to Stan Eisenstat and Craig Douglas at Yale.)
 
     The  hyperbolic  trig  functions  SINH  and  COSH  are   not
available on the DEC system.  Fortran subroutines are included in
the SYS.DEC10 file.
 
 
 
PRIME 400
(Thanks to Richard Franke and Drexel University.)
 
     The terminal is  Fortran  I/O  unit  number  1.   Subroutine
MATLAB has to be changed so that
      RTE = 5  becomes  RTE = 1
      WTE = 6  becomes  WTE = 1
Subroutine MATFN5 has to be changed so that
      WIO = 1  becomes  WIO = 8
      LUNIT = 1  becomes  LUNIT = 8  (in two places).
 
 
 
CDC
 
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 8
 
 
 
     CDC systems offer exciting challenges as far as  portability
is  concerned.  The first question is: which character set should
be used?  An easy  approach  is  to  convert  everything  to  the
venerable  6-bit  character  set.   Even so, you may have trouble
with the colon, which is a pretty important MATLAB character.  It
is  far  more  fun to try to use upper and lower case and all the
special symbols.  I have succeeded in doing this with  the  6/12-
bit  setup  used  on  the NOS system at Sandia, but have given up
with the 6/18-bit coding on LTSS at Los Alamos.
 
     In  "ASCII"  mode  on  NOS,  lower   case   characters   are
represented  by  12 bits -- the first 6 bits are octal 76 and the
last 6 are the corresponding upper case character.  They count as
two  characters.   So, the following changes are required in file
MAT.  Several of the mixed  case  strings  in  FORMAT  statements
extend  beyond column 72.  You might as well convert these to all
upper case.  All the 80A1's  in  FORMATS  should  be  changed  to
132A1's  and all the DATA statements initializing LRECL should be
changed from  80  to  132.   The  DATA  statement  for  ALPHB  in
subroutine   MATLAB  can  be  changed  to  have  all  upper  case
alphabetic characters because subroutine  XCHAR  will  catch  the
prefix octal 76.
 
     An important change involves our  friend  the  colon,  which
becomes  a  12-bit  octal 7404.  In the DATA statement for ALPHA,
make the element just before 1H+ into a 1H(percent  sign).   And,
in  the  DATA statement for ALPHB, make the corresponding element
into a 2H(colon).  Then read the comments in subroutine XCHAR  in
file  SYS.CDC  and  make  sure that the DATA statements there are
correct.
 
     The FTN5 compiler should take MATLAB pretty much is  it  is.
The  older  FTN  compiler  requires  two  familiar changes to the
entire source code.  First, the END= in the READ statements  have
to be replaced by IF (EOF) GO TO ... .  Second, the single quotes
in FORMATS have to be replaced with asterisks.
 
 
 
Good luck.  Please let me know what difficulties  you  have,  and
what I have left out of this guide.  You can call me at:
         505-268-8631  (home)
         505-277-3112  (office)
 
------------
 
     The support of the National Science Foundation and  the  use
of facilities at Argonne National Laboratory, Los Alamos National
Laboratory and Stanford Linear Accelerator Center  is  gratefully
acknowledged.   So  is the assistance of the many people who have
installed early versions of MATLAB.
 
 
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 9
 
 
 
Contents of file MAT:
 
      SUBROUTINE MATLAB(INIT)
      SUBROUTINE PARSE
      SUBROUTINE COMAND(ID)
      SUBROUTINE CLAUSE
      SUBROUTINE EXPR
      SUBROUTINE TERM
      SUBROUTINE FACTOR
      SUBROUTINE FUNS(ID)
      SUBROUTINE STACKP(ID)
      SUBROUTINE STACKG(ID)
      SUBROUTINE STACK1(OP)
      SUBROUTINE STACK2(OP)
      SUBROUTINE PRINT(ID,K)
      SUBROUTINE PRNTID(ID,ARGCNT)
      SUBROUTINE GETSYM
      SUBROUTINE GETLIN
      SUBROUTINE GETCH
      SUBROUTINE GETVAL(S)
      SUBROUTINE MATFN1
      SUBROUTINE MATFN2
      SUBROUTINE MATFN3
      SUBROUTINE MATFN4
      SUBROUTINE MATFN5
      SUBROUTINE MATFN6
      SUBROUTINE ERROR(N)
      DOUBLE PRECISION FUNCTION PYTHAG(A,B)
      SUBROUTINE RAT(X,LEN,MAXD,D)
 
Contents of file HELPER.66:
 
      SUBROUTINE HELPER(H) -- Sequential version
 
Contents of file HELPER.77:
 
      PROGRAM HLPSET       -- Direct access setup
      SUBROUTINE HELPER(H) -- Direct access version
 
Contents of file SYS:
 
      PROGRAM MAIN
      SUBROUTINE FILES(LUNIT,NAME)
      SUBROUTINE SAVLOD(LUNIT,ID,M,N,IMG,JOB,XREAL,XIMAG)
      SUBROUTINE FORMZ(LUNIT,X,Y)
      DOUBLE PRECISION FUNCTION FLOP(X)
      SUBROUTINE XCHAR(BUF,K)
      SUBROUTINE USER(A,M,N,S,T)
      SUBROUTINE PROMPT(PAUSE)
      SUBROUTINE PLOT(LUNIT,X,Y,N,P,K,BUF)
      SUBROUTINE EDIT(BUF,N)
 
 
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 10
 
 
 
Contents of file LIB:
 
      SUBROUTINE WGECO(AR,AI,LDA,N,IPVT,RCOND,ZR,ZI)
      SUBROUTINE WGEFA(AR,AI,LDA,N,IPVT,INFO)
      SUBROUTINE WGESL(AR,AI,LDA,N,IPVT,BR,BI,JOB)
      SUBROUTINE WGEDI(AR,AI,LDA,N,IPVT,DETR,DETI,WORKR,WORKI,JOB)
      SUBROUTINE WPOFA(AR,AI,LDA,N,INFO)
      SUBROUTINE RREF(AR,AI,LDA,M,N,EPS)
      SUBROUTINE HILBER(A,LDA,N)
      SUBROUTINE HTRIDI(NM,N,AR,AI,D,E,E2,TAU)
      SUBROUTINE HTRIBK(NM,N,AR,AI,TAU,M,ZR,ZI)
      SUBROUTINE IMTQL2(NM,N,D,E,Z,IERR,JOB)
      SUBROUTINE CORTH(NM,N,LOW,IGH,AR,AI,ORTR,ORTI)
      SUBROUTINE COMQR3(NM,N,LOW,IGH,ORTR,ORTI,HR,HI,WR,WI,ZR,ZI,IERR
      SUBROUTINE WSVDC(XR,XI,LDX,N,P,SR,SI,ER,EI,UR,UI,LDU,VR,VI,LDV,
      SUBROUTINE WQRDC(XR,XI,LDX,N,P,QRAUXR,QRAUXI,JPVT,WORKR,WORKI,
      SUBROUTINE WQRSL(XR,XI,LDX,N,K,QRAUXR,QRAUXI,YR,YI,QYR,QYI,QTYR,
      SUBROUTINE MAGIC(A,LDA,N)
      SUBROUTINE BASE(X,B,EPS,S,N)
      DOUBLE PRECISION FUNCTION URAND(IY)
      SUBROUTINE WMUL(AR,AI,BR,BI,CR,CI)
      SUBROUTINE WDIV(AR,AI,BR,BI,CR,CI)
      SUBROUTINE WSIGN(XR,XI,YR,YI,ZR,ZI)
      SUBROUTINE WSQRT(XR,XI,YR,YI)
      SUBROUTINE WLOG(XR,XI,YR,YI)
      SUBROUTINE WATAN(XR,XI,YR,YI)
      DOUBLE PRECISION FUNCTION WNRM2(N,XR,XI,INCX)
      DOUBLE PRECISION FUNCTION WASUM(N,XR,XI,INCX)
      INTEGER FUNCTION IWAMAX(N,XR,XI,INCX)
      SUBROUTINE WRSCAL(N,S,XR,XI,INCX)
      SUBROUTINE WSCAL(N,SR,SI,XR,XI,INCX)
      SUBROUTINE WAXPY(N,SR,SI,XR,XI,INCX,YR,YI,INCY)
      DOUBLE PRECISION FUNCTION WDOTUR(N,XR,XI,INCX,YR,YI,INCY)
      DOUBLE PRECISION FUNCTION WDOTUI(N,XR,XI,INCX,YR,YI,INCY)
      DOUBLE PRECISION FUNCTION WDOTCR(N,XR,XI,INCX,YR,YI,INCY)
      DOUBLE PRECISION FUNCTION WDOTCI(N,XR,XI,INCX,YR,YI,INCY)
      SUBROUTINE WCOPY(N,XR,XI,INCX,YR,YI,INCY)
      SUBROUTINE WSET(N,XR,XI,YR,YI,INCY)
      SUBROUTINE WSWAP(N,XR,XI,INCX,YR,YI,INCY)
      SUBROUTINE RSET(N,DX,DY,INCY)
      SUBROUTINE RSWAP(N,X,INCX,Y,INCY)
      SUBROUTINE RROT(N,DX,INCX,DY,INCY,C,S)
      SUBROUTINE RROTG(DA,DB,C,S)
      LOGICAL FUNCTION EQID(X,Y)
      SUBROUTINE PUTID(X,Y)
      DOUBLE PRECISION FUNCTION ROUND(X)
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 11
 
 
 
First subroutine in file MAT:
 
      SUBROUTINE MATLAB(INIT)
C     INIT = 0 FOR ORDINARY FIRST ENTRY
C          = POSITIVE FOR SUBSEQUENT ENTRIES
C          = NEGATIVE FOR SILENT INITIALIZATION (SEE MATZ)
C
      DOUBLE PRECISION STKR(5005),STKI(5005)
      INTEGER IDSTK(4,48),LSTK(48),MSTK(48),NSTK(48),VSIZE,LSIZE,BOT,TOP
      INTEGER ALFA(52),ALFB(52),ALFL,CASE
      INTEGER IDS(4,32),PSTK(32),RSTK(32),PSIZE,PT,PTZ
      INTEGER DDT,ERR,FMT,LCT(4),LIN(1024),LPT(6),RIO,WIO,RTE,WTE,HIO
      INTEGER SYM,SYN(4),BUF(256),CHAR,FLP(2),FIN,FUN,LHS,RHS,RAN(2)
      COMMON /VSTK/ STKR,STKI,IDSTK,LSTK,MSTK,NSTK,VSIZE,LSIZE,BOT,TOP
      COMMON /ALFS/ ALFA,ALFB,ALFL,CASE
      COMMON /RECU/ IDS,PSTK,RSTK,PSIZE,PT,PTZ
      COMMON /IOP/ DDT,ERR,FMT,LCT,LIN,LPT,RIO,WIO,RTE,WTE,HIO
      COMMON /COM/ SYM,SYN,BUF,CHAR,FLP,FIN,FUN,LHS,RHS,RAN
C
      DOUBLE PRECISION S,T
      INTEGER EPS(4),FLOPS(4),EYE(4),RAND(4)
C
C     CHARACTER SET
C            0       10       20       30       40       50
C
C     0      0        A        K        U   COLON  :  LESS   <
C     1      1        B        L        V   PLUS   +  GREAT  >
C     2      2        C        M        W   MINUS  -
C     3      3        D        N        X   STAR   *
C     4      4        E        O        Y   SLASH  /
C     5      5        F        P        Z   BSLASH 
C     6      6        G        Q  BLANK     EQUAL  =
C     7      7        H        R  LPAREN (  DOT    .
C     8      8        I        S  RPAREN )  COMMA  ,
C     9      9        J        T  SEMI   ;  QUOTE  '
C
      INTEGER ALPHA(52),ALPHB(52)
      DATA ALPHA /1H0,1H1,1H2,1H3,1H4,1H5,1H6,1H7,1H8,1H9,
     $    1HA,1HB,1HC,1HD,1HE,1HF,1HG,1HH,1HI,1HJ,
     $    1HK,1HL,1HM,1HN,1HO,1HP,1HQ,1HR,1HS,1HT,
     $    1HU,1HV,1HW,1HX,1HY,1HZ,1H ,1H(,1H),1H;,
     $    1H:,1H+,1H-,1H*,1H/,1H,1H=,1H.,1H,,1H',
     $    1H<,1H>/
C
C     ALTERNATE CHARACTER SET
C
      DATA ALPHB /1H0,1H1,1H2,1H3,1H4,1H5,1H6,1H7,1H8,1H9,
     $    1Ha,1Hb,1Hc,1Hd,1He,1Hf,1Hg,1Hh,1Hi,1Hj,
     $    1Hk,1Hl,1Hm,1Hn,1Ho,1Hp,1Hq,1Hr,1Hs,1Ht,
     $    1Hu,1Hv,1Hw,1Hx,1Hy,1Hz,1H ,1H(,1H),1H;,
     $    1H,1H+,1H-,1H*,1H/,1H$,1H=,1H.,1H,,1H",
     $    1H\,1H!/
C
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 12
 
 
 
      DATA EPS/14,25,28,36/,FLOPS/15,21,24,25/
      DATA EYE/14,34,14,36/,RAND/27,10,23,13/
C
      IF (INIT .GT. 0) GO TO 90
C
C     RTE = UNIT NUMBER FOR TERMINAL INPUT
C     WTE = UNIT NUMBER FOR TERMINAL OUTPUT
C     HIO = UNIT NUMBER FOR HELP FILE
      RTE = 5
      WTE = 6
      HIO = 9
C
      IF (INIT .GE. 0) WRITE(WTE,100)
  100 FORMAT(//1X,'     < M A T L A B >'
     $  /1X,'   Version of --/--/--')
C
C     ASK HELPER TO OPEN HELP FILE
      BUF(1) = 0
      CALL HELPER(BUF)
C
C     RANDOM NUMBER SEED
      RAN(1) = 0
C
C     INITIAL LINE LIMIT
      LCT(2) = 25
C
      ALFL = 52
      CASE = 1
C     CASE = 1 for file names in lower case
      DO 20 I = 1, ALFL
         ALFA(I) = ALPHA(I)
         ALFB(I) = ALPHB(I)
   20 CONTINUE
C
      VSIZE = 50005
      LSIZE = 48
      PSIZE = 32
      BOT = LSIZE-3
      CALL WSET(5,0.0D0,0.0D0,STKR(VSIZE-4),STKI(VSIZE-4),1)
      CALL PUTID(IDSTK(1,LSIZE-3),EPS)
      LSTK(LSIZE-3) = VSIZE-4
      MSTK(LSIZE-3) = 1
      NSTK(LSIZE-3) = 1
      S = 1.0D0
   30 S = S/2.0D0
      T = 1.0D0 + S
      IF (T .GT. 1.0D0) GO TO 30
      STKR(VSIZE-4) = 2.0D0*S
      CALL PUTID(IDSTK(1,LSIZE-2),FLOPS)
      LSTK(LSIZE-2) = VSIZE-3
      MSTK(LSIZE-2) = 1
      NSTK(LSIZE-2) = 2
      CALL PUTID(IDSTK(1,LSIZE-1), EYE)
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 13
 
 
 
      LSTK(LSIZE-1) = VSIZE-1
      MSTK(LSIZE-1) = -1
      NSTK(LSIZE-1) = -1
      STKR(VSIZE-1) = 1.0D0
      CALL PUTID(IDSTK(1,LSIZE), RAND)
      LSTK(LSIZE) = VSIZE
      MSTK(LSIZE) = 1
      NSTK(LSIZE) = 1
      FMT = 1
      FLP(1) = 0
      FLP(2) = 0
      DDT = 0
      RAN(2) = 0
      PTZ = 0
      PT = PTZ
      ERR = 0
      RIO = RTE
      WIO = 0
      IF (INIT .LT. 0) RETURN
C
   90 CALL PARSE
      IF (FUN .EQ. 1) CALL MATFN1
      IF (FUN .EQ. 2) CALL MATFN2
      IF (FUN .EQ. 3) CALL MATFN3
      IF (FUN .EQ. 4) CALL MATFN4
      IF (FUN .EQ. 5) CALL MATFN5
      IF (FUN .EQ. 6) CALL MATFN6
      IF (FUN .EQ. 21) CALL MATFN1
      IF (FUN .NE. 99) GO TO 90
      RETURN
      END
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 14
 
 
 
Typical file SYS (Nonstandard stuff in lower case):
 
C     PROGRAM MAIN
      call overflow-control
      CALL MATLAB(0)
      STOP
      END
 
 
      SUBROUTINE FILES(LUNIT,NAME)
      INTEGER LUNIT,NAME(32)
C
C     SYSTEM DEPENDENT ROUTINE TO ALLOCATE FILES
C     LUNIT = LOGICAL UNIT NUMBER
C     NAME = FILE NAME, 1 CHARACTER PER WORD
C
      character*32 nam
c
c     close exec, save, load and print files
      if (lunit .lt. 0) then
         close(unit=-lunit)
         return
      end if
c
c     Fortran 77 internal file conversion from 32a1 to character*32
      write(nam,'(32a1)') name
c
c     formatted i/o for exec and print
      if (lunit .gt. 2) open(unit=lunit,file=nam)
c
c     unformatted i/o for save and load
      if (lunit .le. 2) open(unit=lunit,file=nam,form='unformatted')
c
c     rewind all except diary
      if (lunit .ne. 8) rewind lunit
c
      RETURN
      END
 
 
      SUBROUTINE SAVLOD(LUNIT,ID,M,N,IMG,JOB,XREAL,XIMAG)
      INTEGER LUNIT,ID(4),M,N,IMG,JOB
      DOUBLE PRECISION XREAL(1),XIMAG(1)
C
C     IMPLEMENT SAVE AND LOAD
C     LUNIT = LOGICAL UNIT NUMBER
C     ID = NAME, FORMAT 4A1
C     M, N = DIMENSIONS
C     IMG = NONZERO IF XIMAG IS NONZERO
C     JOB = 0     FOR SAVE
C         = SPACE AVAILABLE FOR LOAD
C     XREAL, XIMAG = REAL AND OPTIONAL IMAGINARY PARTS
C
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 15
 
 
 
C     THIS VERSION USES UNFORMATTED READ AND WRITE
C
      IF (JOB .GT. 0) GO TO 20
C
C     SAVE
   10 WRITE(LUNIT) ID,M,N,IMG
      DO 15 J = 1, N
         K = (J-1)*M+1
         L = J*M
         WRITE(LUNIT) (XREAL(I),I=K,L)
         IF (IMG .NE. 0) WRITE(LUNIT) (XIMAG(I),I=K,L)
   15 CONTINUE
      RETURN
C
C     LOAD
   20 READ(LUNIT,END=30) ID,M,N,IMG
      IF (M*N .GT. JOB) GO TO 30
      DO 25 J = 1, N
         K = (J-1)*M+1
         L = J*M
         READ(LUNIT,END=30) (XREAL(I),I=K,L)
         IF (IMG .NE. 0) READ(LUNIT,END=30) (XIMAG(I),I=K,L)
   25 CONTINUE
      RETURN
C
C     END OF FILE
   30 M = 0
      N = 0
      RETURN
      END
 
 
      SUBROUTINE FORMZ(LUNIT,X,Y)
      DOUBLE PRECISION X,Y
C
C     SYSTEM DEPENDENT ROUTINE TO PRINT WITH Z FORMAT
C
      IF (Y .NE. 0.0D0) WRITE(LUNIT,10) X,Y
      IF (Y .EQ. 0.0D0) WRITE(LUNIT,10) X
   10 format(2z18)
      RETURN
      END
 
 
      DOUBLE PRECISION FUNCTION FLOP(X)
      DOUBLE PRECISION X
C     SYSTEM DEPENDENT FUNCTION
C     COUNT AND POSSIBLY CHOP EACH FLOATING POINT OPERATION
C     FLP(1) IS FLOP COUNTER
C     FLP(2) IS NUMBER OF PLACES TO BE CHOPPED
C
      INTEGER SYM,SYN(4),BUF(256),CHAR,FLP(2),FIN,FUN,LHS,RHS,RAN(2)
      COMMON /COM/ SYM,SYN,BUF,CHAR,FLP,FIN,FUN,LHS,RHS,RAN
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 16
 
 
 
C
      double precision mask(14),xx,mm
      real mas(2,14)
      logical lx(2),lm(2)
      equivalence (lx(1),xx),(lm(1),mm)
      equivalence (mask(1),mas(1))
      data mas/
     $ z'ffffffff',z'fff0ffff',
     $ z'ffffffff',z'ff00ffff',
     $ z'ffffffff',z'f000ffff',
     $ z'ffffffff',z'0000ffff',
     $ z'ffffffff',z'0000fff0',
     $ z'ffffffff',z'0000ff00',
     $ z'ffffffff',z'0000f000',
     $ z'ffffffff',z'00000000',
     $ z'fff0ffff',z'00000000',
     $ z'ff00ffff',z'00000000',
     $ z'f000ffff',z'00000000',
     $ z'0000ffff',z'00000000',
     $ z'0000fff0',z'00000000',
     $ z'0000ff80',z'00000000'/
C
      FLP(1) = FLP(1) + 1
      K = FLP(2)
      FLOP = X
      IF (K .LE. 0) RETURN
      FLOP = 0.0D0
      IF (K .GE. 15) RETURN
      XX = X
      MM = MASK(K)
      LX(1) = and(LX(1),LM(1))
      LX(2) = and(LX(2),LM(2))
      FLOP = XX
      RETURN
      END
 
 
      SUBROUTINE XCHAR(BUF,K)
      INTEGER BUF(1),K
C
C     SYSTEM DEPENDENT ROUTINE TO HANDLE SPECIAL CHARACTERS
C
      INTEGER DDT,ERR,FMT,LCT(4),LIN(1024),LPT(6),RIO,WIO,RTE,WTE
      COMMON /IOP/ DDT,ERR,FMT,LCT,LIN,LPT,RIO,WIO,RTE,WTE
      write(WTE,10) buf(1)
   10 format(A1,' is not a MATLAB character.')
      RETURN
      END
 
 
      SUBROUTINE USER(A,M,N,S,T)
      DOUBLE PRECISION A(M,N),S,T
C
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 17
 
 
 
      INTEGER A3(9)
      DATA A3 /-149,537,-27,-50,180,-9,-154,546,-25/
      IF (A(1,1) .NE. 3.0D0) RETURN
      DO 10 I = 1, 9
         A(I,1) = A3(I)
   10 CONTINUE
      M = 3
      N = 3
      RETURN
      END
 
 
      SUBROUTINE PROMPT(PAUSE)
      INTEGER PAUSE
C
C     ISSUE MATLAB PROMPT WITH OPTIONAL PAUSE
C
      INTEGER DDT,ERR,FMT,LCT(4),LIN(1024),LPT(6),RIO,WIO,RTE,WTE
      COMMON /IOP/ DDT,ERR,FMT,LCT,LIN,LPT,RIO,WIO,RTE,WTE
      WRITE(WTE,10)
      IF (WIO .NE. 0) WRITE(WIO,10)
   10 FORMAT(1X,/'<>')
      IF (PAUSE .EQ. 1) READ(RTE,20) DUMMY
   20 FORMAT(A1)
      RETURN
      END
 
 
      SUBROUTINE PLOT(LUNIT,X,Y,N,P,K,BUF)
      DOUBLE PRECISION X(N),Y(N),P(1)
      INTEGER BUF(79)
C
C     PLOT X VS. Y ON LUNIT
C     IF K IS NONZERO, THEN P(1),...,P(K) ARE EXTRA PARAMETERS
C     BUF IS WORK SPACE
C
      DOUBLE PRECISION XMIN,YMIN,XMAX,YMAX,DY,DX,Y1,Y0
      INTEGER AST,BLANK,H,W
      DATA AST/1H*/,BLANK/1H /,H/20/,W/79/
C
C     H = HEIGHT, W = WIDTH
C
      XMIN = X(1)
      XMAX = X(1)
      YMIN = Y(1)
      YMAX = Y(1)
      DO 10 I = 1, N
         XMIN = DMIN1(XMIN,X(I))
         XMAX = DMAX1(XMAX,X(I))
         YMIN = DMIN1(YMIN,Y(I))
         YMAX = DMAX1(YMAX,Y(I))
   10 CONTINUE
      DX = XMAX - XMIN
 
 
 
 
 
 
 
 
 
MATLAB Installation, page 18
 
 
 
      IF (DX .EQ. 0.0D0) DX = 1.0D0
      DY = YMAX - YMIN
      WRITE(LUNIT,35)
      DO 40 L = 1, H
         DO 20 J = 1, W
            BUF(J) = BLANK
   20    CONTINUE
         Y1 = YMIN + (H-L+1)*DY/H
         Y0 = YMIN + (H-L)*DY/H
         JMAX = 1
         DO 30 I = 1, N
            IF (Y(I) .GT. Y1) GO TO 30
            IF (L.NE.H .AND. Y(I).LE.Y0) GO TO 30
            J = 1 + (W-1)*(X(I) - XMIN)/DX
            BUF(J) = AST
            JMAX = MAX0(JMAX,J)
   30    CONTINUE
         WRITE(LUNIT,35) (BUF(J),J=1,JMAX)
   35    FORMAT(1X,79A1)
   40 CONTINUE
      RETURN
      END
 
 
      SUBROUTINE EDIT(BUF,N)
      INTEGER BUF(N)
C
C     CALLED AFTER INPUT OF A SINGLE BACKSLASH
C     BUF CONTAINS PREVIOUS INPUT LINE, ONE CHAR PER WORD
C     ENTER LOCAL EDITOR IF POSSIBLE
C
      character*256 s
      open(7,file='----')
      write(7,10) (buf(i),i=1,n)
   10 format(256a1)
      close(7)
      call system('edit  ----')
      open(7,file='----')
      rewind 7
      read(7,'(a)') s
      close(7)
      call system('remove ----')
      n = 0
      do 20 i = 1, 256
         if (s(i:i) .ne. ' ') n = i
   20 continue
      read(s,10) (buf(i),i=1,n)
      RETURN
      END