INSTRUCTIONS FOR CALIBRATING THE

DUAL RANGE FORCE SENSOR

Please do not remove this sheet from the table.

Follow these instructions only if you open a Logger Pro file which involves

measuring forces using a Dual Range Force Sensor.

You need to follow this calibration procedure before you start the experiment.

## Follow the instructions below to calibrate the Dual Range Force Sensor (FS).

### Open the Logger Pro file that you will be working with. Remember, the calibration needs to be done only if the file uses a Dual Range Force Sensor.

### Make sure a Dual Range FS is connected to CH 1 (or CH 2) of the LabQuest interface box.

### On the Logger Pro main window, click on the LabQuest Set Up Sensors icon. See Figure 1.

Figure 1

### In the window that pops open you should be able to see the icon of the Dual Range FS on CH 1 (or CH 2). Click on the black triangle of that icon. A menu pops up. See Figure 2.

Figure 2

### Remove all strings and weights from the hook of the Dual Range FS attached to CH 1 (or CH 2) and hold it vertically. There must be nothing suspended from its hook:  no masses, no pulley, nothing.

### Click on Zero.

## You are done with calibrating the Dual Range Force Sensor. You may now return to your experiment.